## Slide 1: February 13, 2019 EIC Yellow Report Tracking WG Kick-Off meeting Simulation & Integration coordination
Annalisa Mastroserio and Domenico Elia (INFN Bari)

## Slide 2: Simulation and Integration
Goal : integrate the tracking detectors in the EIC simulation framework
  Determine the quality parameters for detectors, tracking and vertexing
Workplan :
  Define the detector technology and design from physics requirements
  Implement detector in the simulation starting from the detector design
  Define the tracking and vertexing quality parameters (see next slide)
  Study tracking and vertexing performances as a function of the detector design
EIC simulation software :
  Full simulations tools -> centrally managed by the EIC software working group
  Fast simulation tools -> centrally managed + other inputs from us

## Slide 3: Brief summary on EIC scenario
Primary requirements for the EIC detector :
  Hermeticity
  Excellent tracking resolution and PID coverage over a wide momentum range
Rates :
  Assuming a luminosity of 1033 cm-2 s-1 with an average cross section of ep collisions ≈ 50 mb, the expected interaction rate is roughly 50 kHz
    Rather small compared to LHC and RHIC conditions
Multiplicity:
  Small compared to LHC and RHIC conditions
e 15 GeV + 250 GeV p
http://eicug.org/web/sites/default/files/EIC_HANDBOOK_v1.1.pdf

## Slide 4: Vertexing / tracking : physics requirements
Central Tracking Systems :
  Main tracker
  Vertex Silicon tracker
  Forwards and Backwards trackers
  Roman Pots
Targets :
Hermetic coverage :
  close to 4p acceptance
  pseudorapidity range up to +- 4
Tracking resolution < than few %
Low material budget (within 5%)
http://eicug.org/web/sites/default/files/EIC_HANDBOOK_v1.1.pdf

## Slide 5: Vertexing / tracking quality parameters
Tracking :
  Efficiency in a wide momentum range and pseudorapidity range
    Combined Gaseous + Si tracking
    Si tracking standalone for low pT particles
  Momentum resolution
    Combined Gaseous + Si tracking
    Si tracking standalone for low pT particles
Vertexing :
  Primary vertex resolution
  Impact parameter resolution
    Convoluted with the primary vertex resolution provides the pointing resolution

## Slide 6: EIC simulation software : general information
Please visit http://www.eicug.org/web/content/eic-software for detailed information on the simulation software user group and material
Full Simulation tutorial with slides and videos is available at https://indico.bnl.gov/event/7281/
  latest tutorials on January 29th and February 6th

## Slide 7: EIC simulation software for detector and tracking
Fast simulation software :
  Available EIC common tool (via docker) https://eic.gitlab.io/documents/quickstart/
  Other fast simulation tools are welcome at this initial stage
    Users are confident with custom tools
    Good for initial cross-checks
    Caveat: we should avoid to have too many custom tools
  -> selection and comparison with centrally managed tools done later
Full simulation software :
  here we have detailed detector geometry, simulation and reconstruction
  performance studies as in fast simulation, but more reliable (and less optimistic)
  options centrally managed by the EIC Software WG:
  Fun4all
  G4E

## Slide 8: Fun4all
Software developed since 2002 for PHENIX, then in 2015 lots of cleanup and modernization
Mature Framework based on ROOT, C++ (steering with ROOT macros)
Modular : each detector has its own entity
No central code needs to be modified when adding new detectors
Detectors are combined using ROOT macros
Detailed documentation available at the Full Simulation tutorial https://indico.bnl.gov/event/7281/
  Installation intructions are available at : https://github.com/EIC-Detector/Singularity
  Code available https://github.com/sPHENIX-Collaboration/coresoftware/tree/master/offline/framework

## Slide 9: G4E : Geant 4 for EIC
A “younger” stage of development, constructed as a pure GEANT4 application and integrated into JupyterLab environment
Contains already several “master” detectors (and IRs) such as BeAST, JLEIC etc.
Easily import Geant4 standalone detector implementations
Ways to send the “right” configuration to a subdetector depending on selected “master” detector, so that one detector implementation could serve for different IRs
• Stay as close to Geant4 as possible, to stay convenient for Geant4 experts
Detailed documentation available at the Full Simulation tutorial https://indico.bnl.gov/event/7281/

## Slide 10: Preliminary workplan outline
EIC Fast simulation:
  Check present implementation of vertexing/tracking dets in the EIC fast simulation tool
  In parallel, try to exploit other available fast simulation tools
    Implement starting configuration (eg nr. of layers, space-point resolution etc) as in the EIC fast sim
  Preliminary study on tracking and vertexing performances
    Efficiency, momentum and impact parameter resolution
    Check performance vs different detector configuration options
  Study track finding algorithms:
    Gaseous only
    Si tracking only
    Combined Gaseous and Si tracking
EIC Full simulation:
  Check present implementation of vertexing/tracking dets in fun4all and G4E
  Cross-checks with fast simulation on basic performance results
  Initial performance studies based on current implementation of tracking algorithms
  Study track finding algorithms (here based on realistic sim + reconstruction):
    Gaseous only
    Si tracking only
    Combined Gaseous and Si tracking

## Slide 11: Final comments
Share your interest and expertise with us to organize together at best your contribution to the YR effort
Our working team needs you: please do not hesitate to express already today or in the coming days
  your field of interest
  your possible involvement in the workplan
  any other ideas / proposals

## Slide 12: Final comments
Share your interest and expertise with us to organize together at best your contribution to the YR effort
Our working team needs you: please do not hesitate to express already today or in the coming days
  your field of interest
  your possible involvement in the workplan
  any other ideas / proposals from your side
THANK YOU!