## Slide 1
Gaseous Detectors Group
YR-Tracking-WG Kick-off Meeting, February 13, 2020
Kondo Gnanvo

## Slide 2: Gaseous Detector Group: EIC Requirements for Central Tracker
http://eicug.org/web/sites/default/files/EIC_HANDBOOK_v1.1.pdf
Barrel Main Tracker
Hermetic coverage, close to 4π acceptance
  pseudo-rapidity range up to +/-1)
  Large area detectors
Low material budget on the level of 3-5% of X0/X for the central tracker region
  Gaseous detectors
Tracking momentum resolution in few % range
Forward and Backward Trackers
Coverage in the end cap
  pseudo-rapidity range up to +/-1 to +/-2.5
  Large area detectors
Low material budget specially for the electron endcap
  Gaseous detectors
Tracking momentum resolution in few % range
  50 µm space point resolution desirable for high P (> 50 GeV) in the hadron end cap

## Slide 3: Gaseous Detector Group: Needs, Goals & Deliverables
Review of available Technologies for EIC
State of the art of gaseous detector technologies
Investigate alternative technologies beyond those currently under consideration within EIC detector R&D program
Encourage groups to join and participate to the Tracking-WG
Broad range of gaseous detectors technologies suitable for complementarity between two general purposed EIC detectors
  scope of program like eRD6
Physics input & Simulation Need
Detector requirements input from the Physics WGs
Integration of tracking detector into EIC simulation frameworks (Annalisa slides)
  Input: Coordinate with and provide input to the simulation group
  Output: Study detector response and derive key performances to optimize the detectors design
Detector R&D (Targeted vs. Generic)
Evaluate maturity for gaseous detectors to satisfy EIC requirements
Targeted R&D: Status and timescale for completion for a day-1 EIC
  scope of program like eRD6
Generic R&D: Identify areas to benefit EIC sciences in the future
  scope of program like CERN RD51 for MPGDs
Rich and diverse field Gaseous Detectors technologies will satisfy the requirements for the central tracking in the central and forward regions of an EIC detector as rate is not a limiting factor, large area capabilities and low material with requirements such as space point resolution and efficiency are possible with these technologies

## Slide 4: Gaseous Detector Group: To Do List
Define list of tasks and timeline for completion
  Detector Technologies (R&D, Integration, services …)
  Simulation needs and outputs
Identify areas of interest for groups and assign tasks
  Start the discussion at next week meeting on people’s interest and commitment to contribute to a successful Yellow Report.
Coordinate the effort between different task and groups
  Tracking Group weekly meeting, Google groups, Workshop …
Tracking WG needs your enthusiastic contributions and your expertise.
So please join and spread the word around to help enlarge the community for a successful outcome for the Yellow Report in a year from now