## Slide 1
Tungsten Scintillator Calorimeter Technologies for EIC
EIC Users Group Yellow Report
Working Group on Calorimetry
February 25, 2020
Craig Woody
Brookhaven National Lab

## Slide 2: eRD1 Collaborators
sPHENIX W/SciFi
W/Shashlik

## Slide 3: Calorimetry for an EIC Detector (Conceptual)
B
Energy resolution ~ (1.0-2.0)%/√E  0.5%
Requires high resolution crystal calorimetry
Candidates for W-Scintillator Calorimeters
EMCAL resolution ~ (5-7)%/√E  1%
EMCAL resolution
~ (10-12)%/√E  (2-3)%

## Slide 4: Kinematics of Scattered and Produced Particles

## Slide 5: sPHENIX W/SciFi EMCAL
Barrel electromagnetic calorimeter covering ± 1.1 in h and 2p in f
2(±h) x 32 (f) = 64 Sectors
  6144 Blocks (24,576 towers)
W Powder ~ 50 mm
Fiber Assembly
Mold with W powder, fibers + epoxy
Readout with light guides and SiPMs
Matrix of tungsten powder and epoxy with embedded scintillating fibers
(0.47 mm, spacing 1 mm, SF ~ 2%)
Density ~ 9 g/cm3
X0 ~ 7 mm (18 X0 total), RM ~ 2.3 cm
2D Projective
Blocks

## Slide 6: sPHENIX EMCAL under construction
11 Tons of W powder now at UIUC
Blocks for Sector 2 at UIUC
Sector 0 undergoing testing at BNL
Sector storage and testing area in the Physics High Bay

## Slide 7: W/SciFi Performance
Non-uniformities are inherent in the design and contribute to the energy resolution
Uniformity of response over 8x8 towers with 8 GeV electrons (test beam data)
Uniformity after position dependent correction
Resolution ~ (13-14)%/√E  3%

## Slide 8
  A compact shashlik offers the possibility of improving the light collection uniformity due to the short light path to the WLS fibers.
  Availability of low cost SiPMs allows reading out each fiber individually. This allows determining the position of a shower even within a tower.
W/Shashlik Calorimetry
80% W/20 % Cu absorber plates
1.5 mm scintillating tiles read out with WLS fibers
Each fiber read out by its own SiPM
3x3 array of W/Shashlik modules built at UTSFM (Chile)