## Slide 1
“Determine, as much as possible, the power generated by the readout for all tracking technologies”
Presumably this question is driven by a desire to understand the power dissipated within the detector volume.
For the silicon it makes sense to express this as a function of silicon area. This allows for the scaling of power dissipation for different detector layouts.
For silicon sensors under consideration, the power dissipation for ALPIDE is known, the dissipation for ITS3 like sensors is scaled, and the numbers for MALTA are a private communication from Heinz Pernegger.
The dissipation in the detector volume has 2 components, the direct power dissipation on the sensors and the power dissipated in the cables that bring the power to the sensors. The ratio is preserved between the options.
The RDO boards sit outside of the detector volume and are not part of the power dissipation budget.
For all sensors the power is divided into analog (matrix) power and digital (usually periphery) power which will be shown as estimates for all sensors.
In general, the power dissipation for MAPS based detectors is low in comparison to other silicon technologies.
These are estimates (except for ALPIDE) but should be good for power budgeting purposes.

## Slide 2
For ITS2 like sensors (ALPIDE):
1 module = 63 cm^2 VDD = 2.1V @ 1.3A, VDA = 1.9V @ 0.3A => 3.3W so 100 cm^2 = 5.24W dissipated in the sensors and power cables.
ITS3 like sensors scaled:
0.5 x 0.52W/100 cm^2 = 2.6W/100cm^2
For MALTA:
Same silicon process (TJ 180 nm) 75 mW/cm^2 Analog + 10 mW/cm^2 Digital = 85mW/cm^2 for sensor.
Assume power delivery is same so 30% additional power dissipated in cabling => 110.5 mW/cm^2 or 11.05 W/100cm^2
Power estimates:
Sensors | Power dissipated / 100 cm^2 in detector volume (W)
ALPIDE | 5.24 W
ITS3 like | 2.6 W
MALTA | 11.05 W