## Slide 1
Using Eic-Smear and Generators A Walkthrough
Jets & HF Yellow Report Meeting March 9, 2020
Kolja Kauder

## Slide 2
This Talk – What it is and isn’t
Quickstart guide for those comfortable with ROOT and the command line.
Help for those that want to run locally
NOT an introduction to the Jupyter/EPIC framework
https://eic.gitlab.io/documents/quickstart/ https://www.youtube.com/channel/UCXc9WfDKdlLXoZMGrotkf7w

## Slide 3
Eic-smear – What it is and isn’t
Utility for unifying EIC MC output in ROOT
And for smearing said output
NOT a replacement for Geant!
But if you are asking...
“Given a known detector performance, how well can I measure some physics observable(s)?”
“If I need to measure X with to some precision, what detector performance do I need?”
or
… then it is an excellent tool

## Slide 4
Work Flow
Standard Format: analyze different generators without change
Truth ⬌ Smeared: Friend Trees
Install packages
Run MC
Build ROOT tree
Build “Detector”
Perform Smearing
Analyze Output
Djangoh
PEPSI
Rapgap
PYTHIA
Milou
BeAGLE
DPMJet
gmc_trans

## Slide 5
Shortcut
If you have an EIC RCF account at BNL, all packages are installed and available under $EICDIRECTORY
Make sure to include the following in your .cshrc
$ cat ~/.cshrc
setenv EIC_LEVEL pro source /afs/rhic.bnl.gov/eic/restructured/etc/eic_cshrc.csh
$
$ # this should work now
$ cp $EICDIRECTORY/PACKAGES/PYTHIA-RAD-CORR/STEER-FILES-Other/ep_noradcor.20x250.quicktest .
$ $EICDIRECTORY/bin/pythiaeRHIC < ep_noradcor.20x250.quicktest
If you don’t, read on. Everything runs on my MacBook

## Slide 6
Prerequisites
Necessary:
c++ and fortran compilers
cmake 3.1+
ROOT (6 is preferred)
Good to have:
LHAPDF
CERNLIB
Potentially FLUKA
gcc 4.8.5 is just enough for most things
5 is recommended, some PDFs are missing in 6
Resources:
Your admin
Your favorite package manager (e.g. homebrew)
Google
My READMEs
EIC software support
My installation notes on SL6 are world-visible on afs:
/afs/rhic/eic/restructured/env/pro/PACKAGES/READMES/

## Slide 7
Pythia (et al) Installation
$ git clone https://gitlab.com/eic/mceg/PYTHIA-RAD-CORR
$
$ cd PYTHIA-RAD-CORR
$ mkdir build ; cd build
$
$ cmake ../ -DCMAKE_INSTALL_PREFIX=<path>
$ make -j 2 install
More generators are available at https://gitlab.com/eic/mceg
All with README
Please report issues!
BeAGLE is hosted separately

## Slide 8
Eic-smear Installation
$ git clone https://gitlab.com/eic/eic-smear
$
$ cd eic-smear
$ mkdir build ; cd build
$
$ cmake ../ -DCMAKE_INSTALL_PREFIX=<path>
$ make -j 2 install
auto_ptr warnings are being fixed
Development is on-going – check back often for new features and additional options
Please report issues!
Example detectors are in /scripts directory
“True” reference detectors are coming – needs time and collaboration with Detector groups

## Slide 9
Generation
Generate 1M PYTHIA6 events, MinBias, Q2 = 10 – 100 GeV2
  ~ 1 hour to generate
Large files (9 GB). Future: Automatically use gz or bz2 streams
$ ${MYBINDIR}pythiaeRHIC < input.data.ep_noradcor.20x250.eic > log.txt
May require adapting your environment (e.g., include LHAPDF5 in (DY)LD_LIBRARY_PATH)
Many STEER files exist
  Tune, energy, radiative correction etc.
Which STEER cards to use is beyond the scope of this talk.
But needs to be agreed upon in this group or YR-wide!

## Slide 10
Common ASCII Format
wiki.bnl.gov/eic/index.php/PYTHIA
Based on Lund format

## Slide 11
Transform with BuildTree
  ~ 17 minutes to transform
$ root -l
root [0] gSystem->Load("libeicsmear")
root [1] BuildTree("pythia.txt",".", -1)
Transformation
Or compile:
$ g++ `root-config --cflags` \ `root-config --libs` \
-I<…>/include -L<…>/lib -leicsmear …
Note: BuildTree guesses generator from the filename
Note: Working on mechanism to bypass ASCII creation – this will form the basis for Pythia8 and other modern MCEGs

## Slide 12
Smearing
“Smearer” defines some element of performance
+ acceptance
Smearer
Smearer
Smearer
Smearer
Smearer
“Detector”
NOT a “physical detector”
Represents the overall performance in measuring a quantity.
Standard Smearers are provided
Define your own via inheritance
Smearers applied to each final particle
Optionally, recalculate derived values e. g. x, Q2

## Slide 13
In Practice
Function returning a Smear::Detector
… same for HCal
BeAST Calo parameters from eRHIC design study
Acceptance (in q)
Genre selects set of PIDs
 can be customized

## Slide 14
Example Continued
Tracking follows similar TFormula's.
Assemble devices
Kinematics options

## Slide 15
root [0] gSystem->Load("libeicsmear")
root [1] .L smearBeAST.cxx
root [2] SmearTree(BuildBeAST(), "pythia.root", "smeared.root")
Execution and Output
Smeared with SmearTree
  ~ 10 min to Smear (1.5k evts/sec)
root [0] TFile mcf ("pythia.root")
root [1] TTree* mc=(TTree*)mcf.Get("EICTree")
root [2] mc->AddFriend("Smeared","smeared.root")
Load and befriend!
Smeared property is stored if final and in acceptance
Otherwise store NULL  1-to-1 matching
Investigating recent “Error in <ROOT::Math::BrentRootFinder>”

## Slide 16
Repeat for Emphasis
Only the smeared property of an accepted particle is stored
  Consequences:
  NULL can mean particle not accepted OR particle not smeared for some other reason
  E smeared  P set to 0 and vice versa, may need to recover from original or recalculate
  In principle, E and P can both be non-0, if smeared by different devices
Also note, if multiple devices smear the same quantity, only the last one in the list acts

## Slide 17
Analysis
Befriend and get matched branches
Particle Loop
Assign p mass to EMCal "hits"
Some additions at analysis level:
Tracking efficiency
Add convenience functions?

## Slide 18
My Quick Result
No claims to correctness of these; main point of this slide:
This took ~two days to put together from scratch,
and I could now run many detector design variations in O(minutes)
Jet pT
Jet Mass

## Slide 19
Some Physics Examples
Jet pT Performance study for various HCAL options
From B. Page
y, x, Q2 response and resulting purity
eRHIC Design Study

## Slide 20
Limitations and Outlook
Currently, no support for Pythia8, Herwig, …
No support for HepMC
Integration with eJANA is on-going
End of this week
Not hard in principle. Can profit from eJANA.
But: HepMC2 is limited, HepMC3 not widely supported
PID: Matrix-based functionality exists. But unclear origin of existing parameterization
Acceptance should reflect B-field
No 12 processes, decay vertices, helixes, material budget, …
dE/dx, TOF, RICH smearing coming soon
Underway
Suggestions are welcome! But focus is on light-weight parameterization

## Slide 21
Resources
All hosted at gitlab.com/eic
Use issue tracker for bugs & requests!
Slack channel: eicug.slack.com/#software-support
Mailing list: eic-bnl-soft-l@lists.bnl.gov
Contact: kkauder@bnl.gov
Online users’ guide: wiki.bnl.gov/eic/index.php/Eic-smear
Class documentation (temporary location): www4.rcf.bnl.gov/~eickolja/

## Slide 22
BACKUP

## Slide 23
Extending (e.g., to Sartre)

## Slide 24
A Brief History
Originally written by Michael Savastio (student)
Long-time main developer Thomas Burton
Current maintainers are Alex Kiselev … and as of late, me
Walk with me through a full analysis
With Annotations
And potential future development

## Slide 25
Summary
eic-smear is fast, light-weight, extensible, well-written
No dependencies beyond ROOT
First stage unifies a host of EIC-relevant MC output
Cannot replace a full simulation – but gives a good estimate of detector effects on observables in <10% of the time it takes to generate PYTHIA6.