## Slide 1: EIC Accelerator Overview
Christoph Montag, BNL
EW-BSM 2020
May 6 – 7, 2020

## Slide 2: Requirements for the EIC
Requirements for an Electron-Ion Collider are defined in the White Paper:
High luminosity: L = 1033 to 1034 cm-2sec-1 - factor 100 to 1000 beyond HERA
Large range of center-of-mass energies Ecm= 20 to 140 GeV
Polarized beams with flexible spin patterns
Favorable condition for detector acceptance such as pT =200 MeV
Large range of hadron species: protons ….Uranium
Collisions of electrons with polarized protons and light ions (h3He, hd,…)

## Slide 3: EIC Design Concept (in a nutshell)
Take one RHIC ring with its entire injector complex as the EIC hadron ring
Add electron cooling to lower emittance and counteract IBS
Modify the hadron ring to be suitable for EIC beam parameters
Install an electron storage ring in the existing tunnel
Use a spin-transparent rapid-cycling synchrotron as full-energy polarized electron injector for rapid bunch replacement to counteract depolarization
Build a high luminosity interaction region that fulfills acceptance requirements

## Slide 4: Facility layout
Electron complex to be installed in existing RHIC tunnel – cost effective

## Slide 5: Tunnel Cross Section
All accelerators fit into the existing tunnel
Existing RHIC
tunnel
eSR
RHIC
RCS

## Slide 6: Parameters for Highest Luminosity
Hadron beam parameters similar to present RHIC, but smaller vertical emittance and many more bunches
2 hour IBS growth time requires strong hadron cooling, OR frequent beam replacement
Electron beam parameters resemble a B-Factory
Parameters optimized for high luminosity at high energy
Alternative optimizations are possible, for example for high luminosity at low energy

## Slide 7: Luminosity vs. CM Energy
Parameter and IR optimization at 105 GeV center-of-mass energy
Optimization yields luminosity at 105 GeV

## Slide 8: Electron Storage Ring
Composed of six FODO arcs with 60º /cell for 5 to 10 GeV
90º /cell for 18 GeV
Super-bends for 5 to 10 GeV for emittance control
5 straight sections with simple layout, plus IR straight
Radiate approx. 10 MW for maximum luminosity parameters at 10GeV
 14 superconducting 2-cell 591 MHz RF cavities
Storage
Ring

## Slide 9: EIC Electron Polarization
Physics program requires bunches with spin “up” and spin “down” (in the arcs) to be stored simultaneously
Sokolov-Ternov self-polarization would produce only polarization anti-parallel to the main dipole field
Only way to achieve required spin patterns is by injecting bunches with desired spin orientation at full collision energy
Sokolov-Ternov will over time re-orient all spins to be anti-parallel to main dipole field
Spin diffusion reduces equilibrium polarization
Need frequent bunch replacement to overcome Sokolov-Ternov and spin diffusion

## Slide 10: High Average Electron Polarization
Frequent injection of bunches with high initial polarization of 85%
Initial polarization decays towards P∞ < ~50%
At 18 GeV, every bunch is replaced (on average) after 2.2 min with RCS cycling rate of 2Hz
B P
Refilled every 1.2 minutes
B P
Refilled every 3.2 minutes
Pav=80%
Pav=80%
Re-injections
P∞= 30%
(conservative)
Re-injection

## Slide 11: Rapid Cycling Synchrotron as Full Energy Polarized Injector
Both the strong intrinsic and imperfection resonances occur at spin tunes:
  Gϒ = nP +/- Qy
  Gϒ = nP +/- [Qy] (integer part of tune)
To accelerate from 400 MeV to 18 GeV requires the spin tune ramping from
  0.907 < Gϒ < 41.
If we use a periodicity of P=96 and a tune Qy with an integer value of 50 then our first two intrinsic resonances will occur outside of the RCS energy range:
  Gϒ1 = 50+νy (νy is the fractional part of the tune)
  Gϒ2 = 96 – (50+νy ) =46-νy
  Imperfection resonances will follow suit with the first major one occurring at Gϒ2 = 96 – 50 = 46

## Slide 12: Spin Tracking in the Rapid-Cycling Synchrotron
High quasi-symmetry, with identity transformation in straight sections
 Good spin transparency properties
Requires well aligned quadrupoles, rms orbit ≤ 0.5 mm, and good reproducibility
Well within the present state of the art of orbit control
Orbit stability routinely achieved by NSLS-II Booster synchrotron

## Slide 13: Hadron Ring
Existing RHIC facility will be re-purposed as EIC hadron storage ring
Beam parameters are similar to RHIC, except number of bunches and vertical emittance
Need strong hadron cooling at store energy to counteract IBS,
OR
utilize existing second RHIC ring as full energy injector, replacing entire hadron fill every 1-2 hours

## Slide 14: Hadron Storage Ring Modifications
In-situ beam pipe coating with copper and amorphous carbon to improve conductivity and reduce SEY,
OR
insertion of pre-coated sleeves
Rebuild injection area with faster kickers to accommodate shorter bunch spacing
Remove energy-limiting DX separator dipoles
Inner arc between IRs 2 and 4 for circumference matching during 41 GeV low-energy operation
(Energy range from 100 to 275 GeV can be covered by radial shift)

## Slide 15: EIC Hadron Polarization
EIC will fully benefit from present RHIC polarization and near future upgrades
Measured RHIC Results with Siberian Snakes:
Proton Source Polarization 83 %
Polarization at extraction from AGS 70%
Polarization at RHIC collision energy 60%
Planned near term improvements:
AGS: Stronger snake, skew quadrupoles,
increased injection energy
expect 80% at extraction of AGS
RHIC: Add 4 snakes to 2 existing, no polarization loss
expect 80% polarization in RHIC and eRHIC
Expected results obtained from simulations which are benchmarked by RHIC operations
Polarized 3He in EIC with six snakes
Achieved ~85% polarization in 3He ion source
Benchmarked simulations:
Polarization preserved with 6 snakes, at twice the design emittance
Polarized Deuterons in EIC:
Requires tune jumps in RHIC to overcome few intrinsic resonances
Benchmarked simulation shows 100% spin transparency
No polarization loss expected in the EIC hadron ring
Siberian Snakes

## Slide 16: Spin Rotators
Longitudinal polarization is provided by pairs of spin rotators around the IR:
Helical dipole rotators for hadrons (same as in present RHIC)
Solenoid-based rotators for electrons (dipole based Steffen-rotator as in HERA would lead to meter-size vertical orbit excursions at low energy)
Rotators are included in spin matching to avoid polarization loss

## Slide 17: Interaction Region
+/- 4.5 m machine-element free space for central detector
25 mrad total crossing angle
Transverse momentum acceptance down to 200 MeV/c
Peak magnetic fields below 6T (NbTi sufficient)
Most magnets direct-wind; few collared magnets

## Slide 18: Positrons
Necessary preparation during EIC construction
  Provide space for future LINAC and source building
  Foresee polarity change of superconducting IR magnets
  Provide space for a positron damping ring
Luminosity
  Unpolarized: same as for electrons
  Polarized: challenging, but many ideas around
  (self-polarization at 18 GeV for free, but
          No arbitrary spin patterns)
Cost
  LINAC $20M, building $50M, Damping Ring $40M

## Slide 19: Summary
The EIC is designed to collide highly polarized electron and light ion (p, d, h) beams, as well as unpolarized heavy ions
Arbitrary spin patterns (“up” and “down”) in both beams are provided by injectors
Ingenious design of the rapid cycling electron synchrotron (RCS) allows polarization preservation all the way up to 18 GeV
Additional Siberian snakes in the hadron ring will provide 100 percent polarization preservation during the ramp
EIC reaches a peak electron-proton luminosity of
L= 1.05·1034cm-2s-1
at 105 GeV center-of-mass energy
Alternative parameter schemes are possible, for example for optimization at lower center-of-mass energy

## Slide 20: Backup Slides

## Slide 21: Alternative Luminosity Optimizations
Example: Optimization at 63 GeV and at 105 GeV center-of-mass energy to
meet different physics needs
Independent optimizations – different beam parameters, different IR designs
Either optimization yields luminosity