## Slide 1: Contents

## Slide 2: Intermediate Silicon Tracker (INTT) Specifications Daniel Cacace, Connor Miraval, Rachid Nouicer, and Itaru Nakagawa Brookhaven National Laboratory
Ladder
  HDI Design
  Stave Design
  Stave FEA Analysis
  Barrel Configuration
Ladder Support Structure
  End Ring Design
  End Ring FEA Analysis
Barrel Support Structure
  Service Barrel Design
  Service Barrel FEA Analysis
Detector Support Structure
  Supports Design
  Supports FEA Analysis

## Slide 3: Status
Parts | Material | Concept | Design | FEA Analysis | Drawings | Prototype | Production
Stave | CFC | Done | Done | Done | Done | Done | WIP
Ladder base | Aluminum | Done | Done | N/A | Done | Done | N/A
Chip tools | Acrylic | Done | Done | N/A | Done | Done | N/A
Sensor tools | Acrylic | Done | WIP | N/A | Done | Done | N/A
End rings | PEEK | Done | Done | WIP | WIP | Done | 
Barrel asm fixture | Aluminum | WIP |  |  |  |  | 
Ring attachment | Aluminum | Done | WIP |  |  |  | 
Service barrel outer | CFC | Done | WIP |  |  |  | 
Service barrel inner | CFC | Done | WIP |  |  |  | 
Ribs | Aluminum | Done | WIP |  |  |  | 
Cooling attachment | PEEK | WIP |  |  |  |  | 
Cable attachment | PEEK | WIP |  |  |  |  | 
ROC attachment | Aluminum | WIP |  |  |  |  | 
ROC cooling | Aluminum | WIP |  |  |  |  | 
Support tube | CFC | Done | WIP |  |  |  | 
Support beams | Aluminum | Done | WIP |  |  |  | 
Installation tooling | TBD | WIP |  |  |  |  | 

## Slide 4: Requirements
Physics
|h| ≥ 1.0 @ |Zvertex|= 10 cm
100% φ coverage
X/X˳ ≤ 1.25%
Mechanics
T ≤ 20°C
δ ≤ 50μ
ω ≥ 80Hz

## Slide 5: 1.1 HDI Design

## Slide 6: Sensor Design
BUS Extender
BUS Extender
Silicon Module
Silicon Module
HDI
HDI
Thickness: 320 um
Pitch: 9.984 mm/128 = 78 um
F-length (single sensor) = 22.5 mm F-length (active area) = 20.0 mm
Z-length type-A (single sensor) = 130.0 mm Z-length type-A (active area) = 128.0 mm
Z-length type-B (single sensor) = 102.0 mm Z-length type-B (active area) = 100.0 mm

## Slide 7: HDI Design
HDI Thickness: 473 um
Width: 38.0 mm
z-length total: 400 mm (radiation length = 0.49%)
Sensor thickness: 320 um
FPHX chip thickness: 320 um

## Slide 8: Layer Structure of HDI

## Slide 9: Radiation Length of INTT Ladder
Material | Thickness [μm] | 
Silicon | 320 | 0.34%
HDI | 473 | 0.39%
Stave | 3620 | 0.40%
Total | 4413 | 1.13%
Material | Thickness [μm] | 
Silicon | 320 | 0.34%
HDI | 473 | 0.39%
Stave | 3620 | 0.40%
Total | 4413 | 1.13%
HDI Material | Thickness [μm] | 
Copper* | 52 | 0.26%
Polyimide | 380 | 0.13%
Total** | 432 | 0.49%
*Copper thickness is not physical thickness, but effective thickness. **Total thickness is not 473μm, because of copper effective thickness. |  | 
HDI Material | Thickness [μm] | 
Copper* | 52 | 0.26%
Polyimide | 380 | 0.13%
Total** | 432 | 0.49%
*Copper thickness is not physical thickness, but effective thickness. **Total thickness is not 473μm, because of copper effective thickness. |  | 
The HDI is composed of 7 copper layers. 4 layers are solid ground or power layers.
The remaining 3 layers are signal line layers containing a few percent of solid copper per layer.

## Slide 10: 1.2 Stave Design

## Slide 11: Prototype Stave Design
Thickness: 0.76 mm
Height: 3.76 mm
Width: 38.00 mm
Length: 497 mm
Material: Carbon Fiber, Polymethacrylimide (PMI),
Stainless Steel and Epoxy
(radiation length = 0.40% )

## Slide 12: Prototype Stave Design
Tube Bend
(316 Stainless)
CFC Flat
(K13C2U +
20301A 34 GSM)
Endcap
(Carbon PEEK)
CFC Formed
(K13C2U +
20301A 34 GSM)
Rohacell 110 RIST Foam
(polymethacrylimide)
CFC Tube (OD: 3mm,
ID: 2mm) (T700)
Pin Receptacle
(Copper)
Tube Sleeve
(316 Stainless)
Epoxy
(EP75-1)

## Slide 13: Stave Average Radiation Length
Stave | Equivalent Thickness (mm) | Radiation Length (mm) | X/X0 *100
CFC Flat | 0.3300 | 256.4122 | 0.1287
CFC Formed | 0.3411 | 256.4122 | 0.1330
CFC Tube | 0.1033 | 282.2909 | 0.0366
Foam | 1.4740 | 3771.3741 | 0.0391
Epoxy | 0.1016 | 298.7463 | 0.0340
Water | 0.0826 | 356.7854 | 0.0231
 |  | Total | 0.3946
 | Radiation Length (mm) | Fraction
CFC | 194.0909 | 0.6
Epoxy | 349.8941 | 0.4
Total | 256.4122 | 
Water | 360.8000 | 0.7
Glycol | 349.2849 | 0.3
Total | 356.7854 | 
Notes: 13
Le plan de l’expose se presente de la manière suivante :

## Slide 14: Ladder – Stave with Two HDIs
BUS Extender
BUS Extender
|h| = 1.1 @ |Zvertex|= 10 cm
Signal
Signal
Silicon Module
Silicon Module
Ladder
HDI
HDI
|h| a | ZSi - Zvertex| / Radius
465.5 mm

## Slide 15: 1.3 Stave FEA Analysis

## Slide 16: Structural – Under its Own Weight
Deflection – MAX: 0.0001 in (2.5 um)
Stress – MAX: 105 psi (0.7 MPa)

## Slide 17: Vibration – Natural Frequencies
First Mode – 469 Hz
Second Mode – 784 Hz

## Slide 18: Thermal – Temperatures
Stave ΔT – 3.8 °C (6.8 °F)
Sensors ΔT – 1.2 °C (2.2 °F)

## Slide 19: Thermal – Midplane Cross Section
Temperature
Heat Flux

## Slide 20: 1.4 Barrel Configuration

## Slide 21: INTT Components
Cooling Barb
(316 Stainless Steel)
CFC Stave
(K13C2U)
Stave Endcap
(Carbon PEEK)
CFC Outer Shell
(Inner Shell not shown)
Endcap Ring
(Carbon PEEK)
HDI
(High Density Interconnect)
Sensor
(Silicon)
Chip
(FVTX)

## Slide 22: INTT Two Barrels
Full Detector
Half Barrel
Outer Layer
Inner Layer

## Slide 23: Two Barrel Layout
Water Cooling
1a (Inner)
1b (Outer)
2a (Inner)
2b (Outer)

## Slide 24: Two Barrel Layout Active Area
1a (Inner)
1b (Outer)
2a (Inner)
2b (Outer)
The width of the active area is 52.6% of the total width of the ladder. In order to have overlap for full PHI coverage and have a reasonable stave thickness, the ladders were stager radially with no tilt.

## Slide 25: Two Barrel Configuration
Barrel | Center of Sensor Tangent Radius (mm) | Pseudo rapidity | QTY of Ladders | Angle (deg) | Coverage (PHI) (%) | Overlap (%) | Clearance (mm) | Chip Power Dissipation (W) | Stave Rad Length (%) | Barrel Rad Length (%)
1 | - | - | 24 | - | 100 | 1.8 | 2.0 | 62.30 | 0.80 | 2.26
1a (Inner) | 71.88 | 1.37 | 12 | 0 | 52.7 | 0 | 0.6 | 31.15 | 0.40 | 1.13
1b (Outer) | 77.32 | 1.31 | 12 | 0 | 49.4 | 0 | 3.6 | 31.15 | 0.40 | 1.13
2 | - | - | 32 | - | 100 | 1.8 | 2.0 | 83.07 | 0.80 | 2.26
2a (Inner) | 96.80 | 1.12 | 16 | 0 | 52.4 | 0 | 0.6 | 41.53 | 0.40 | 1.13
2b (Outer) | 102.62 | 1.07 | 16 | 0 | 49.4 | 0 | 3.0 | 41.53 | 0.40 | 1.13
Total | - | - | 56 | - | - | 100 | 11.22 | 145.37 | 1.60 | 4.52
BUS Extender
BUS Extender
|h| ≥ 1.0 @ |Zvertex|= 10 cm
Signal
Signal
Silicon Module
Silicon Module
Ladder Concept
HDI
HDI
|h| a | ZSi - Zvertex| / Radius
465.5 mm
Notes: 25
Le plan de l’expose se presente de la manière suivante :

## Slide 26: Two Barrel Configuration

## Slide 27: 2.1 End Ring Design

## Slide 28: Cooling Connection

## Slide 29: Endcap Rings - Half Barrel, One Side
Endcap Rings With Staves and HDIs
Endcap Rings With Staves

## Slide 30: Endcap Rings - Half Barrel, One Side
End Ring 1
End Ring 2
End Ring 3
Gap for layers 1a and 1b
Gap for layers 2a and 2b

## Slide 31: Assembly

## Slide 32: 2.2 End Ring FEA Analysis

## Slide 33: Structural – Under its Own Weight
Deflection – MAX: 0.0025 in (63.5 um)
Stress – MAX: 170 psi (1.17 MPa)

## Slide 34: Vibration – Natural Frequencies
First Mode – 83 Hz
Second Mode – 85 Hz

## Slide 35: 3.1 Service Barrel Design

## Slide 36: INTT Service Barrel
Ladder Layers
Cylinder Panel
Carbon Fiber
Extension Cables
ROCs
Ball Transfers
End View
Back View

## Slide 37: Support Structure
Aluminum I Beams
(6061)
Cylinder Panel
Carbon Fiber
End View

## Slide 38: INTT Installation
Installing
Installed
Roll in on Ball Transfers

## Slide 39: iHCal, EMCal, TPC, INTT & MVTX

## Slide 40: 3.2 Service Barrel FEA Analysis

## Slide 41: 4.1 Supports Design

## Slide 42: 4.2 Supports FEA Analysis

## Slide 43: End