## Slide 1
Tungsten Scintillator Calorimeter Technologies for EIC
EIC Users Group Yellow Report
Working Group on Calorimetry
March 31, 2020
Craig Woody
Brookhaven National Lab

## Slide 2: eRD1 Collaborators
sPHENIX W/SciFi
W/Shashlik

## Slide 3: Calorimetry for an EIC Detector (Conceptual)
B
Energy resolution ~ (1.0-2.0)%/√E  0.5%
Requires high resolution crystal calorimetry
Candidates for W-Scintillator Calorimeters
EMCAL resolution ~ (5-7)%/√E  1%
EMCAL resolution
~ (10-12)%/√E  (2-3)%

## Slide 4: Kinematics of Scattered and Produced Particles

## Slide 5
Calorimeter Requirements
(from the EIC Handbook)
Better resolution is provided by tracking
Provide e/h separation to > 1:100
Needs to be compact to fit inside the magnet and minimize cost
Readout must work inside magnetic field
Minimal resolution from tracking because of solenoid field
Requires good spatial resolution (i.e., segmentation)
Needs to be radiation tolerant since is close to beamline
Resolution provided by a tradeoff between calorimeter and tracking
(resolution and segmentation depends on h)
Needs to be compact and cost effective
Readout must work in fringe field of magnet

## Slide 6: sPHENIX/ePHENIX
Sectors and blocks are approximately projective and tilted in h and f
DIS event simulated in a converted sPHENIX detector for EIC
EMCAL Sector
Barrel EMCAL

## Slide 7: sPHENIX W/SciFi EMCAL
Barrel electromagnetic calorimeter covering ± 1.1 in h and 2p in f
2(±h) x 32 (f) = 64 Sectors
  6144 Blocks (24,576 towers)
W Powder ~ 50 mm
Fiber Assembly
Mold with W powder, fibers + epoxy
Readout with light guides and SiPMs
Matrix of tungsten powder and epoxy with embedded scintillating fibers
(0.47 mm, spacing 1 mm, SF ~ 2%)
Density ~ 9 g/cm3
X0 ~ 7 mm (18 X0 total), RM ~ 2.3 cm
2D Projective
Blocks

## Slide 8: sPHENIX EMCAL under construction
11 Tons of W powder now at UIUC
Blocks for Sector 2 at UIUC
Sector 0 undergoing testing at BNL
Sector storage and testing area in the Physics High Bay

## Slide 9: W/SciFi Performance
Non-uniformities are inherent in the design and contribute to the energy resolution
Uniformity of response over 8x8 towers with 8 GeV electrons (test beam data)
Uniformity after position dependent correction
X axis projection
Y axis projection
Light Guide Boundaries
Block Boundary
Light Guide Boundaries
Block Boundaries

## Slide 10: Energy Resolution
Energy resolution after position dependent correction
Resolution ~ (12-13)%/√E  2.5%
Resolution ~ (13-15)%/√E  3%
Beam covering a 1.0 x 0.5 cm2 area centered on a tower
Beam covering a 2.5 x 2.5 cm2 area centered on a tower

## Slide 11
  The inherent energy resolution can be tuned by adjusting the sampling fraction (at some expense in reducing the density and hence the radiation length and Moliere radius).
  However, the main limitation in the energy resolution is the position dependence of the shower due to the fact that the shower is so compact
  One can improve the non-uniformities by minimizing the mechanical and optical boundaries.
  One can try and measure the shower position within a tower or increase the segmentation.
Improvements to the Energy Resolution

## Slide 12: Increasing Photocathode Coverage of W/SciFi Blocks
  The sPHENIX W/SciFi blocks consist of 4 towers, each read out with its own light 1” long guide with four 3x3 mm2 SiPMs. The uniformity of the light exiting the fibers is very good but the light guide provides poor mixing and the SiPMs cover only 23% of the readout area of the light guide (6.4% of the total readout area of the block).
  The light collection efficiency and uniformity can be greatly improved by increasing the photocathode area coverage on the readout end of the block
Maximum photocathode coverage using the sPHENIX blocks
Hamamatsu S13360
6x6 mm2 SiPM with TSVs
(50 mm pixels)
Increased coverage using existing sPHENIX light guides
2x2 array of 6x6 mm2 SiPMs
Short (1.5 mm) light guide covering entire block
3 SiPMs in series then 3 summed in parallel
(C/3 x 3 = C)
PCB Readout

## Slide 13
  A compact shashlik offers the possibility of improving the light collection uniformity due to the short light path to the WLS fibers.
  Availability of low cost SiPMs allows reading out each fiber individually. This allows determining the position of a shower even within a tower.
W/Shashlik Calorimetry
80% W/20 % Cu absorber plates
1.5 mm scintillating tiles read out with WLS fibers
Each fiber read out by its own SiPM
Ray tracing withing a scintillation tile
Light collection efficiency for 2 adjacent WLS fibers vis position

## Slide 14: Progress on W/Shashlik Calorimetry
Nine W/Shashlik modules were produced and tested at UTFSM and have now been delivered to BNL.
The modules will be assembled into a 3x3 array and tested using the sPHENIX calorimeter readout electronics.
Cosmic Ray Spectra
3x3 array of W/Shashlik modules
Test enclosure for W/Shashlik modules and front-end readout electronics

## Slide 15
  W/Scintillator calorimetry provides a cost effective option for instrumenting the barrel region of an EIC detector and could possibly be used in the electron or hadronic endcap regions.
  Due to its compactness the position dependence of the shower can lead to non-uniformities that contribute to the energy resolution (particularly in the constant term).
  Minimizing the mechanical and optical boundaries of the readout will help to minimize the position dependencies and lead to better energy resolution.
  A large central EMCAL barrel calorimeter is currently under construction for sPHENIX and will be available for use at EIC.
Summary