## Slide 1: PID
:
Physics
Detectors
Machine
Community
PID Deliverables to Pavia:
Requirements on “external” systems
Pro/Con matrix (e-Arm, Barrel, h-Arm)
Physics requirements.
RICH
TOF
mRICH
DIRC
PID
Others
Patrizia Rossi
Thomas K Hemmick

## Slide 2: Were we are: Summary Table
:
 | p-Range @ Radiator L | Contr. Jc | Param. | Pro/Con | Ext Const | MONTECARLO Simulatoin
psec TOF LGAD TOF | Up to 10 Depends on sT and L | NO | ~YES | YES | ~ YES | NO
dual RICH (aerogel, gas) | 2-60 @ 1.6 m | YES Chroma Emission Pixel Field Tracking | YES | YES | YES Simulated constant w/ momentum | YES GEMC/Geant4 AI-driven Optimization
GEM RICH (Gas Electron Multipliers) | 20-50 @1m | Chroma (Emission) Pixel Tracking | YES | YES | YES | YES (Simplified)
modular RICH (mRICH) | 2-10 @ 3 cm | YES Chroma Emission Pixel Tracking | ~YES | YES | YES (tracking) | ~YES GEMC/Geant4 work in progress
Detection of Internally Reflected Cherenkov (DIRC) | 0.8-6 @ 1.7 cm | YES Tracking Mult. Scat Chroma, Emission, pixel | YES | YES | YES | YES GEMC/Geant4 without B-field

## Slide 3: High Momentum GEM RICH
:
1m of CF4 radiator at 1.003 bar (slightly overpressure)
CsI Photocathode on top GEM
Mirror in deep UV  MgF2 coating
Single Photon Capability  quintuple GEM stack with APV25-SRS
Particles ~perpendicularly incident on spherical mirror, focused onto a GEM stack directly
Pro
  Sensor insensitive to B-field
  Short (12pe/m windowsless)
  Thin photo-cathode leads to more ideal optics.
Con
  Unknown how to bridge the gap in p-K
    High pressure??
    Different gas??
  Loses light with contaminants @ few ppm level (round trip; tougher than PHENIX HBD...)
    Requires superb gas system (OK)
    Requires better detector materials
  Photo-cathode in high radiation zone.
H. Klest

## Slide 4
:
High Momentum GEM RICH
4
:
Tracking is leading error contribution if worse than ~7mrad.
Negligible resolution factor around 2 mrad.
Between 2 and 7mrad , more detailed investigation is required.
Plot shows viscerally the effect.
More detailed simulation required.
OK
hmm
H. Klest

## Slide 5: mRICH
Cherenkov radiator
Aerogel, n = 1.03
Radiator length, L = 3cm
Lens with focal length, 𝑓= 6”
Photon Detector
3 mm pixel size
More quantitative estimate of dead area (foam holder/box/Fresnel corners)
Sensor issue is general, independent of radiator and optics.
Provide a time meas. with proper sensor?
Utility of the device is expanded if it provides picosec TOF & Cherenkov
X. He M. Sarsour

## Slide 6: mRICH
6
Tracking influence minor
Tracking influence major
e/p excellent at lowest p
X. He M. Sarsour

## Slide 7: dRICH
Cherenkov radiator
○ Refractive Index
n = 1.02 (aerogel) 1.0008 (C2F6)
○ length of the radiator
L = 4 cm (aerogel) , 160 cm (C2F6)
Mirrors
Photon Detector
3 mm pixel size; 200-500 nm MAPMT
Particle Generation
Originate from the vertex
Pro
Con
E. Cisbani
M. Contalbrigo

## Slide 8: dRICH
Exquisite detail in simulation.
AI-based optimization.
Good parametrization
Uses constant external angular resolution assumption.
External assumption
Jc contributions
Material budget evaluation
Sensors in the acceptance
E. Cisbani
M. Contalbrigo

## Slide 9: DIRC
Generic reference design: 1m barrel radius, 16 sectors
176 bars: synthetic fused silica,17mm (T) ´ 32mm (W) ´ 4200mm (L)
Photo sensors: MCP-PMTs -3x3mm2 pixels
G. Kalicy J. Schwiening

## Slide 10: DIRC
External assumption
NOTE:
DIRC optics design-level adaptable to magnetic field orientation at the sensors.
Need ~settled field direction prior to construction.
Performance ~independent of device radius.
G. Kalicy J. Schwiening

## Slide 11: psTOF
Multiple technologies (two examples):
  LAPPD: best st B-field ~, moderate pixel size
  LGAD: excellent st field tolerant, tiny pixels
M. Chiu W. Li

## Slide 12: psTOF
𝜋/K
K/p
LGAD 20 psec
LAPPD 5 psec
Crab limit vs emittance limit?
Physics pT resolution required?
Polarization variation within bunch?
Needs additional study
Not TOF, but really “t0”
Assumes 4m flight path (conflict?)
Time resolution very challenging
Multiple scattering may contribute path length uncertainty (coupling to tracking).
External start time provided by forward detectors could be helpful
Study of self-timing (Internal) using tracks
Measure (Z,t0); Learn Collision pT
M. Chiu W. Li

## Slide 13: Conclusions
:
PID is challenging!
Tracking requirement for Cherenkov
  Parameterizations of gas Cherenkov indicate pointing required at 0.5-1.0 mrad level while inside the radiator.
  Calculations of aerogel devices indicate 0.5 -1.0 mrad level.
  Calculations of DIRC indicate 0.5 mrad level or better.
Good progress but still some open questions:
  Simulations are still preliminary except for a few detectors
  Sensors and electronics in the detector require an evaluation of radiation hardness.
  R&D on photon sensors is on going (magnetic field tolerance a primary concern: Visible light sensor solution for 3T magnetic field problematic.)
  No discussion on the material budget
  Available space is a driving concern for some technologies.
    Shifting vertex is expensive, but helps most technologies in hadron arm.
    Need quantitative optimization of cost/benefit
  Resolution for TOF includes multiple terms in addition to superb st
    Clock reference/distribution
    Path length.