## Slide 1
Itaru Nakagawa, RIKEN
May 27, 2020
Final Design and Safety Review of the INTT Ladder and Barrels
WBS: 3.0X
Ladder Electronic Components:
HDI, Chips and Sensors

## Slide 2: Ladder Overview
Tracking System: MVTX+INTT+TPC
½ Ladder
Silicon Sensors
Type-A
Type-B
FPHX Chip
HDI
Silicon
Wirebonding
FPHX Chip
Type-A
Type-B
Silicon strip sensors
INTT Full Ladder
HDI Readout Cable

## Slide 3: Silicon Sensors
Tracking System: MVTX+INTT+TPC
Type | # of Blocks | Active Area
A | 8 x 2 | 128mm x 19.96mm
B | 5 x 2 | 100mm x 19.96mm
Strip orientation
Readout orientation
Readout orientation
128 strips
128 strips
Type-A
Type-B
Sensor | Make | Coupling | Bias | Thickness | Strip Pitch | Depletion Volt.
Strip Strip | Hamamatsu | AC | Poly-Si Bias | 320±15 mm | 78 mm | Max 120V

## Slide 4: Silicon Sensors
Tracking System: MVTX+INTT+TPC
Type-A
AC readout pads
probe trace
40 % of pad
60 % of pad are secured for wirebonding
Type-B

## Slide 5: FPHX Chip
Tracking System: MVTX+INTT+TPC
Specification | FPHX
ADC/channel | 3 bits
Power Consumption | 64 mW
Number of channels | 128
Data Transmission | 200Mbps
Developed for Forward Vertex Detector for PHENIX at Fermi Lab.
Each FPHX chip integrates and shapes (CR-RC) signals, digitizes and sparsifies the hit channels each beam crossing (106ns beam clock), and serially pushes out the digitized data.
Front end
(Analog section)

## Slide 6: FPHX Chip (Analog Section)
Tracking System: MVTX+INTT+TPC
+
_
Vref
Shaper
Integrator
Input
Comp
Vth0
Comp
Vth1
Comp
Vth7
Programmable Thresholds
Disc outputs
3-bit ADC
T-peak ~ 60 ns (programmable)
Program gain and Vref
128 channel
46, 50, 60, 67, 85, 100, 150, or 200 mV/fC
60 ns peak time (rt- pgmbl)
3—bit ADC (th-pgmbl)
Optimized to 1 to 2.5 pf input
115e + 134e/pf
~ 70 to 140 mW/ch (dep. gain)
At max. input transistor bias of 38uA: 115e + 134e/pF
Silicon strip + readout line capacitance ~ 6pF
Predicted noise ~ 115e + 134e/pF * 6pF ~ 1,000e
Signal ~ 20,000e
Expected S/N ~ 20/1

## Slide 7: FPHX Chip (Digital Section)
Tracking System: MVTX+INTT+TPC
Analog
Data Processing
Data Output
20 bit Serial data word structure

## Slide 8: High Density Interconnect (HDI) Cable
Tracking System: MVTX+INTT+TPC
INTT HDI (Manufactured by Yamashita co.)
Digital GND pad
 | FVTX | INTT
# Layers | 7 | 7
Length [cm] | ~20 | 40
Pitch [mm] | 40 | 60
M20-7910342R
Thermistat 3pin readout
Analog GND pad
Analog and digital pads are used for grounding in the final barrel configuration.
The design is based on HDI’s of FVTX. The cable length is longer, but the pitch of the signal line is somewhat relaxed 60 [mm] instead of 40 [mm].
FVTX HDI
Bias connector
Hirose DF18 connector
Data, slow control, FPHX power

## Slide 9: High Density Interconnect (HDI) Cable
Tracking System: MVTX+INTT+TPC
7 cupper layers
High signal line density in 2 layers
Solid ground outer layers to shield signal layers
L1
L2
L3
L4
L5
L6
L7
Analog GND
Clock Signal
Bias
Power
Signal
Digital GND
Thermistats & RF

## Slide 10: High Density Interconnect (HDI) Cable
Tracking System: MVTX+INTT+TPC
~1cm
100×2MHz BCLK
Cu Layer-7
Cu Layer-1
Due to spatial limit of signal layers, some part of signal lines have to run unshielded layer-7 for a few cm.
The corresponding frequency is 10 – 30GHz, which is at least an order of magnitude higher frequency than the highest frequency (100×2MHz BCLK) signal transmits layer-7.
No problem has found in the past 2 beam test.

## Slide 11: Summary
• The INTT Ladder consisted of Silicon strip sensors, FPHX chips, HDIs and stave.
• The INTT Silicon strip sensors are manufactured by Hamamatsu photonics. Basic design is based on FVTX silicon strip sensors. The primary difference is the dimension of the strip and sensors. The thickness is standard 320mm.
• FPHX chips are developed by Fermi lab for FVTX detector for PHENIX. Some programmable parameters will be optimized for INTT.
• The HDI cable is also designed based on the one of FVTX. The cable consisted of 7 layers and signal layers are kept inner layers to be shielded by ground or bias layers. Some signals lines are exposed in the layer-7, but they are kept short. So far we haven’t observed any problem throughout beam tests.

## Slide 12: Back Up