## Slide 1: Run 15: Polarized Protons 100 GeV
V. Schoefer
RHIC Retreat
8/14/2014

## Slide 3
Last time on “100 GeV Protons”…
Vertical
Horizontal
Yellow IPM Emittances
Longitudinal scraping being used to reduce beam loss during rebucketing at 100 GeV.
Moving to a vertical-only scraping scheme increased beam-beam tune spread, Qbb
Ran into the beam-beam limit:
Transverse emittance blowup
Increase in polarization decay
  >2%/hr, compared to ~1%/hr nominal
Diminishing tune spread from beam-beam is exactly the goal of the electron lens
Feb 28-Mar 11, Run 12

## Slide 4: E-lens Effort
E-lens proper (See earlier talk)
Lattice design for e-lens
  First tried (and abandoned) in Run13
  Reworked* using ATS principle for
    Improved nonlinear chrom
    Improved DA
Beam stability with e-lens/BBB damper development
*S. White, W. Fischer, Y. Luo “Optics solutions for pp operation with electron lenses at 100 GeV” (C/AD Note)

## Slide 5: E-lens Lattice Requirements
Β* (IP6 and 8) | 0.85 m | Same as Run 12, could push a little
Β* (IP10) | Large as possible (20 m ?) | Beam stability with e-lens
ΔΦ (per cell) | π/2 | Nonlinear chrom comp
ΔΦ(Elens->IP6) | kπ | E-lens kick
Injection γtr | Not near injection γ | Matching/stability
DA (on/off momentum) | Compare favorably to previous lattices | 
Spin resonance strengths | Compare favorably to previous lattices | STILL NEEDS CHECKING!
*S. White, W. Fischer, Y. Luo “Optics solutions for pp operation with electron lenses at 100 GeV” (C/AD Note)

## Slide 6: ATS Store Optics
ΔΦ =π
ΔΦ/cell =π/2
Integer tune increased (28,29)(29,30):
Injection γtr refit to 23.5 (nominally 23.3)
Injection Β* = 7.5 m (2/3 driving?)

## Slide 7: ATS Store Optics
Β = 20 m
Β = 0.85m
Lattice requires modification of Q-trim to make it bipolar

## Slide 8: Nonlinear Chroms Improve

## Slide 9: E-lens and transverse stability
E-lens presents a substantial impedance to the beam* , “transverse mode coupling instability” (think head-tail instability)
Primary stabilizing force is the solenoidal field at the e-lens (pins the electrons)
Additional stabilizing (against all coherent instabilities, including e-lens) to be provided by the transverse BBB damper.
*Burov et al, “Transverse beam stability with an ‘electron lens’” Phys. Rev. E, Vol 59, Num 3 (1999)
Bth = min solenoid field for stability
r = beam radius (controlled via β*)
ΔQ = |Qx – Qy| (assumed to be 0.01, could be a problem)

## Slide 10: BBB Damper
Hardware (pickups and kickers in the injection area)
Yellow BBB kicker
Y-arc
Yel beam
Blue BBB kicker
PUE can be chosen between Q11 and Q15 (depends on lattice)

## Slide 11: So, RHIC will handle higher intensity… can the injectors deliver? (an important measurement from Run 14)
Intensity
AGS Cycle
Booster input
AGS Extractions
Change source temp to get different input
Adjust scraping to keep AGS extraction intensity constant
Measure emittances
Data cut:
AGS late = 2.0 +/- 0.05 e11
Typical RHIC fills
More scraping = lower emittance ???

## Slide 12
Booster Input
Increased scraping 
Emittance (vert, 95% norm, pi-mm-mrad)
MW 006
AGS IPM injection
AGS IPM FLATTOP
Absolute emittances

## Slide 13
Booster Input
Increased scraping 
Emittance (vert, 95% norm, pi-mm-mrad)
Booster Input
Absolute emittances
Relative emittances
Increased scraping 

## Slide 14: Booster emittance dilution
If we cannot get brighter beam from the more intense beam, then we lose (lumi AND polarization)
Possible cures (all aimed at space charge driven problems):
  Second harmonic in RF (not two bunches, but flatter bunch)
  Altered scraping scheme
    Scrape earlier (pre blow-up), even just at injection (do not ever circulate in the Booster what we would scrape later)
  Two bunches in the Booster, merge in the AGS (?!)

## Slide 15: Booster emittance dilution
If we cannot get brighter beam from the more intense beam, then we lose (to say nothing of polarization)
Possible cures (all aimed at space charge driven problems):
  Second harmonic in RF (not two bunches, but flatter bunch)
  Altered scraping scheme
    Scrape earlier (pre blow-up), even just at injection (do not ever circulate in the Booster what we would scrape later)
  Two bunches in the Booster, merge in the AGS (?!)
Fixing this problem is crucial with or without the e-lens

## Slide 16: Conclusions
The lattice is in really good shape
    …and early
    …and well-documented
    …but needs to pass the spin test
    …but the Devil is always in the ramp implementaion details
E-lens driven improvements in figure of merit will only happen with a real improvement in the injectors (the Booster in particular)
Important things I did not mention
  eIPM: emittance understanding/preservation in AGS
  56 MHz: Is there are need for MD during pp?