## Slide 1: Accelerator Physics EXperiment Highlight of RUN 14
RHIC Retreat 2014
M. Bai, C-A Dept., BNL

## Slide 2: Outline
Goal
  Improve machine performance
  Support developments for RHIC future
  Support beam instrumentation development
  Inter-lab collaboration
  Enrich accelerator physics knowledge
Statistics
Highlights
Summary of RUN 14 APEX

## Slide 3: RUN 14 Focus @ APEX workshop
Heavy ion program
  New lattice options for further improvement luminocity via
    Beta* squeeze below 0.5m to accommodate the emittance reduction from Stochastic cooling
  E-lens commissioning
  Preparation for pA program
    DX aperture scan
    Au beam lifetime at proton injection energy
Injector chain
  He-3 accelerating
DX shift for preparation of asymmetric collision operation

## Slide 4: APEX Statics
Run-11 APEX average availability: ~82%(ops certified accounting)
lower ratio of Scheduled/Planned was due to the poor machine availability
RUN | Scheduled/Planned[%] | Beam Availability [%]
RUN-3 | 80 | 65
RUN-4 | 90 | 84
RUN-5 | 84 | 83
RUN-6 | 89 | 86
RUN-7 | 92 | 72 (physics: 49%)
RUN-8 | 97 | 83.4 (physics: 59%)
RUN-9 | 98 | 82.9 (physics: 54%)
RUN-10 | 79 | 82.5 (physics: 83%)
RUN-11:pp | 42 | 92 (physics: 37%)
RUN-11:Au | 63 | 78.5 (physics: 59%)
RUN-12:pp | 134 | 86.8
RUN-12:ion | 61 | 93.7

## Slide 5: APEX Statics
RUN | Scheduled/Planned[%] | Beam Availability [%]
RUN-6 | 89 | 86
RUN-7 | 92 | 72 (physics: 49%)
RUN-8 | 97 | 83.4 (physics: 59%)
RUN-9 | 98 | 82.9 (physics: 54%)
RUN-10 | 79 | 82.5 (physics: 83%)
RUN-11:pp | 42 | 92 (physics: 37%)
RUN-11:Au | 63 | 78.5 (physics: 59%)
RUN-12 | 100 | 83.3
RUN-13 | 78 | 86.6
RUN-14:Au | 100 | 79.9
RUN-14:He3Au | 100 | 88.1
Data collected from Peter Ingrassia

## Slide 6: Studies Proposed for RUN14
Study # | title | Studiers | priority | Total time [h]
14.2 | DA measurement w. 2.5GeV working point | Montag | 1B | 4
14.9 14.7 | DX aperture scan & effect of H offset in triplets | Luo, Marusic, Tepikian, Bai | 0A 1A | 11
11-33 | IP coupling matrix measurement | Tepikian | 0A | 7
14.16 | Ramp optics | Liu | 0A | 6
14.10 | Momentum aperture scan | Luo | 0A | 4.5
14.6 | Elens and Ion beam | Gu, Fischer, Luo, White | 1A | 24
N/A | Telescope Beta squeeze | GRD, Marusic, Bai | N/A | 7.5
14.8 | RHIC longitudinal impedance measurement | Blaskiewicz | 1A | 4.5
14.4 | Measurement of total AuAu cross-section | Fischer | 2A | 2
14.3 | S* knob S* correction for He3Au | Bai, Hao, GRD, Duan, Shen | 0A | 7 2

## Slide 7: Studies Proposed for RUN14
Study # | title | Studiers | priority | Total time [h]
14.5 | Non-linear driving term | Jing | 0A | 7
14.14 | Polarimeter target light observation | Huang | 0A | 2
14.13 | Beam-beam driven non-linear resonances and amplitude detuning measurement | White | 1B | 5
12-22 | Head-tail chromaticity measurement | Ranjbar | 0A | 2
 | Asymmetric beam beam study | Luo |  | 5
 | Au ramp and store just above transition | Montag |  | 3.5
 | Spin flipper AC dipole bump closure | Oddo |  | 1
 | Injection tuning | Liu |  | 1
14.12 | Off-momentum optics as a function of phase advance between low-beta insertions | White | 1A | 0
14.11 | Near-integer Beam Dynamics Study | Luo, Bai | 2B | 0
14.1 | 2.5GeV Au beam in RHIC | Montag | 1A | 0

## Slide 8: Elens Commissioning
Plan to
  exercise transverse alignment of e beam w Au beam
  Measure the impact of e-Au on beam emittance as well as beam lifetime
    The SC cooled Au beam allows for reversal of emittance growth
  Observe beam-beam driven instabilities
 | Au+Au 2014 | p+p 2015 (100 GeV)
Beam loss | ~8 %/hour burn-off dominated | ~3 %/hour beam-beam dominated
Emittance growth | negative IBS + stoch. cooling | positive beam-beam
Max beam-beam param. x | 0.006 / IP | 0.012 / IP
se-beam / sp-beam | ≈ 2 | ≈ 1
Courtesy of W. Fischer

## Slide 9: Elens Commissioning
Tune
Vertical kick (from orbit)
Effect of e-beam on Au beam’s orbit and tune was measured and used as 1st alignment tool
Courtesy of W. Fischer

## Slide 10: Elens Commissioning
780 mA (last 2 b.)
Coherent mode emerging with increasing electron current
Vertical BTF measurement with e-beam during Physics store shows reduction of the incoherent tune spread and also the emergence of coherent mode at higher e beam current
Courtesy of W. Fischer
0 mA (all bunches)
365 mA (last 2 b.)

## Slide 11: Elens Plan for coming pp RUN
Large cathodes
  allows for matched beam size w. high solenoid field
  Raises instability threshold
  Easier alignment
Transverse damper
  Bunch by bunch to fight beam-beam driven instabilities if needed
New lattice using ATS optics
  Phase advance between IP6/8 and IP10 is k
  Minimize the nonlinear chromaticity
  Polarization transparent
Courtesy of W. Fischer

## Slide 12: DA Measurement with 2.5 GeV working point
Goal is to understand the surprisingly small DA at 5.86 GeV(proton beam), for which working point was set to 0.17/0.13
Measure DA at Au regular injection energy with several different working points
Data is affected by various issues
  Blown up beam due to AtR quadrupole problem
  Non-gaussian beam profile
Nevertheless, qualitatively the measurement confirmed that DA aperture at tune of 0.17/0.13 is worse than all other choices, especially 0.13/0.12, which had been used at other low energy runs

## Slide 13: DA Measurement with 2.5 GeV working point
DA scan (only showing Blue data)
0.23/0.22
0.17/0.13
0.13/0.12
0.09/0.08
14.9
8.44
39.9
19.7

## Slide 14: DX Aperture Scan
Confirm the DX aperture scan in RUN13
Exercise the Triplet aperture scan at injection and store
Blue IP8@store
Blue IP4@store

## Slide 15: DX Aperture Scan
Confirmed the DX aperture scan in RUN13
Exercised the Triplet aperture scan at injection and store
  Critical in developing as well
  as debugging the Ramp
  Manager and WFG Manager
  to accommodate un-equal
  species collisions
  Confirmed a 15mm offset in
  triplet has negligible effect
  on beam lifetime for the
  He3Au lattice in RUN13

## Slide 16: He3Au Orbit@Store
Blue
Yellow

## Slide 17: He3Au Run
Last AuAu store
He3Au
setup

## Slide 18: Telescope beta squeeze development
Blue
SC opens up the possibility of lumi leveraging by further squeeze beta* during a physics store
Launch large beta-beat in the arcs to reach beta* of 0.5 m
This technique was inspired by the Achromatic Telescopic betasqueeze, first invented and tested at LHC by S. Fartoukh
Yellow

## Slide 19: Telescope beta squeeze development
APEX attempt
  First APEX attempt: Fill #18126
    Established the storage ramp for telescope beta squeezing to 0.6m beta*
    1st time 100% online betabeat correction with loptics
  first time reaching 50cm in Blue for Fill #18128
  first time with 50cm in Yellow for Fill #18239
End of store experiment:
  with a 12x12 test ramp (APEX) = Fill #18272
  with a full 111x111 = failed (LISA used Au14-s0 to re-optimize), Fill #18261
  with a full 111x111 = successful, Fill #18320 (both Blue and Yellow)
THOR declared operational at Fill 18413 (6/12/2014)
From GRD

## Slide 20: Telescope beta squeeze
ZDC rate
Beam Decay rate
Direct benefit of success of THOR lattice
STAR Live time and Vtx Eff
After THOR was operational and implemented at 7 hour into a physics store

## Slide 21: Summary
RUN 14 APEX program has been very fruitful. A handful of beam studies directly benefited the RUN14 performances in luminosity as well as versatility
The past decadal experience of APEX has shown that APEX is one of the crucial investment to ensure the continuous performance improvement of RHIC as well as future projects
  CeC PoP, low energy operations, etc
APEX HAS NOT been and WILL NEVER be the Stumbling Block of RHIC!!!