## Slide 1: Last words before Pavia
Bringing together the Pros & Cons Matrix
P Rossi & TK Hemmick

## Slide 2: Were we are: Summary Table
 | P Range | Contr. Jc | Param. | Pro/Con | Ext. Const | MONTECARLO Sim.
psec TOF LGAD TOF | Up to 10 Depending on the sT and L | NO | ~YES | YES | ~ YES | NO
dual RICH (aerogel, gas) | 2-60 @ 1.6 m | YES Chroma Emission Pixel Field Tracking | YES | YES | YES Simulated constant w/ momentum | YES GEMC/Geant4 AI-driven Optimization
GEM RICH (Gas Electron Multipliers) | 20-50 @1m | Chroma (Emission) Pixel Tracking | YES | YES | YES | YES (Simplified)
modular RICH (mRICH) | 2-10 @ 3 cm | YES Chroma Emission Pixel Tracking | YES | YES | YES (tracking) | ~YES GEMC/Geant4 work in progress
DIRC | 2-6 @ 1.7 cm | YES Tracking Mult. Scat Chrom, Emis, pix | YES | YES | YES | YES GEMC/Geant4 without B field

## Slide 3: High Momentum GEM RICH
Pro
  Sensor insensitive to B-field
  Short (12pe/m windowsless)
  Thin photo-cathode leads to more ideal optics.
Con
  Unknown how to bridge the gap in p-K
    High pressure??
    Different gas??
  Loses light with contaminants @ few ppm level (tougher than PHENIX HBD...)
    Requires superb gas system (OK)
    Requires better detector materials
  Photo-cathode in high radiation zone.
Supply
Return
Triple length => Transmission3
NOTE: PHENIX Contamination was the detector, not the gas system

## Slide 4: mRICH
:
Cherenkov radiator
(Aerogel) refractive index, n = 1.03
Length of the radiator, L = 3cm
lens with focal length, 𝑓= 6”
Photon Detector
3 mm pixel size
Provide a time meas. with proper sensor?

## Slide 5: mRICH: A few comments/questions
More quantitative estimate of dead area:
Aerogel size from foam holder/box.
What about corners of Fresnel lens?
  Even without lens = proximity focus.
  Blocking the corners:
    Less light.
    Only focused photons?
  Eliminate the corners?
    2nd prototype moves that way.
Why curve the array?
Simulations w/ huge incident angle!
Ng flat to 90o ??
Ns best @ 90o ?
Integration improvement dramatic if the array is flat.
Utility of the device is expanded if it provides psec TOF & Cherenkov

## Slide 6: dRICH
:
Cherenkov radiator
○ Refractive Index
n = 1.02 (aerogel) 1.0008 (C2F6)
○ length of the radiator
L = 4 cm (aerogel) , 160 cm (C2F6)
Mirrors
Photon Detector
3 mm pixel size; 200-500 nm MAPMT
Particle Generation
Originate from the vertex
PROS
CONS

## Slide 7: dRICH: A few comments/questions
“Too good” for aerogel
Limited by emission pt.
Sensors out of acceptance
Lower material budget
Lower radiation
Lower field
Limited by emission
Sensors in acceptance
Decrease emission term.
Curved at exit?
Fewer pe (1.1/1.6)?
“Implemented”
“Optimized”
sPHENIX/JLEIC fields comparable/feasible
Index seems good (pure C2F6), can be tuned by gas mixing.
What are material budget limits?
  Question to others…

## Slide 8: DIRC
:
Generic reference design: 1m barrel radius, 16 sectors
176 bars: synthetic fused silica,17mm (T) ´ 32mm (W) ´ 4200mm (L)
Photo sensors: MCP-PMTs -3x3mm2 pixels
Simulation & Test Match

## Slide 9: DIRC
Generic reference design: 1m barrel radius, 16 sectors
176 bars: synthetic fused silica,17mm (T) ´ 32mm (W) ´ 4200mm (L)
Photo sensors: MCP-PMTs -3x3mm2 pixels
Can I have that one please?
What is the sensor time resolution assumed in the simulations?
Which types of sensors are compatible with the strength/direction of B-field at the focal plane.
Should we SUPPLY a specification (max & preferred direction)?
Tricky field here

## Slide 10: TOF

## Slide 11: TOF
~0.5m for EMCAL/HCAL…tight?
Move collision vertex?
𝜋/K
K/p
LGAD 20 psec
LAPPD 5 psec
Collision pT
  Is our only hope having both vertex + time measured independently?
  Spec on pT resolution required?
  Performance of dpT vs dt?
  How do we fill in these blanks?
Not TOF, but really “t0”
What if the result of psec TOF readout of mRICH?
Ultimate resolutions/PID.
Is it like improving by sqrt(2)?

## Slide 12: Hadron Arm Cartoons
mRICH
Gas’
dRICH
Gas’
dRICH
mRICH/TOF
LAPPD
Fresnel
MPGD
PMT
Either

## Slide 13: Hadron Arm Cartoons
mRICH
Gas’
LAPPD
Fresnel
MPGD
PMT
Either

## Slide 14: Hadron Arm Cartoons
Gas’
mRICH/TOF
LAPPD
Fresnel
MPGD
PMT

## Slide 15: Hadron Arm Cartoons
dRICH
LAPPD
Fresnel
MPGD
PMT

## Slide 16: Hadron Arm Cartoons
dRICH
LAPPD
Fresnel
MPGD
PMT

## Slide 17: Barrel Cartoon
Not presently addressed by us:
  Proximity focus liquid RICH(?) ala ALICE HMPID
  dE/dx from TPC
  TORCH
DIRC
LGAD TOF
Length of equal performance ~1.2 meters

## Slide 18: Electron Arm
Need further consideration following Pavia…