## Slide 1: Collecting Thoughts On Derived Data Needs In GND

## Slide 2: Generic Processing Paths
ENDF -> RENDF
  Reconstructed pointwise resonances at 0 K
  Unionized, linearized energy grids
RENDF -> TENDF
  Thermally broadened cross-section
  And, thermally broadened emissions, if needed for GROUPR
  Addition of derived data – gas production, damage and ‘average’ data
TENDF -> ACE
  Conversions for sampling
    Point-wise/equi-probable versions of polynomials, particularly Legendre
TENDF -> GENDF
  Multigroup cross sections, derived data and scattering/production matrices
GENDF -> NDI / MATXS / DTF / …
  SN application libraries

## Slide 3: List of “Derived Data”
Generic
  Gas production and other summed or derived reactions
  Damage, dose, or other auxiliary data
  Average emission energy by emission particle / recoil; total energy deposited (KERMA)
  Q-matrix for fission product yields
MC Transport
  Legendre/Polynomial -> PDF/CDF
  PDF -> PDF/CDF
  Kalbach-Mann parameters
  PURR tables
SN Transport
  Weight function – parameterized, continuous, multigroup
    Bondarenko or other self-shielding parameters
    Associated velocity (or inverse)
  Multigroup cross section, scattering matrix, and/or transfer matrix
    Multi-band variation

## Slide 4: derivedFrom Container
Needs list of sub-elements
Each sub-element contains:
  List of link(s) to data used [0..]
  Code element
    Code name
    Code version
    Input parameters