## Slide 1: Neutron Production Capabilities: LBNL 88-Inch Cyclotron UCB High Flux Neutron Generator
Leo Kirsch November 7, 2014
This work was performed under the auspices of the U.S. Department of Energy by Lawrence Livermore National Laboratory under contract DE-AC52-07NA27344. Lawrence Livermore National Security, LLC and the Lawrence Berkeley National Laboratory contract XXX and the University of California Office of the President

## Slide 2: Who I am
I’m a 2nd year grad student at UCB, post-prelim, looking to start research
Working with Lee Bernstein in the Bay Area Nuclear Data Group funded by NA-22 and NSSC
The NSSC is a NNSA-funded $25 million grant to Seven Universities Coordinating Coursework and Experience from Student to Scientist in a Partnership for Identifying and Preparing Educated Laboratory-Integrated Nuclear Experts (SUCCESS PIPELINE)
I’ve worked on the development of the HFNG and most recently on measuring (n,n’𝛾)

## Slide 3: Why we care about (n,n’𝛾)
Neutron transport and data for applications
  Extended-EGAF: partial (n,x𝛾i) cross sections)
Nuclear Structure (ENSDF)
  Low lying states
Statistical Models
  Level densities, Radiative strength functions
  Highly excited states

## Slide 4: Deuteron Breakup n source at the 88-Inch cyclotron for 𝜎(n,n’𝛾)
Our plan is to evaluate (n,n’g) cross sections and structure and fill in any deficiencies
Activated Foils (29MeV D on Ta)
Meulders et al, Phys. Med. Biol.,
1975, 20 (2), pp 235-243

## Slide 5: Iron spectrum
1 hour of data, 2uA
natural iron: 92% Fe56; 2% Fe57
Four clovers, up current to 20uA
64 “clean”𝛾/s /barn /1%Na/cm2
Rushed analysis

## Slide 6: HFNG – what it does
Poly for Thermal Operation
Monoenergetic Beam: 104-6 n/s/cm2
Internal:
108-10 n/s/cm2
July 25th Commissioning
Indium Foil (n,n’)
108 n/s
106
104
102
100
10-9 10-7 10-5 10-3 10-1 101
(w/ 2mm Cd foil in vault)
Runs quietly
all the time

## Slide 7: Summary/What’s Next
Inelastic scattering capabilities at cyclotron
  Deuteron Breakup: 5MeV<En<60MeV
  1012 n/s/cm2 in situ; 107 n/s/cm2 beam
High Flux Neutron Generator at UCB with multiple operation modes
  Ion source based DD neutron source En=2.45MeV
  108-10 n/s/cm2 uniform flux in situ; 104-6 n/s/cm2 beam
  Moderation capabilities
  Rabbit system: shuttle time <1s
What’s Next at Cyclotron
  Chopper to improve nTOF measurements
  4 clover detectors (Clovershare)
  Neutron energy spectrum using scintillators
  Indium and Zirconium foil activation for fast fluence

## Slide 8: Collaborators
M.S. Basunia2, T. Becker4, L. A. Bernstein1,3, J.A. Brown1, R.B. Firestone2, A M. Hurst2, J. James, W. Kable1, J. Labrum1, K.N. Leung1, P. Renne4, B. Sleaford3, K. Thayer1,
K.A. Van Bibber1, J. Vujic1, C. Waltz1
1 U.C.-Berkeley Dept. of Nuclear Engineering
2 Lawrence Berkeley National Laboratory – Nuclear Science Division
3 Lawrence Livermore National Laboratory
4 Berkeley Geochronology Center

## Slide 9: Berkeley offers two complementary neutron sources
Thick target Deuteron Breakup Neutron Source (TTDBNS)
  Faraday cup in vault acts as breakup target
  1 < En (MeV) < 60
  Flux (in situ): ≥1012 n/s/cm2
  Neutron beam flux: 107 n/s/cm2
High Flux
Neutron Generator (HFNG)
  Ion-source based DD source
  Self-loading Titanium target
  En (MeV) =2.45 MeV & Ethermal
  Flux (in situ): 108-10 n/s/cm2
  Neutron beam flux: 104-6 n/s/cm2
  Rabbit System

## Slide 10: High Flux Neutron Generator at UCB - how it works
Deuterium Gas
RF
D Plasma
100kV
D beam
1-1000mA
DD Fusion
2.45MeV neutrons
H2O

## Slide 11
The 56Fe(n,n’g2->0) partial cross section was well-measured
using the GEANIE spectrometer

## Slide 12: Neutron spectral characterization Activation foils
Meulders et al, Phys. Med. Biol.,
1975, 20 (2), pp 235-243
Result of a constrained linear least-squares fit and non-linear 5-parameter functional fit to five thresholding activation reactions.
(29 MeV deuterons on tantalum)

## Slide 13: Geochronology: K-Ar Dating Method
Rocks
39K
40K
t1/2=1.2 Gyr
40Ar
Determine Age
We have some rocks. We want to know how old they are.
At formation, an initial fixed quantity of potassium is trapped in each rock.
Electron Capture Decay of 40K to 40Ar: half life of 1.2 billion years.
By measuring 40K content versus 40Ar content, can determine age of rock sample.
Measure K Content
Measure Ar Content

## Slide 14: Geochronology: K-Ar Dating Method
Two Different Measurements Required to Determine Age:

## Slide 15: Geochronology: 40Ar/39Ar Variant
Rocks
39K
40K
t1/2=1.2 Gyr
40Ar
Determine Age
Enter nuclear physics: the 39K(n,p)39Ar reaction.
Neutron irradiation of K-containing samples will produce 39Ar.
Comparison of measurement of two Ar isotopes determines age.
Measure K Cotent
Measure Ar Content
39K(n,p)39Ar
39Ar

## Slide 16: Geochronology: 40Ar/39Ar Variant
Single Measurement Required to Determine Age:
With neutron fluence parameter, J:

## Slide 17: Neutron Fluence Parameter, J
Currently, J is determined from irradiating “standard” samples of “known” age. These standards are arrayed around the sample, and J is extrapolated between them.
Introduces uncertainty in age from standards and increased time spent irradiating and analyzing standards.
Solution: measure J. Use activation foils to measure the flux, and use a known quantity of potassium to measure the cross section.
Fixed
Fixed
Known
Unknown