## Slide 1: Criticality and Reaction Rate Calculations with CIELO “Starter” Files
A.C. (Skip) Kahler
Los Alamos National Laboratory
Cross Section Evaluation Working Group
November 4-6, 2014

## Slide 2
ABSTRACT We summarize criticality calculations with ICSBEP benchmarks performed with a selection of CIELO “starter” files, including 16O, 56Fe, 235,238U and 239Pu.

## Slide 3: CIELO Nuclides
1H
16O
  Preliminary files from ORNL (Leal) and LANL (Hale).
56Fe
  A joint ORNL/BNL effort; “ORNL4_e1LevelFixes_4.11.2014.endf”.
235U
  Revised RR (ORNL, Leal) inserted into JENDL-4 and ENDF/B-VII.1.
238U
  IAEA “ib33”.
239Pu
  Build upon SG34 (Toshihiko Kawano); pfns by Denise Neudecker.

## Slide 4: CIELO Nuclides
NJOY Processing
  ACE Files created by NJOY2012.
  16O and 56Fe contain LRF=7 Resolved Resonance data
    NJOY patch by Bob MacFarlane can create scattering angular distributions based upon these RR data (a work-in-progress).
    LANL has shared this patch on an “as-is” basis.
  235U
    Revised resonance parameters inserted into JENDL-4.0 and ENDF/B-VII.1 files.
  238U
    A mix of sections with data to 20 MeV or 30 MeV.
    LANL arbitrarily deleted 20+ MeV data to overcome NJOY processing issues.
  239Pu
    Build upon SG34 work; contains either the ENDF/B-VII.1 PFNS or a modified PFNS (see Neudecker).

## Slide 5: 16O Results
Comparison of Leal and Hale 16O elastic scattering and (n,α0) cross sections.

## Slide 6: 16O Results
LCT7.x, cases 1 through 4, vary the rod pitch … undermoderated to overmoderated. Revised 16O files cause a ~30 to more than 100 pcm decrease in calculated eigenvalues, but this difference is of questionable statistical significance. The “Leal” file includes resonance parameter calculated angular distributions.
Much of the 16O absorption occurs in water regions far removed from the fuel assembly, hence the Hale eigenvalues are not expected to change significantly when this file is upgraded.

## Slide 7: 56Fe Results
Comparison of ENDF/B-VII.1 56Fe MF3/MT2 with that calculated by NJOY2012 from a pre-ORNL4 file (56Fe file by Leal/ORNL; NJOY plot by Bob MacFarlane).

## Slide 8: 56Fe Results
Comparison of ENDF/B-VII.1 56Fe MF4/MT2 Legendre Coefficients with those calculated by NJOY2012 from a pre-ORNL4 file (56Fe file by Leal/ORNL; NJOY plot by Bob MacFarlane).

## Slide 9: ICSBEP Benchmarks with Iron
HMF13 – Spherical HEU assembly with 3.65 cm thick steel
HMF21 – Spherical HEU assembly with 9.7 cm thick steel
HMF24 – Spherical HEU assembly with 0.8 cm thick steel & 9.65 cm thick polyethylene
HMF87 - HEU cylindrical assembly with interstitial steel
HMF88 – HEU cylindrical assembly with interstitial steel or steel & polyethylene plus a polyethylene radial/axial reflector
PMF25 – Spherical 239Pu assembly with 1.55 cm thick steel
PMF26 – Spherical 239Pu assembly with 11.9 cm thick steel
PMF28 – Steel (19.65 cm thick) reflected 239Pu spherical assembly
PMF32 – Steel (4.49 cm thick) reflected 239Pu spherical assembly

## Slide 10: 56Fe Results
Previously obtained good eigenvalues are retained … rem results suggest cross section revisions and new angular distribution results undo each other!

## Slide 11: ICSBEP Benchmarks Used for 239Pu Testing
PMF1 – Jezebel, a spherical 239Pu assembly
  Also central region spectral indices 238Uf/235Uf; 237Npf/235Uf; 239Puf/235Uf plus selected (n,2n) ratios
PMF6 – Flattop-Pu, a spherical 239Pu core plus a natU reflector
PSTxx – A subset of 8 PST critical assemblies used during SG34 data testing

## Slide 12: 239Pu Results
Jezebel eigenvalue sensitivity … prompt ν, fission cross section, pfns, …

## Slide 13: 239Pu Results

## Slide 14: 239Pu Results
TK1 = e71 plus SG34 RR, SG34 prompt nu to 650 eV; “DN” = Neudecker pfns.
Benchmark | E71 (w/fixed 239Pu) | E71 + SG34 239Pu | E71 + TK1+DN 239Pu
PMF1 (Jezebel, rev3) | 1.00079 | 1.00037 | 0.99821
PMF6 (Flattop-Pu) | 1.00106 | 1.00054 | 0.99849
PST1.4 | 1.00500 | 1.00199 | 1.00932
PST4.1 | 1.00389 | 1.00044 | 1.00683
PST9 | 1.01939 | 1.01543 | 1.01695
PST12.10 | 1.00402 | 1.00083 | 1.00475
PST12.13 | 1.00970 | 1.00611 | 1.00757
PST18.6 | 1.00462 | 1.00202 | 1.00461
PST34.4 | 1.00254 | 0.99922 | 1.00320
PST34.15 | 0.99731 | 0.99679 | 0.99988
PST average: | 1.00581 | 1.00285 | 1.00664

## Slide 15: 239Pu Results
TK1 = e71 plus SG34 RR, SG34 prompt nu to 650 eV; “DN” = Neudecker pfns.
Reaction | 238Uf/235Uf | 237Npf/235Uf | 239Puf/235Uf
Experiment | 0.2121 | 0.9730 | 1.4300
E71 "Big Paper" | 0.2085 | 0.9708 | 1.4242
E71 "Big Paper" C/E | 0.983 | 0.998 | 0.996
E71 + DN pfns | 0.2038 | 0.9582 | 1.4206
E71+TK1+DN pfns C/E | 0.961 | 0.985 | 0.993
Reaction | 238U(n,2n) | 169Tm(n,2n) | 191Ir(n,2n)x190Ir
Experiment | 1.0580E-02 | 3.1250E-03 | 3.2060E-03
<E>, MeV | 8.5 | 10.7 | 10.7
E71 Calc | 1.3259E-02 | 3.6774E-03 | 3.6439E-03
E71 Calc C/E | 1.253 | 1.177 | 1.137
E71+TK1+DN Calc | 1.2127E-02 | 3.2047E-03 | 3.1748E-03
E71+TK1+DN Calc C/E | 1.146 | 1.026 | 0.990

## Slide 16: 235U Results
JENDL-4.0 + ORNL FAST benchmark results are generally worse than those obtained with ENDF/B-VII.1 + ORNL, but …
GODIVA (HEU-MET-FAST-001) |  | 
Cross Section Set | Benchmark keff | kcalc
ENDF/B-VII.1 | 1.000(1) | 0.99983(3)
E71 + ORNL8 |  | 0.99985(2)
J4 + ORNL8 |  | 0.99757(2)
Flattop-25 (HEU-MET-FAST-028) |  | 
ENDF/B-VII.1 | 1.0000(16) | 1.00285(2)
JENDL-4.0 |  | 0.99779(9)
E71 + ORNL8 |  | 1.00300(13)
J4 + ORNL8 |  | 0.99899(13)
Big-10 (IMF7, detailed model) |  | 
ENDF/B-VII.1 | 1.0045(7) | 1.00443(2)
JENDL-4.0 |  | 0.99710(7)
E71 + ORNL8 |  | 1.00471(8)
J4 + ORNL8 |  | 0.99764(11)

## Slide 17: 235U Results
but …
JENDL-4 + ORNL calculated eigenvalues are more accurate than ENDF/B-VII.1 + ORNL.

## Slide 18: ICSBEP Benchmarks Used for 238U (IAEA “ib33”) Testing
HMF28 – Flattop-25 (HEU core and natU reflector)
IMF7 – Big-10 (detailed model). A large heterogeneous assembly of uranium plates
IMF1 – Cases 1 and 4 (“Jemima” plates)
PMF6 – Flattop-Pu (Pu core and natU reflector)

## Slide 19: 238U Results
Calculated eigenvalues with the “ib33” file are often closer to unity than those obtained with pure ENDF/B-VII.1 cross sections.

## Slide 20: Concluding Observations
LANL data testing to date has been limited to a few ICSBEP critical benchmarks
  There is much more testing needed!
“Starter” files (yes plural!) exist for 16O, 56Fe, 235,238U and 239Pu … but we expect there will be numerous additional iterations.
Testing with replacement of a single data set will always yield a worse result when compared to a “tuned” library.
Integrated testing with multiple new files has not been performed (yet!).