## Slide 1: Prompt fission neutron spectra of U-235, integral reaction rates & U-238 cross sections
Andrej Trkov and Roberto Capote
NAPC - Nuclear Data Section, IAEA, Austria

## Slide 2
OUTLINE
Update of U-238 after ib33: (n,2n)
Validation of integral measurements of reaction rates and fission spectra – Cf-252/U-235 ratios
IAEA Projects (PFNS CRP & Standards DDP)
  Selection of experimental data
  Initial scaling of experimental data
  Generalised least-squares fit with GANDR
  Impact on integral benchmarks
Conclusions

## Slide 3: U-238 Starter File
ib25 + physics  inelastic up, (n,2n) down ib33
IRDFF-v1.05 238U(n,2n) close to ib25
PROFIL experiment  requires (n,2n) up
SPA (PFNS U-235)  requires (n,2n) up but
SPA (SF Cf-252) close to ib25
New ib34: changes to (n,n’), (n,2n)
See:” https://www-nds.iaea.org/CIELO_U238/”

## Slide 4: 238U(n,n’) evaluations

## Slide 5
238U(n,2n) evaluations
7 8 9 10 11
Incident Energy (MeV)
SPA XS in 252Cf(sf) PFNS
IRDFF-1.03 20.607
ENDF-B/VII.1 21.363
Blinov et al, 20.61 ± 2.02

## Slide 6: 238U(n,2n) evaluations
SPA XS in 252Cf(sf) PFNS
IRDFF-1.03 20.607
ENDF-B/VII.1 21.363
Blinov et al, 20.61 ± 2.02
238U(n,2n) evaluations

## Slide 7: IRDFF-v1.05: 238U(n,2n)
[42] Kobayashi et al, YAYOI reactor core FNS, EXFOR 20693015
[43] Hashimoto et al, KUR reactor core FNS, EXFOR 20810002
[45] Blinov et al, 252Cf(sf) PFNS, EXFOR 40996002,
(Corrected to new monitors from IRDFF)

## Slide 8: Possible sources of error in (n,2n)
Many measurements were made inside the reactor core
 Strong gamma field
Possible impact of (γ,n) reactions (K. Zolotarev)
All (n,2n) reactions may be affected
Implications for the PROFIL and SPA measurements
(γ,n) contribution needs to be determined

## Slide 10: U-238 impact on benchmarks

## Slide 12: Information from SPA cross section ratio 252Cf (sf)/235U(nth,f)
Check consistency between SPA cross sections measured in 252Cf (sf) and 235U(nth,f) fields for E50% < 11 MeV (good PFNS measurements)
Determine 252Cf (sf)/ 235U(nth,f) spectrum ratio at E50% >11 MeV (poor PFNS measurements)
  May define the 235U(nth,f) PFNS in that energy range, but
  SPA experimental data not consistent

## Slide 13: Desired new measurements
238U(n,2n) in 235U(nth,f) PFNS (behind fission plate, careful room-return correction by MC simulation, (γ,n) expected to be small)
27Al(n,2n) precision measurement by AMS (mass spectrometry) after irradiation in PFNS of 252Cf (sf) and 235U(nth,f) (behind fission plate)
27Al(n,2n) E50% ~ 16 MeV
27Al(n,2n) differential cross section already measured by AMS (Wallner et al) up to 19 MeV

## Slide 14
IAEA CRP on PFNS evaluation (2008-2014)
INDC(NDS)-0541, RC et al, Summary Report of the Consultants’ Meeting on Prompt Fission Neutron Spectra of Major Actinides, Nov. 2008
Matrix ©
Déjà vu
A. Smith, P. Guenther, G. Winkler, D.L. Smith, NSE 76(1980) 357

## Slide 15
, normalised to 1)
What to evaluate? PFNS or Yield?
Without loss of generality (ENDF-6 PFNS representation):

## Slide 16: Definition of (ND) Evaluation
A properly weighted combination of selected experimental data (and modelling information).
Evaluation approaches (WPEC SG24)
“Non-model” LSQ fit (Neutron standards)
Model prior + GLSQ fit of experimental data
(in the “parameter” or “data” space)
Stochastic: BFMC, FMC, TMC, UMC, UMC+TMC, …
Experimental data and uncertainty analysis

## Slide 17
235U(nth,f) PFNS, IAEA CRP, 6 years later
Ratio to
Maxw.(T=1.32)
Eaver[MeV]
Maxw 1.98 (T=1.32)
Maslov 1.96 Semi-empirical
Morillon 1.97 LANL model
Shu 2.08 Semi-empirical
Talou 2.00 LANL model
Vogt 1.91 MC Freya
Pronyaev 2.00
ENDF-B/VI 2.03
Eval. 2.000(9)

## Slide 18: Sensitivity to high-leakage solution benchmarks from ICSBEP

## Slide 19: DDP on Neutron Cross Section Standards
235U(nth,f) PFNS candidate for secondary standard (in addition to 252Cf (sf) PFNS)
Primarily based on differential data
Preference for non-model evaluations – WHY?
  Because models may introduce a bias (shown later)!

## Slide 20: PFNS evaluation: Current Experience
All data used as “shape data”; systematic errors are accounted in the normalisation uncertainty (i.e. nu-bar)
nu-bar is measured by independent experiments with much smaller uncertainty

## Slide 21: PFNS evaluation: Procedures
Identify a (reliable) data set that overlaps with all others ( reference data set)
Scale all other measurements to the reference in the overlapping region (suitable scaling)
Scaled union of all data sets covers a broad energy range  apply normalisation (minimum uncertainty due to broad E-range)
Proceed with GLSQ fitting

## Slide 22: PFNS 235U(nth,f): Data selection
Lead Author | EXFOR Entry No. | Comment
B.I.Starostov,ET.AL. (85) | 40930006(4) | Flag 4 only, others = ratio
A.Lajtai,ET.AL. (85) | 30704003 | E < 0.16 MeV (Li glass eff)
N.Kornilov*,ET.AL. (10) | 31692006 | Ratio to Cf-252(sf)
Wang Yufeng,ET.AL. (89) | 32587002 | E > 1.3 MeV
V.N.Nefedov1*,ET.AL. (83) | 40871011 | Ratio to Cf-252(sf)
V.N.Nefedov2*,ET.AL. (83) | 40871012 | Ratio to Cf-252(sf)
B.I.Starostov*,ET.AL.(83) | 40872007 | Ratio to Cf-252(sf)
A.S.Vorobyev*,ET.AL. (13) | 41597002 | Ratio to Cf-252(sf)

## Slide 23: Model Fit (Examples)
SCALE Method (single parameter, scaling the energy = E_av; ref.: N. Kornilov)
WM Basis Function Method (linear combination of Watt and Maxwellian distributions, four parameters)

## Slide 24: SCALE_0 (fixed data) normalisation)

## Slide 25: SCALE_6 (iterated solution)

## Slide 26: Basis (PNT_0, fixed norm.) for compar.

## Slide 27: Basis (PNT_6, iterated) for compar.

## Slide 29: Non-Model Fitting
Scaled & normalised data fitted by GLSQ procedure with GANDR
Use non-informative prior (100% uncorr. Unc.)
Assumptions for a further step:
  No single experiment dominates the fit
  Fit is a better approximation to the truth
  Use fitted curve to rescale (and renormalise) experimental data
  Redo the fitting and iterate to convergence

## Slide 30: 235U(nth,f) PFNS GANDR fit (lin E)
PFNS 235U (n,f)/Maxw(T=1.32 MeV)
non-model evaluation for STD (GANDR)
Eaver(GANDR)= 2.000(9)
Eaver(B/VII.1) = 2.03

## Slide 31: 235U(nth,f) PFNS GANDR fit (log E)
PFNS 235U (n,f)/Maxw(T=1.32 MeV)
non-model evaluation for STD (GANDR)
Eaver(GANDR)= 2.000(9)
Eaver(B/VII.1) = 2.03

## Slide 32: GANDR fit without normalisation
No norm:
6.4%
235U(n,f)/Tmaxw(1.32 MeV)

## Slide 33: Iterated GANDR fit with normalisation
__ Maxw. (T=1.32)
--- GANDR (1 iter., normal.)
--- GANDR (6 iter., normal.)
__ PNT fit (z0_MIX)
1.72%
235U(n,f)/Tmaxw(1.32 MeV)

## Slide 34
GANDR normalisation: Uncert. analysis
0.8% unc.
consistent exper. data

## Slide 35: Features of the GANDR fit
Little change with iterations
Minimum PFNS uncertainty 0.8% almost equal to the minimum yield uncertainty
In the tails the PFNS uncertainty is equal to the prior (no measured data, no model correlations)

## Slide 36: Spectrum fit for incident fast neutrons
Data selected for incident neutrons in the range 0.5 MeV to 2 MeV
The same procedure was followed
Narrower data range, fewer data sets, larger scattering
Slight increase in the average energy (+8 keV)

## Slide 37: 235U(nfast,f) PFNS GANDR fit (log E)
PFNS 235U (n,f)/Maxw(T=1.32 MeV)
0.5 1 2 5 10
Outgoing neutron energy (MeV)

## Slide 38: 235U(nfast,f) PFNS GANDR fit (selected)
PFNS 235U (n,f)*100/Maxw(T=1.32 MeV)
1 2 5 10
Outgoing neutron energy (MeV)
1 2 5 10

## Slide 39: GANDR fit thermal & fast
thermal
fast

## Slide 40: Integral effects
ICSBEP Benchmarks were analysed
Increase in reactivity of high-leakage thermal solutions partly compensated by Hale’s O-16 evaluation or by a decrease of nu-bar
Decrease in reactivity of fast assemblies partly compensated by U-238 – overall improvement

## Slide 41: 235U(n,f) PFNS (thermal solutions)

## Slide 42
235U(n,f) PFNS, 16O (thermal solutions)
PRELIMINARY!

## Slide 43
235U(n,f) PFNS, 238U (fast assemblies)

## Slide 44: Combined 235U(n,f) PFNS, 238U

## Slide 45: Labels legend
e71 ENDF/B-VII.1 (reerence)
ib25 Older version of U-238
ib33 U-238 CIELO starter file
ib33n ib33 with updated (n,2n) from IRDFF
g6 U-235 PFNS GANDR fit
ib33n_g6 combined (as above)

## Slide 46: Conclusions U-238
No major revision to ib33 starter file
(n,2n) reaction investigated (IRDFF-v1.05)
Uncertainties in integral measurements to be clarified
Contribution of (γ,n) to be determined

## Slide 47: Conclusions U-235
Non-model fit of U-235 PFNS thermal and fast
Average energy lower than ENDF/B-VII.1
Reactivity increase for high-leakage thermal solutions, decrease for fast assemblies
Possible compensating effects were studied, namely new O-16 data, nu-bar, new U-238

## Slide 48: ADDITIONAL SLIDES

## Slide 49: Measured PFNS data normalisation
Kornilov et al (IRMM) data taken as reference
All data converted to 252Cf/235U or 235U/Mxw(1.32MeV) ratios
252Cf/235U or 235U/Mxw(1.32MeV) ratios integrated over the overlapping interval for each experiment
Upper energy cut-off 10 MeV
Measured data normalised to match integrals over the overlapping regions
REALLY independent of ANY model

## Slide 50: Union of all data (PNT_raw)
All data converted to 235U/Mxw(1.32MeV) ratios
Union of all data in the ratio space prepared
Data converted back to spectrum
Integral of the spectrum normalised to one – all data re-normalised with same normalisation factor (0.8% correction)
Average energy of raw data spectrum is 1.998 MeV
(uncertainty can not be estimated by this method)
Notes: Added note on the contribution of extrapolated spectrum to the integral, 11-Aug-2014

## Slide 51: Fitting the data – simple model (PNT)
Initial work
Basis function: linear combination of a Watt function and a Maxwellian function (4 free parameters).
Chi-square minimisation to determine optimal parameters
Check influence of removing datasets (e.g. Starostov data, etc.)
Extended work
Assume fitted function is a better approximation to the true spectrum – normalise the data to the fitted function (model dependence ?)
Repeat the fitting,
Iterate to convergence

## Slide 52: Results (PNT = microscopic data only)
The average energy is 2.000(9) for all data
The average energy is 1.986(9) without Vorobyev
Convergence is rapid (very little change to Chi-squared after the first renormalisation of data)
Iterations slightly change the shape, but not the average energy

## Slide 53: Convergence of Basis Function (PNT)
Chart: 
| 0 | 1 | 2 | 3 | 4 | 5 | 6
PNT | 0.6016 | 0.4486 | 0.4478 | 0.4476 | 0.448 | 0.448 | 0.4477

## Slide 54: Starostov data excluded (lin scale)

## Slide 55: Starostov data included (PNT_0 lin scale)

## Slide 56: Iterated solution (PNT_6, linear scale)

## Slide 57: Starostov data excluded (log scale)

## Slide 58
Starostov data included (PNT_0 log scale)

## Slide 59: Iterated solution (PNT_6, log scale)

## Slide 60: Fitting the data (SCALE)
Method by Kornilov (NSE 169, p.295, 2011)
Parameter as=Eav(235U)  identity
Assumption: PFNS shape equals 252Cf s.f. shape with linear transformation of the energy axis (Eq.4)
With fixed data normalisation, Eav(235U) is the only free parameter, giving Eav(235U)=1.980MeV
Improvement of fit requires distortion of data normalisation
After iterations, Eav(235U)=1.973MeV

## Slide 61: Convergence of Basis Function (SCALE)
Chart: SCALE
| 0 | 1 | 2 | 3 | 4 | 5 | 6
SCALE | 1.0435 | 0.7039 | 0.6881 | 0.6858 | 0.686 | 0.6883 | 0.6883

## Slide 62: SCALE_0 (fixed data) normalisation)

## Slide 63: SCALE_6 (iterated solution)

## Slide 64: Basis (PNT_0, fixed norm.) for compar.

## Slide 65: Basis (PNT_6, iterated) for compar.

## Slide 66: SCALE_0 (fixed data normalisation, log)

## Slide 67: SCALE_6 (iterated solution, log)

## Slide 68: GANDR GLSQ solution
Start with some initial normalisation
Perform GLSQ fit with GANDR
Normalise the spectrum
Re-scale the data to the new spectrum
Redo the GANDR fit (iterate)
Solution is equivalent to including data scaling factors as fitting parameters in GLSQ fit

## Slide 69: GANDR fit – 6 iterations

## Slide 70: Basis (PNT_6, iterated) for comparison

## Slide 71: GANDR fit – log scale

## Slide 72: Iterated solution (PNT_6, log scale)

## Slide 73: GANDR Normalisation
Fitting performed without normalisation constraint
Total uncertainty in spectrum normalisation is about 3%
Uncertainty in the average energy is about the same
The minimum uncertainty is about 3% at 2 MeV
Minimum uncertainty in the PFNS is 0.81%
Covariance matrix is strongly correlated in the range where data are available

## Slide 74
GANDR fit (no normalis.) – covariances
~3% unc
corr>0

## Slide 75: GANDR normalisation (Cont.)
Normalisation of the spectrum is trivial
Normalisation uncertainty is removed from the covariance matrix using Eq. 35.2 from the ENDF Manual
Uncertainty in the normalisation is zero by definition
Uncertainty in the (norm.PFNS) average energy is 0.45%
Minimum uncertainty in the norm.spectrum is 0.81%
Covariance matrix shows discrete structure in the range where data are available

## Slide 76
0.8% unc
anticorr
GANDR normalisation (Cont.)

## Slide 77
Ratio to
Maxw.(T=1.32)
--- Maxw. (T=1.32)
--- GANDR (no norm)
--- GANDR (normal.)
--- PNT fit
GANDR normal. Vs no-normalisation

## Slide 78: 235U(n,f) PFNS, 238U (thermal solutions)

## Slide 79: Conclusions (Methodology)
PFNS are SHAPE data (no absolute data needed)
Evaluated neutron yield consistent with measured
No need to (adhoc) increase of the PFNS uncertainty
SCALE method is a remarkably good first order approximation to PFNS spectrum, BUT
One adjustable parameter is not sufficient to accurately fit arbitrary measured data, slightly distorted spectra
PFNS evaluation results of the PNT_raw, PNT and GANDR fits in excellent agreement

## Slide 80: PFNS average neutron energy
E-bar [MeV] | Case
1.998 | PNT_raw
1.998 | PNT_0_no_Starostov
2.001 | PNT_0
1.993 1.986 | PNT_6 (iterated) PNT_6_no_Vorobyev
1.985 | SCALE_0_no_Starostov
1.988 | SCALE_0
1.973 | SCALE_6 (iterated)
1.974 | SCALE_6_no_Starostov
2.004 | GANDR_6(iterated)
Notes: PNT_raw typo corrected (1.999  1.998, 11 Aug 2014)

## Slide 81: Conclusions (average neutron energy)
The most likely average neutron energy is 2.000(9) MeV
If Vorobyev data excluded – 1.986(9) MeV
The SCALE method underestimates the average energy due to inherent assumptions about the shape of the spectrum (1.974 MeV, Kornilov NSE 169 (2011) 290 )
THANKS FOR YOUR ATTENTION !