## Slide 1: 1.2 TPC Update
TK Hemmick
Production & Services
Faculty, Graduate Students, Undergraduate Students, Engineers
Name shout outs with orange background; Mistakes/omissions are the fault of TKH

## Slide 2: Inner Field Cage HV
Inner Field Cage Test
Max Running Voltage = 44.5 kV
Sample Material re-tested (2 years on shelf) to 80 kV.
Actual field cage tested to 50 kV
  Current as expected.
  Zero “activity”.
  1 hour test.
Prakhar Garg, Klaus Dehmelt, Henry Klest, Luke Legnosky

## Slide 3: Voltage Tests for Trip Conditions
A concern raised during the prior review concerning sparks during trip conditions:
  Normally module-to-module is at the same voltage (tail = obvious exception).
  Normally module-to-cage is at the same voltage.
  When one module trips, it becomes ground.
A simple stand-in test:
  GEM-to-GEM in air:
    Position two GEMs accurately.
    Ground one (top & bottom)…HV on the other.
    Run up the HV to the spark point.
  GEM-to-GEM in gas:
    Built a clear gas vessel (aquarium).
    Flow 6 turns Ne:CF4.
  GEM-to-Field Cage
    Use 3D printed fake wall (establishes spacing).
    In air and in gas.
Caveats:
No gain
No radiation
Running condition: 4.5 kV
Prakhar Garg, Henry Klest

## Slide 4: Results
Test Procedure:
  Run Bertan supply to limit (5 kV…modified by BNL) watching current.
  Wait at 5 kV (zero activity under all conditions).
  Run Glassman supply to spark point.
  Observe spark locus (in gap?, surface to surface?, moves around?, …)
Gap | Gas | Spark Point | Locus/pattern
GEM-GEM/tail | Air | 14 kV | SurfaceSurface Fixed
GEM-GEM/tail | Ne:CF4 50:50 | 13 kV | SurfaceSurface Moving
GEM-Cage | Air | 13 kV | SurfaceSurface Fixed
GEM-Cage | Ne:CF4 50:50 | 11.5 kV | SurfaceSurface Fixed
Air 14 kV
Ne:CF4 13 kV
Ne:CF4 11.5 kV
All tests stable at 10 kV
Prakhar Garg, Henry Klest

## Slide 5: Module Progress
  Frames
  GEMs
  Pad Planes
  Strongback
Frames 100% Complete, Delivered to Factories

## Slide 6: GEMs Order Placed (today)
GEM order placed today.
Should be out this week. (EVMS: $$ = Time)
Klaus Dehmelt

## Slide 7: School(s) of ROC
Oleg Grachov (WSU): GEM Factory Manager
  Personally Trained all personnel via WSU visits.
  Wrote Procedures to be followed at all sites.
  Make production GEMs and guide/supervise all factories.
Oleg Grachov
School of ROC

## Slide 8: Early GEM Results from WSU
Excellent results from all framed GEMs.
Vanderbilt (Sourav) actively framing pre-production GEMs.
Also excellent currents!
Vanderbilt trained: Sourav Tarafdar (lead person)
Temple Trained: Matt Posik (lead person)
Weizmann Trained: Evgeny Shulga (lead person)

## Slide 9: Strongbacks (100% Complete)
All strongbacks were test fitted to one wagon wheel.
Perfect fits.
Spring Energized Seals:
  Inner Field cage:
    Both fit.
  Outer field cage:
    Two seals not identical.
    One 0.5-0.75” too large circumference.
  Company will replace (no charge).
  No schedule impact.
Henry Klest, Aiwu Zhang, Ross Corliss

## Slide 10: R3 Pad Planes
New vendor (whew)
Excellent quality.
July 15 estimate.
R2 & R1 order TBD
  Same vendor
  Sole Source

## Slide 11: Assembly of Field Cage & Modules
The TPC is assembled at Stony Brook and transported to BNL via air ride suspension truck.
During transport, the TPC and Assembly Cart will be mounted on top of an isolation system.
All parts except green tube being welded now.
Cage Assembled Vertically
Modules Installed Horizontally
John Cozzolino, Connor Miraval

## Slide 12: TPC FEA Position 1
Connor Miraval

## Slide 13: TPC FEA Position 2
Connor Miraval

## Slide 14: TPC FEA Position 3
Connor Miraval

## Slide 15: Central Membrane Stripes (Calibration)
Evaporated Al stripes on Gold (ENIG) surface.
~2X MIP p.e. per flash from Al; few from Au.
Laser rate ~ trigger rate.
Stripe Pattern: ~4000 stripes per side.
Hall of the Mountain King
Sara Kurdi, Nikhil Kumar, Ross Corliss
g4hits!

## Slide 16: Evaporator Rig
Uses the CsI evaporator (from HBD days)
  Upgraded for e-beam source.
  Cr followed by Al
Multiple panels in one step.
“Mask” asserts pattern of Al stripes.
Mask for evaporation
Petal awaiting Evap
Nikhil Kumar
Src
Aperture
Slow rotation
Src
Aperture
Nikhil Kumar, Ross Corliss, Klaus Dehmelt

## Slide 17: General Layout of diffuse light source
Beam Expander (~98%)
(Galilean telescope)
Light Pipe Homogenizer (~98%), uniformity depends on LP length
Couple flat top laser light into fiber bundle
Beam pick-off for energy monitor/trigger (~5%)
Fiber bundle
15 fibers: 12 + 3 spare
Large core (600um), multi-mode, step index bundled fibers (Attenuation ~500dB/km, Trans. ~ 95%/km)
1 fiber bundle per laser head; 1 laser head per endcap
Quad diffuser on each of 12 fibers provides ~uniform illumination
Bob Azmoun, Nikhil Kumar, Ross Corliss

## Slide 18
DAM (Felix) Card
SAMPA v5
FEE Card
Electronics
Low Voltage Plant
Optical Data Plant
Takao Sakaguchi, John Kuczewski, Jin Huang

## Slide 19: SAMPA Deliveries Starting
Wow, Sunday Delivery!
SAMPA accepted.
All tests passed.
OK to proceed:
  Balance of Engineering Run
  Production Run.
~4400 packaged SAMPA chips to ship soon.
Reminder:
Accounting for spares, yield, etc… the shipment is less than ½ the need, but it is still very significant.
Marco Bregant, Wilhelmus Van Noije, Takao Sakaguchi, David Silvermyr

## Slide 20: FEE card production
MAJOR purchase requires major paperwork & careful bidding process.
  Three trusted vendors identified by us and recommended.
  Three bids came in (reasonably similar costs)
Order will include first articles.
  First article boards will be tested before release of full order.
  First article boards will use V5 chips (sufficient quantity passed Lund testing)
  No additional paperwork after approval of first boards to complete acquisition.
In the hands of BNL purchasing.
Now
Soon
Takao Sakaguchi, John Kuczewski, Joe Mead, Kevin Wolniewicz

## Slide 21: Line Laser (“lighthouse”)
  Light carried into volume via TIR in quartz bar.
  Full map of TPC volume achieved by scanning the beam.
    Full phi
    Up to 85o incident angle.
Full 3D Map of Static Distortions (E-field only, E & B-fields)
Dan Cacace, Kristina Finnelli

## Slide 22: Dual Mirror system controlled by piezo motors
Advantages
  All angles possible.
  Larger mirror pieces.
  Simpler machining.
  Redundancy of angles.
Disadvantage
  Two motors.
Selected as design.
Can avoid this effect:
Dan Cacace, Kristina Finnelli

## Slide 23: Laser Bench Updated
Dog Leg Mirror #1
Dog Leg Mirror #2
Primary steering
Secondary steering cavity (SSC)
Beam shaping optics
Dan Cacace, Connor Miraval

## Slide 24: Updated Optical Table Assembly
INTT and MVTX will like this
All the parts of laser system moved away from beam pipe.
Elegant
NOTE: Everywhere you see green, you’re looking at low mass.
Dan Cacace, Connor Miraval

## Slide 25: TPC Wagon Wheel Cooling
Wagon wheel adding Line laser heads & Cooling Blocks.
Laser head compactly directs line laser into quartz bars.
45% of gas system orders are now placed (Thanks Rob).
NOTE:
Further updated picture available from Dan
It was “live share” of Inventor screen.
Updated pics coming soon…
Next cooling step requires lab access for Rob Pisani
Rob Pisani

## Slide 26: ANSYS Temps – Improvement
Input: Air 22C, Water in 16C, 0.62l/min and 2.14l/min flow, FEE 15W (FPGA 4W, REGs 4W, SAMPAs 7W), Gap Pad 2.4W/mK
PCB 1W/mK (iso), Connector 16W/mK (iso), Water HTC 2000W/m2K and 3000W/m2K, Air HTC 2W/m2K, epoxy conductance 11800W/m2K
Other: Gap Pad Pockets Added, Regulators Added, Blocks 4” Tall, Aluminum Plates 220W/mK and Blocks 160W/mK
Pressure
Temperature
Dan Cacace, Rob Pisani

## Slide 27: Cooling Scheme Further Details
Rob Pisani

## Slide 28: Summary
TPC making very much progress despite challenging times.
Design work coming along very efficiently,
Lab work delayed somewhat, but resuming.
  Limited undergrad availability.
  SBU will add a technician after job search (at least 1 good candidate)
Note shown, but significant:
  HV Central Membrane Supply ordered.
  HV GEM Power Supplies ordered.
  Mechanics for Central Membrane assembly complete. (road trip after evaporation SBU  Vandy)
  Hall Probes & Rad monitor allocated space.
Non-TPC news:
  SBU shop remained open, but reduced staff.
    EMCAL sawteeth were kept running.
    Machinists made EMCAL cooling loop parts while working from home.

## Slide 29: Laser Bench – Improvement

## Slide 30: Apparent Ionization profile with Trans. Diffusion
Since trans. diffusion contributes significantly to broadening the ionization profile at large drift lengths, is it better to focus the beam at larger z to counter-act this effect?
Answer: diffusion dominates, so it doesn’t really make a big difference where we focus, *in terms of ionization profile*. Looks like black dashed curve (w/ beam focused mid-way) gives the best overall results (see next slide for direct comparison).
Gas: Ne-CF4 (50/50)
D_T = 40mm/sq(cm) @ 1.4T
W(z) ~1/e2 ~2s
~ (W(z)/2)/
Ion. Yield Ratio
~ w02/w(z)2
Case study for properties along ~130cm track at ~35o

## Slide 31: Ionization Yield Consideration
Seems like w0(z=65) is probably the best compromise: better avg. rel. res. along the beam (right plot) and a smaller IY ratio (~2 compared to ~5; see gold curves on prev. slide). So, we’ve come full circle, but hopefully we now feel better about it 
Because we are so dominated by diffusion and w0(z=65) is a bit of a sweet spot, looks like a variable zoom lens isn’t worth considering
Though the spatial profile of the collected charge cannot be changed much, we do have a strong handle on the ionization yield profile along the beam
The ionization yield directly impacts the contribution to the resolution via Neff: s2drift = D2TL/Neff
Focus beam close to membrane (counteract D_T)
Small gains, moderate losses
Focus beam in nominal TPC center (optimize for ~avg. pathlength)
Best overall res. along beam, smallest IY ratio
Focus beam near endcap (concentrate our efforts where they are most effective)
Small gains, larger losses
Neff along track ~ Ion. Yield (IY) profile
Case study for properties along ~130cm track at ~35o
(Assume pads collect charge uniformly along track, ie, Neff dictated by IY profile alone)
Results are similar due to diffusion, but w0(z=65cm) looks like best overall candidate

## Slide 32: Pad Planes
R3 “First Article” Samples delivered to SBU Friday.
Likely to us on Tuesday ~mid day.
Inspections:
  Microscope for quality of pad shapes.
  Mechanical fit to strongback.
R2 pad plane under final cross-checks:
  Electrical/design rules: Hemmick
  Mechanical (aligns with cooling etc…): Cacace
  Update Fab. Notes ala R3 Engineering Questions
  Likely send out this week.

## Slide 33: AC/DC Review
Review of AC and DC power distribution.
  DC for FEE (Takao for Ivan, John, Connor, Eric, Steve)
  Power for TPC Laser Systems (Bob Azmoun)
  HV for field cage and GEMs (Klaus, next slide).
Ivan & Takao

## Slide 34: HV Power Supplies/Crates
Central Membrane HV supply ordered weeks ago.
  Standalone rack-mounted 60 kV power supply.
  Operating voltage ~45 kV (“Administrative Limit”);
GEM HV Power Supply Requisition placed
  Quotation matches BOE very well.
6 kV/1mA power supplies
  >5kV operation in test beam.
  Removed “double-thick” frame at bottom GEM (now single thick)
  Same voltage configuration = below 4600 operating voltage
  Uses “special” SVH connector:
    Mechanically the same as ordinary SHV.
    Rated for 8 kV.
  Wish to order these connectors through Weiner as separate order.
    Easiest to defend with Safety Committee that we got the right thing…

## Slide 35: Laser Bench Converging on Final Scheme

## Slide 36: Things To Consider
The pictured Attenuator is different than the provided dimensions.
  The connector for the Beam Energy Monitor is displayed on opposite sides, and the possible orientation of the provided dimensions does not match that of the picture.
  We should verify with QLI that our Attenuator does indeed fit the laser. Should not effect design so long as the 42.5 mm thickness does not change.

## Slide 37: Things To Consider
Where exactly do we put the beam intensity/timing pickoff?
  Laser exit.
    Made to mount.
    Pushes back laser a bit.
    Disturbs “elegance”.
  Former Beam Shaper Location
    Puts laser into ~ideal mechanical spot.
    We have to mount it ourselves.

## Slide 38: Laser Error Propagation
  Finite Precision of Piezo motors propagates to final laser direction.
  Trace Pro Model allows for understanding how these errors accumulate on final laser direction.
  Updates coming to put BS optics after the dog leg.
Bore sight lasers are precision aligned.
On Order