## Slide 1: Mechanical Structure for FST
20 July 2020 @ F2F meeting
Han-Sheng Li, Pu-Kai Wang, Yi Yang
Chung-De Chen, Pei-Chia Chung,
Bing-Teng Hong, Tsai-Hsuan Hsieh,
Jian-Yu Wang, Tian-Shiang Yang
Tang-Shiang Chang, Ming-Tang Dong,
Yuan-Ruey Chuang, Yean Ho Liao
Department of Physics, NCKU
Department of Mechanical Engineering,
NCKU
Aerospace Industrial Development Corporation

## Slide 2: Presentations/Document
Document:
  Version 2: https://www.dropbox.com/s/cndffu9ybv8zkyu/Mechanical_Structure_for_FST_at_STAR_v2.pdf?dl=0
F2F Meetings:
  2020-02-28: https://www.dropbox.com/s/xaszsze9q5es1g7/20200228_FST_Mechanical_YiYang.pdf?dl=0
  2019-08-08: https://www.dropbox.com/s/8a5o85qvgy8haof/20190808_FST_Mechanical_YiYang.pdf?dl=0
  2019-03-30: https://www.dropbox.com/s/43aiy53zandld9q/20190331_FST_status_YiYang.pdf?dl=0

## Slide 3: The Forward Silicon Tracker
Silicon sensor: UIC/SDU/NCKU
Flexible hybrid PCB: SDU/IU
APV25 Chip: UIC
T-Board: SDU/IU
Mechanical Structure
(+ cooling pipe): NCKU/AIDC
Supporting Structure &
Integration: BNL
Inner Signal Cable: BNL
Simulation: UIC/BNL/IISER/NCKU
Cooling: BNL/NCKU

## Slide 4: The Final Design
Main structure:
Material: PEEK
Thermal Conductivity: 0.24 W/m/K
Heat sink:
Material: Al 6061
Size: ~8.2 x 8.0 x 3 mm2
Tube:
Material: Stainless 316 (with Chroming)
Size: OD 6.35 mm, ID 5.54 mm
Thermal Conductivity: 14 W/m/K
Tube fixture:
Material: PEEK

## Slide 5: First Prototypes: FST-001, FST-002
Two prototypes assembled by AIDC on Jan. 30 and Feb. 11, 2020
Many issues found: flatness, bubbles, shifting…
Thicker hybrid
(new vender)
Thinner hybrid
(older vender)
Flatness (RMS) | Thicker hybrid | Thinner hybrid
Inner | 0.2942 (mm) | 0.2663 (mm)
Outer | 0.4654 (mm) | 0.2585 (mm)
~2-3 mm

## Slide 6: New Assembly Procedure
To improve the precision of the assembly, we are using the robotic machine at TiDC (https://www.taiwan-tidc.org) to mount hybrid PCBs to inner and outer structures
 More precise positioning
 New fixtures and LabView codes are ready
Optical Gauging Products (OGP)
Assembly table and gantry
STAR FST
sPHENIX INTT
CMS HGCal

## Slide 7: Connector & Components on Hybrid
FST-001 & FST-002: connector and components were mounted before assembly
New procedure (FST-003, FST-004):
  Connector were mounted by outsourcing company
  Perform plugging-unplugging test
  Perform open connection test
  (Assembly hybrid + mechanical structure)
  Solder components manually
  Perform electrical test

## Slide 8: New Assembly Procedure: Outer
Place the pickup tool, outer MS + tray, outer Hybrid + tray on table
Place guide pin on outer MS
Apply glue on outer Hybrid
Use camera to locate the reference points
Glue
pickup tool
Outer MS + tray
Outer Hybrid + tray

## Slide 9: New Assembly Procedure: Inner
Need to pre-fit and calculate the correct positions due to the shrinking of the MS (will be fixed)
Place the outer MS+Hybrid+Cooling tube (outer wedge) + tray and inner MS + tray on table
Located the reference points
Use robotic arm to place the inner MS on the outer wedge
Record the positions and calculate the shifting
Outer wedge + tray
Inner MS + tray

## Slide 10: New Assembly Procedure: Inner
Place pickup tool, inner MS + tray, inner Hybrid + tray on table
Use camera to locate the reference points
Pick up inner MS and glue it on the inner Hybrid
Inner Hybrid + tray

## Slide 11: New Assembly Procedure: Outer+Inner
Place pickup tool, inner wedge + tray, outer wedge + tray on table
Use camera to locate reference points
Pick up inner wedge and glue

## Slide 12: New Assembly Procedure: Video

## Slide 13: Second Prototypes: FST-003, FST-004
FST-003
FST-004
Look good by eyes!

## Slide 14: Second Prototypes: FST-003, FST-004
"The inner chip placement was off .500 mm so I needed to reposition. The outer placement was off .200 mm”
(slightly larger misalignment for FST-004)
"They were inboard toward the sensor area . I needed to slide the chips back or outward. Michelle mention adhesion under some pads was not so good and created some issue but she got all in adjusting the powers.”
(Only for FST-003)
(1) Mainly due to the guide pin and this will be fixed after using the recommendation from Rahul’s team
(2) Will improve the glue pattern
(See next slides)

## Slide 15: Issue on Thicker Hybrid (new vender)
The conducting lines are too thick: 48 mm vs. 24 mm
 Difficult to be fixed on the vacuum tray
 Need to use the thinner one for production
Thicker
Thinner

## Slide 16: Modified Gluing Pattern
Old
New
Add extra glue
underneath the
bonding pads

## Slide 17: Modified Mechanical Structure
Implemented the suggestions from Rahul’s team
  Precision bushings and pins (inner holes), larger through holes (outer holes)
  Add inner supporting part (screw hole)
Precision bushing

## Slide 18: Bushing and Pin
Precision bushings and pins will be customizely made in Taiwan
  Bushing: MOQ: 500 pcs, ~15 USD/pc
  Pin: MOQ: 500 pcs, ~4 USD/pc
  Total: ~9,500 USD
Tolerance: H7
Tolerance: H7

## Slide 19: Modified Gluing Procedure for Inner Hybrid
Glue the inner MS first
Place pickup tool, inner MS + tray, outer wedge + tray on table
Use camera to locate reference points
Pick up inner MS and glue it on the outer wedge
* Manufacturing new fixtures now

## Slide 20: Modified Gluing Procedure for Inner Hybrid
Follow the “same” procedure as the outer Hybrid
Place pickup tool, inner Hybrid + tray, outer wedge + inner MS + tray on table
Use camera to locate the reference points
Pick up inner Hybrid and glue it on the inner MS

## Slide 21: Soft Tube Compatibility Tests
Tygon C-544-A I.B.
Tygon 3370 I.B.
Use the Soxhlet extraction method (suggested by 3M)

## Slide 22: Soft Tube Radiation Tests
Use Co60 source at Institute of Nuclear Energy Research (INER)
Cost: ~150 USD/test
Two dosages:
  3.2 kGy (from proposal)
  16 kGy (5 times higher)
Tygon C-544-A I.B.
Tygon 3370 I.B.

## Slide 23: Plan for the Measurements
Plan to outsource (Taiwan CK Techno Co.,Ltd.) the measurements of flatness and parallelism
Extremely expensive:
  Flatness for single inner or outer MS (before assembly):
    Price: ~200 USD/pc
    Method: optical
  Flatness and parallelism for assembled module:
    Price: ~400 USD/pc
    Method: mechanical (their know-how)
  Total of 60 sets: 48,000 USD Working on getting a better deal
Plan for the prototypes:
  Flatness for single inner or outer MS (before assembly) at TiDC
  Flatness and parallelism for assembled module (first 10) by CK Techno

## Slide 24: Schedule for Production
Estimated production times:
  One week for preparation
  One module per day
  70 working days for 60 modules
Current Schedule:
  Aug. 12, 2020: place orders
  Sept. 14, 2020: preparation
  Sept. 21, 2020: start production
  Dec. 24, 2020: finish production
  Dec. 31, 2020: ship to UIC

## Slide 25: Backup