## Slide 1: FTT Module design, production and test
Qian Yang/ Yingying Shi
Shandong University

## Slide 2: Outline
Full Size Prototype
  Full size prototype design and production procedure
  Full size prototype performance test
Pentagon Prototype
  Pentagon prototype design and production status
Summary

## Slide 3
Full size prototype design, production and performance test

## Slide 4: Full size prototype design
FEE
Station
Endcap view for the whole layer
60cm*60cm active area

## Slide 5: Full size prototype design : station structure
Strip plate ( FR4 + Copper strip + Graphite)
Anode wire plate ( 50 gold-plated tungsten wire)
Cathode (copper pad )
Honeycomb plate (60cm*60cm)
FEE slot
Chamber1
Chamber2

## Slide 6
Full size prototype production : chamber production
1⃣️
2⃣️
3⃣️
4⃣️
5⃣️
6⃣️
PCB inspection
Spray graphite: Graphite : Plastik-70 = 3:1
Tape support strip area
Polish graphite to
Support strip installation
Buckle installation

## Slide 7
Full size prototype production : chamber production
Anode:
50μm gold-plated tungsten wire
340 wires with a pitch of 1.8mm and a tension of 350g
The resistance is 10MΩ
high-voltage 3100v
Monitoring anode wire current <100nA is qualified
8⃣️ HV scan
7⃣️ Wire winding

## Slide 8
Full size prototype production : chamber production
The chamber is under a force of 40 kilograms, which is about 11g/cm2
Follow with CO2 for about six hours
🔟 Synthesize
9⃣️ Gluing

## Slide 9
Station production
1⃣️
2⃣️
3⃣️
Install support strip
Gluing
Add honeycomb board
4⃣️ Synthesize

## Slide 10
Test System
Readout area: 22*10cm2
Gas: 45%n-Pentane + 55%CO2
HV: 2700V

## Slide 11: Detector performance
X-ray scan
Detector efficiencies at the level of 98%
Long time leakage current tracking
Position distribution w/o alignment

## Slide 12: Detector shipping
Full size prototype has been shipped to BNL in June

## Slide 13
Pentagon prototype design and production status

## Slide 14
Pentagon prototype design
Endcap view for the whole layer
Station
x

## Slide 15: sTGC geometry
sTGC layout-side-view
Anode wire
1.4mm
1.4mm
Anode: 50 gold-plated tungsten wire, wire pitch 1.8mm, the wire tension 350g;
Cathode: graphite epoxy mixture
Readout: copper strips (0 and 45 ); 0 strips are perpendicular to anode wires; 45 strips for ghost hits rejection
Cathode
Cathode
x

## Slide 16: Tooling for pentagon sTGC production
Location-frame for graphite edge
Location-frame for graphite edge
Vacuum tool on marble table

## Slide 17
New gas system
Control Evaporation Mixing

## Slide 18
PCB inspection
10 sets of PCBs
PCB thickness and flatness inspection
  All qualified
Connectivity check
  One PCB needs replacement
Cleaning support frame and painting Luka on it

## Slide 19
Pentagon production readiness
PCB thickness and flatness check √
Connectivity check √
Painting Luka on support frame √
Graphite spraying (this week )
Wire winding machine √
Gas system √

## Slide 20
sTGC production schedule
design
Vender production
Prototype production
Final design
Vender production
Mass production
Jul. to Sep.
Aug. to Oct.
Sep. to Nov.
Oct. to Jul. 2021

## Slide 21: Summary
Full Size Prototype
The full size prototype has been produced and detector shows good performance
Prototype has been shipped to BNL
Pentagon Prototype
The pentagon prototype design has set down.
Tools and new gas system has been developed
PCB inspection has done
sTGC production is on going