## Slide 1: Electronics Status at USTC
Feng Li, Shuang Zhou, Peng Miao, Ge Jin
July 21st, 2020
University of Science and Technology of China

## Slide 2: Outline
System Architecture
FEB Status
VMM3 Usage on FEB
ROD Status
Adapter Board design

## Slide 3: System Architecture

## Slide 4: Complete sTGC layer
The strips of each sTGC layer can be handled by 24 Front-End Boards.
In total, there will need 96 FEBs for 4 sTGC layers.
The innermost sTGC layer locate in the cone at the place with diameter of 152cm
About 10cm gap between the sTGC border and the cone
FEB boards are vertically inserted in the sTGC chamber.

## Slide 7: Layout in the cone
7-inch distance between adjacent sTGC chambers.
FEBs are vertically inserted into the connector slots on chamber.
FEBs are almost parallel to the particle beams.
3-6 power cables can be grouped together and then distributed to each FEB near the chamber.
Notes: FEB is almost parallel to the particle beams, which can help reduce the radiation on electronic chips.

## Slide 8: Connector between chamber and FEB
Connector P/N on chamber: SAMTEC HSEC1-060-01-S-DV-A-K, used as board slot connector
Connector size on chamber: 69.5 * 5.6 * 7.8mm (L*W*H)
1.0mm pitch, dual rows, 60 positions/row
120 strip signals can be connected to the connector
Surface-mounted, can be soldered manually.
No connectors needed on FEB: Golden fingers on both layers of FEB
Each FEB contains two connectors, capable of up 240 strip channels (sTGC chamber can supply ~210 strips for each FEB).

## Slide 9: Connector Pin Map
120 positions:14 for signal Ground(marked with ‘G’), 106 for strips.
Footprint on chamber
Golden fingers on FEB

## Slide 10: Read-out Electronics Architecture
96 Front-End Boards
16 Read Out Driver Module
ROD modules are designed based on Standard VME 6U Crate(with DC power supply)

## Slide 11: FEB Status

## Slide 12: 3D show of FEB

## Slide 13
FEB is shown on the right.
Test the performance of the GTX link .
The VMM configuration and readout.
Check the power supply of the FEB.
FEB weight:
  shown<70g
  cooling pad and cages（power） < 20g
  data cable and power cable < 15g
  ……
FEB weight < 110g

## Slide 14
Test the performance of the GTX link at 4 Gbps by Xilinx IBERT core.
The left picture shows the test platform, and the results are shown below.
Test the GTX link with different length of the mini-SAS cable (0.5m, 1m, 2m, 3m), and the GTX link works steadily at all length.
Power: 10V, 0.8A (4 VMMs configured and readout, GTX activated).

## Slide 15
Completed work:
VMM configuration and readout. We can configure VMM in right mode, and readout the events data of test pulses from VMM.
Reformat events data. Add Cyclic Redundancy Check in each data packet, and scramble the data stream before transmitting.
Transmit data packets at 4 Gbps by GTX.
Slow data links(40Mbps) tests. Slow data links between FEB and ROD, include the clock signal, the trigger signal, and the commands.

## Slide 16
Next to do:
Test VMM readout with the external test pulse.
Monitor the temperature sensor of VMM.
Power connector and Data connector will be replaced by vertical types in the next version of FEB.

## Slide 17: VMM3 usage on FEB
configuration and readout

## Slide 18: Architecture of VMM3

## Slide 19: VMM3 configuration
Global register: 192 bits
  Charge polarity
  Gain(0.5,1,3,4.5,6,9,12,16mV/fC)
  Peaking Time(200,100,50,25ns)
  Coarse threshold DAC
  Test Pulse DAC
  ……

## Slide 20: VMM3 configuration
Channel register: 24 bits/CH
  Threshold trimming
  Internal test pulse
  ……
VMM Configuration Process:
  192 + 24 * 64 = 1728 bits
  configure VMM through SPI.
  Each VMM can be configured individually.
  18*96-bits: 2*96-bits for global registers, 16*96-bits for channel registers.

## Slide 21: VMM3 configuration GUI
Used for ATLAS FEB mass inspection
Can be transplanted to be used for STAR FEB test before shipment.

## Slide 22
VMM Mode: Non-ATLAS Continuous Mode.
VMM Data Format:
Each event data is 38 bits, contains 1 bit flag, 1 bit threshold, 6 bits channel ID, 10 bits PDO, 8 bits TDO, and 12 bits BCID.

## Slide 23: ROD Status

## Slide 24: ROD Architecture
6 DATA connectors compatible with 6 FEBs
Xilinx Kintex-7 FPGA: XC7K325T-2FFG900I
FEAST power modules
2 optical fiber SFP+ to communicate with STAR DAQ (1 for spare)
ROD size:233*100mm
TCD circuit for STAR DAQ connection.
USB3.0 connector added for communication with PC(not necessary for STAR).

## Slide 26
LVPECL(from cable)  LVTTL  FPGA
120-ohm resistors kept but only one board needs to solder them
Busy signal from FPGA will return to TCD board.
TCD circuit

## Slide 27: POWER
4 FEAST ASICs used:
  Digital 3.3V: SFP+ Powering, SPI Flash, TCD, GPIO
    DDR_1.5V(LDO): DDR powering
      0.75V(LDO):DDR reference voltage
  Digital 1.0V: FPGA core voltage and MGT_AVCC
  Digital 1.2V: MGT_AVTT
  Digital 1.8V: FEB links

## Slide 28: Board Status
ROD boards will be back early August. Then 1-2 weeks for soldering.
Firmware development ongoing:
  Decode data packet; Descramble; CRC
  10G SFP+ code transplanting;
  DDR3 code development

## Slide 29: Adapter between FEB and Simulator Board

## Slide 30: STGC Signal Simulator board
256 channels charge output, ~0.4pC
Used as external test pulse source for FEB

## Slide 31: Adapter board design

## Slide 32: Connection

## Slide 33: Thanks!