## Slide 1: Study of Particle Detector by Simulation - The DTOF in STCF Experiment
Ming Shao
University of Science and Technology of China
State Key Laboratory of Particle Detection and Electronics
湖州暑期讲习班
7月10-23日，湖州师范学院

## Slide 2: Outline
Detector system in particle and nuclear physics: Simulation vs. experiment
The DTOF detector in STCF experiment
  Motivation
  Conceptual design
  Key parameters in study
  Performance expectation
Summary

## Slide 3
detector
Instruments to ‘see’ objects
Tools vs. Objects of Study in Research

## Slide 4: Detector System in High-Energy Physics Program
To measure the momentum, energy and type of final state particles in particle or nuclear collisions, by recording the spatial, time and energy information leaved in the detector system.
ALICE

## Slide 5: Simulation vs. Experiment
Importance of simulation in high-energy physics experiment
  Physics simulation (benchmark channels)
  Design and Optimization of the Detector system
  Accelerator and detector physics
Physics (data) analysis
  Control of systematic errors
  Theoretical (model, event generator etc.)
  Experimental (detector, reconstruction etc.)
Physics Analysis
Experiment
Simulation
Theory

## Slide 6: What Is Super Tau-Charm Facility (STCF)
Collision energy: 2-7 GeV
Luminosity: 1.0×1035 cm-2 s-1
Circumfluence: 600~800 m
Detector
RF cavity
LINAC: ~300 m
Current Beijing Electron-Positron Collider (BEPCII)：
Collision energy: 2-4.6 GeV
Luminosity: 1.0×1033 cm-2 s-1
Circumfluence: ~240 m

## Slide 7: STCF Experiment
Main Tracker
Inner Tracker
Barrel PID
Endcap PID
Electro-magnetic Calorimeter
Super-conducting Magnet (1T)
York/Muon Detector
IP
3~6 cm
10 cm
15 cm
85 cm
105 cm
135 cm
185 cm
245 cm
120 cm
140 cm
190 cm
240 cm
300 cm
20
Main Tracker
xy<~130 um
p/p ~ 0.5% @ 1 GeV
dE/dx~6%
Inner Tracker
~0.15%X0 / layer
xy~50-100 um
PID
/K (K/p) 3-4 separation
Momentum 2GeV/c
EMC
Energy range: 0.02-3GeV
Resolution E (%)@1GeV
barrel: 2.5%
endcap: 4%
MUD
Low momentum ~0.5GeV
 suppression >30
York/Muon Detector

## Slide 8: PID Requirements
Particle Identification (PID) of charged particles： /K (K/p) 3-4 separation, up to p= 2GeV/c

## Slide 9: PID Technology for Charged Hadron
Nucl. Instr. & Meth. A 666 (2012), 148-172
Options for STCF PID:
RICH (barrel),
DIRC or DIRC-like (endcap)
Q1：dE/dx, TOF, measurement alone is not sufficient for particle type distinguishing, what, and how many, other parameters are needed to do PID?

## Slide 10: Cherenkov Radiation
Cherenkov radiation angle

## Slide 11: Cherenkov Detector Performance
B. N. Ratcliff, NIMA 502 (2003) 211-221
for particles well above threshold
C6F14 (liquid)
C4F10
Aerogel (1.04)
Fused Silica
0.5 mrad
1 mrad
Particle momentum (GeV/c)
Ns p/K separation
3 s
CF4

## Slide 12: RICH – Ring Imaging Cherenkov Detector
CF4 gas
300 mrad
120 mrad
Flat mirrors
Spherical mirrors
~7 m
RICH at LHCb
RICH at SLD, DELPHI, 1994
RICH has been widely applied in high-energy physics or astrophysics experiments since 1990’s, providing PID over large kinematic coverage

## Slide 13: DIRC – Detection of Internal Reflected Cherenkov Light
Started operation in 1999
p/K separation: 3s at 4 GeV/c
Single photon timing resolution: 1.7 ns
B.N. Ratcliff, SLAC-PUB-6047 (Jan. 1993);
P. Coyle et al., NIM A343 (1994) 292
DIRC at Babar

## Slide 14: Development of DIRC Technique
DIRC structure is very compact and robust, yet with excellent PID capability (3 /K separation up to 4-6 GeV/c)
Belle2-TOP
DIRC@PANDA
DIRC@EIC

## Slide 15
DIRC-like detector, first proposed for superB forward PID
Use time information, rather than Cherenkov angle , to identify particle
Very accurate timing property to achieve 3D (x, y, t) measurement, usually employing multi-anode MCP-PMT
Very compact and simple structure, highly robust and radiation resistive
Challenges：
  for single photon
  Very fine polished quartz surface（Ra<1nm）
DIRC-like Timing Detector
Baseline technology for STCF endcap PID detector
Overall time resolution <30ps
FTOF at superB:
Forward Time-of-Flight
TOF detector considered for LHCb Upgrade II
PID in 2-10 GeV/c momentum range
Single photon st ~ 70 ps, single track st ~ 15 ps
TORCH at LHCb

## Slide 16: DIRC-like Detector Timing Error Sources
: Number of photo-electrons
: error from tracking（~20 ps for 0.8 GeV/c kaon)
: error from collision（~40ps for STCF, bunch crossing）
: error from electronics (~15ps for STCF)
: transit time spread (TTS) of MCP-PMT
: error from DIRC detector (dispersion, position, reconstruction etc.)

## Slide 17: A Simple Example
Incident particle along Z generates a Cherenkov light cone at (0,0,0):
At imaging plane y=C，Cherenkov light curve is
The time of propagation (TOP) of Cherenkov light
  =
The time of Cherenkov light emission (particle hitting radiator)
  ，
Z
Y
error comes from (mainly and ), (dispersion), (position), and (particle velocity)
For simplicity, by ignoring the difference between and )
  

## Slide 18: A Simple Example (cnt.)
With a sensitive wavelength range (300-600nm)，
  ~ (n@300nm-n@600nm)/4 ~ 0.0075
, where for STCF
includes the thickness of Cherenkov radiator (~2cm), and the size of photon sensor (~0.6cm), combining to

## Slide 19: Result
We take
  and
  for kaon
Other effects, such as surface roughness and multiple Coulomb scattering (MCS), are not included
Timing error from detector (reconstruction) is discussed in the following slides

## Slide 20: Reconstruction of Cherenkov Light Cone
Measurement  Cherenkov parameter
The correlation between and is “confused” by limited resolution and structure of the detector
Multiple possibilities between and may cause uncertainties in TOP reconstruction, which is mainly from unsureness of the length of propagation (LOP)
Unfold
BELLE-II TOP
PANDA barrel DIRC

## Slide 21: Reconstruction of Cherenkov Light Cone (cnt.)
Unfold
Suppress “confusion” in reconstruction  improved timing
  Proper radiator size
  Excellent position and time resolution  3D reconstruction
  Proper optics (focusing)
  Proper reconstruction algorithm
Unfold
Q2：The first DIRC at Babar made use of quartz bars of small cross-section, why didn’t it suffer from “confusion” in reconstruction?

## Slide 22: STCF-DTOF Design and Modelling in Geant4
MCP-PMT
Z = (1400 mm - 1600 mm)
R = 560 mm – 1050 mm
18×3×4(sectors)×2(endcaps)=672 MCP-PMTs
MCP-PMT:
  27.5mm*27.5mm*16.6mm
  4*4 multi-anode
  pixel size: 5.5mm*5.5mm
DTOF: DIRC-like Time-of-Flight
FTOF at superB
DTOF v1
DTOF v2

## Slide 23: Simulation Parameter Setting
Reflection coefficient of mirror
=1 – absorption coefficient
dielectric-metal = reflection ratio
dielectric-dielectric = reflection + refraction ratio
Reflection coefficient between air and fused silica
Absorption length
Refractive index
Left
Right
Bottom
Top
Back
Front
Back
Wrapping set:
  Top and Bottom are absorbed
  Left and Right are reflected (Average Ref Index: ~92%)
  Front and Back have no wrapping.
Radiator surface set:
  Surface roughtness:
MCP-PMT set:
  Quantum efficiency taken from Hamamatsu R10754
Optical parameters of fused silica

## Slide 24: Simulated DTOF Hit Pattern

## Slide 25: Simulated DTOF Performance
K/pi separation ()
Total time resolution :
Separation power =

## Slide 26: Expected PID with Different DTOF Time Resolution
The direction of track can affect both the number of photons and time resolution
The momentum of track only affects time resolution
Total time resolution always below 50 ps.
K/pi separation better than 3 sigma.

## Slide 27: Reconstruction Algorithm
Y
Z
T
H
X
Y

## Slide 28: Reconstruction Algorithm (cnt.)
，，
Solve:
  ，
Total reflection criteria:
X
Y
Z
x

## Slide 29: Reconstructed LOP

## Slide 30: Reconstructed TOF

## Slide 31: Another Incident Position

## Slide 32: TOF Distribution of π/K

## Slide 33: π/K separation
peak2 and peak3：3.0σ
peak1 and peak3：4.1σ
peak2 and peak4：4.0σ
Q3： Why does the mean TOF with wrong hypothesis shift beneficially as in the figure, and what’s the relationship among peak 1 - 4?
1
2
3
4

## Slide 34: π/K separation
Likelihood method

## Slide 35: π/K separation
In larger phase space
p = 2 GeV/c

## Slide 36: K/p separation

## Slide 37: π/e and π/μ separation
π/e
π/μ

## Slide 38: Background at STCF
1RBB electron
2RBB photon
3Two photon
4Touschek
5Coloumbscattering
6Brems
7Total
Dedicated background study in the framework of STCF software
Detailed simulation of machine and MDI design, background generation and beam transport

## Slide 39: Time Structure of Background
gamma
electron

## Slide 40: Time Structure of Background (cnt.)
= 0, 8, 16.. ns
= Uniform (-50ps, 50ps)
, time of flight
DTOF all sectors

## Slide 41: DTOF Background Simulation
  Background hit number sampled by Poisson distribution, mean hits from STCF background simulation
  Particle parameters directly sampled from STCF background simulation, including particle type, position, momentum/energy
  Hit time sampled by Uniform distribution

## Slide 42: DTOF Simulation with Background
θ=24, φ=45, p=2GeV, pion
Assume PMT gain~106，10 years’ operation （50% duty time）
Background，12p.e. in 100ns  12C/cm2 accumulated anode charge
Signal，22p.e.@400K  0.8C/cm2 accumulated anode charge

## Slide 43: Likelihood Method with Background
Contribution from Npe is included in the likelihood
TOF distribution, gaussian fit
Np.e. distribution (bkg), crystalball fit
Np.e. distribution (signal+bkg), crystalball fit

## Slide 44: π/K Separation with Background
Without background，4.30 σ
With background，4.27 σ
With 3-time background，4.26 σ
Conclusion: PID capability not affected by background hits
No background
Simulated background
Simulated background*3

## Slide 45: DTOF PID with Background
Bz = 1 T

## Slide 46: Optimization of DTOF Shape
Design-A
4 sectors per disc
18×3 MCP-PMTs per sector
Design-B
12 sectors per disc
18 MCP-PMTs per sector
Design-C
24 sectors per disc
8 MCP-PMTs per sector

## Slide 47: DTOF Design with Mirror
Design-α
No mirror, absorber
Design-β
Mirror on top surface
Design-γ
Mirror with 45°chamfer

## Slide 48: Comparison – Different Shape
Aα15
Bα15
Cα15
θ=24°, φ=45°, p=2GeV, pion

## Slide 49: Comparison – Different Shape (cnt.)
Aα15
Bα15
Cα15

## Slide 50: Comparison – Different Shape (Summary)
Different design | Aα15 | Bα15 | Cα15
Sector number | 4 | 12 | 24
Sector angle | 90° | 30° | 15°
MCP-PMTs (per sector) | 18×3 | 18 | 8
Anode charge density | 11 C/cm2 | 12 C/cm2 | 13 C/cm2
Signal number of p.e. (θ=24°, φ=45°, p=2GeV, pion) | 22 | 22 | 17
φ=45°, p=2GeV/c |  | θ=24° | θ=27° | θ=30° | θ=33°
π/K PID | Aα15 | 4.29σ | 4.34σ | 4.30σ | 4.24σ
 | Bα15 | 4.20σ | 4.20σ | 4.23σ | 4.14σ
 | Cα15 | 3.77σ | 4.03σ | 4.16σ | 4.10σ

## Slide 51: Comparison – Different Thickness
Aα15
Aα10
Aα20
θ=24°, φ=45°, p=2GeV, pion

## Slide 52: Comparison – Different Thickness (cnt.)
Aα15
Aα10
Aα20

## Slide 53: Comparison – Different Thickness (Summary)
Different design | Aα10 | Aα15 | Aα20
Quartz theckness | 10mm | 15mm | 20mm
Anode charge density | 9 C/cm2 | 11 C/cm2 | 12 C/cm2
θ=24°, φ=45°, p=2GeV |  |  | 
Signal number of p.e. (pion) | 15 | 22 | 26
π/K PID | 4.03σ | 4.29σ | 4.36σ

## Slide 54: Comparison – Mirror
θ=24°, φ=45°, p=2GeV, pion
Aβ15
Aα15
Aγ15

## Slide 55: Comparison – Mirror (cnt.)
Aβ15
Aα15
Aγ15

## Slide 56: Comparison – Mirror (Summary)
Different design | Aα15 | Aβ15 | Aγ15
Mirror design | No mirror | 90° mirror | 45° mirror
Anode charge density | 11 C/cm2 | 17 C/cm2 | 22 C/cm2
θ=24°, φ=45°, p=2GeV |  |  | 
Signal number of p.e. (pion) | 22 | 33 | 39
π/K PID | 4.29σ | 4.32σ | 4.27σ
Q4： Why does the DTOF PID change little, even with much more Npe when including mirrors in the design?

## Slide 57: Optimization of DTOF Geometry
Thickness of radiator
Shape of radiator
Including of mirror
Configuration/Geometry ID | 0 | 1 | 2 | 3 | 4 | 5 | 6
Radiator shapes (sector number) | 4 | 12 | 24 | 4 | 4 | 4 | 4
Radiator thickness (mm) | 15 | 15 | 15 | 10 | 20 | 15 | 15
Outer side surface | A | A | A | A | A | M | 45° M
Inner side surface | A | A | A | A | A | A | A
Lateral side surface | M | M | M | M | M | M | M
Number of photoelectron for pions (except background) | 21.8 | 21.9 | 17.0 | 15.5 | 25.7 | 33.2 | 38.7
Accumulated charge density on MCP-PMT anode (C/cm2) | 10.8 | 10.5 | 9.6 | 8.8 | 11.8 | 17.0 | 25.6
π/K separation power | 4.17σ | 4.08σ | 3.66σ | 3.99σ | 4.27σ | 4.26σ | 4.19σ
Performance of DTOF with different configurations
Optimized DTOF structure

## Slide 58: Further Improvement?
Include position information in the likelihood
pion
kaon
pion
kaon

## Slide 59: PID Capability with All Info. From DTOF
x, t, Npe
t, Npe
/K separation
Timing method
Imaging method

## Slide 60: Summary
We illustrate the design of the DTOF detector for the future STCF program. The simulation tool are extensively used to study various aspects of the DTOF:
  Key factors influencing the time resolution
  Detector geometry and optimization
  Background effect
  PID algorithm and expected performance
  And many more not introduced here …
Thank you !
References: A DIRC-like time-of-flight detector for the experiment at the Super Tau-Charm Facility, https://arxiv.org//abs/2104.05297; STCF Detector Conceptual Design Report, to be released soon.

## Slide 61
BACKUP SLIDES

## Slide 62: Beckmann-Spizzichino Reflection
能量反射公式：
  为纯镜面反射场强
  光波长，波数，入射角，出射角，表面粗糙度（h为表面轮廓高度），关联长度，照射（矩形）表面积
  （从空气到介质）
  或（从介质到空气）
GEANT4 Optics
Specular spike
Specular lobe

## Slide 63: B-S Reflection (cnt.)
表面非常光滑时，能量反射由，、
其中代表光强的衰减，为降低多次内表面反射导致的光衰减，要求尽可能小
代表反射光的角发散，，其中，，且，因此，已假设，（d为石英厚度）
分布非常窄，可近似为函数
但sinc函数方差不收敛小概率出现大角散射

## Slide 64: Rayleigh scattering
For Rayleigh scattering (elastic scattering), the transmissivity T of a path of length L at wavelength  is:
，其中是波长处的吸收长度
根据Babar的测量，@
对于数米长度的石英，因瑞利散射损失的光强~5%（对比：因表面粗糙度损失的光强~5-10%（，200次反射）或~30% （，200次反射） ）

## Slide 65: Multiple Coulomb Scattering (MCS)
The incident charged particle suffers from MCS effect when passing the fused silica plate (~1cm), its velocity direction changes continuously – correspondingly the Cherenkov light emission direction also changes, following a Gaussian distribution with the standard deviation () as
，其中为辐射长度（对于熔融石英，该值为12.3cm）
对低动量粒子影响较显著

## Slide 66: 聚焦型DIRC探测器
15 mm厚度石英板切伦科夫辐射体
光学聚焦设计：thickness=87mm，R=300mm
聚焦覆盖范围：12°-48°
DIRC有效覆盖区间：θ=21°-35°
DIRC死区范围：θ=35°-38°

## Slide 67: 模拟创建结果
σ = 2.9 mrad
σ = 6 mrad
σ = 4.2 mm
σ = 33 ps
θ = 24°，φ = 0°, p = 2GeV/c

## Slide 68: 粒子鉴别能力
For Np.e. = 32

## Slide 69: Wider Momentum Range
利用切伦科夫角，可以实现p = 5 GeV下 3 σ 的π/K分辨能力
θ = 24°，φ = 0°
For Np.e. = 32