## Slide 1: The CERN Neutrino Platform
20th October2014
Marzio Nessi, CERN & University of Geneva

## Slide 2
CERN Neutrino Platform
CERN Neutrino Platform
Neutrino detectors R&D :
prototypes, components, final assemblies
Logistics +
Test Beams Infrastructure (EHN1 ext)
Design and eventually implement a Neutrino Beam
EU participation in a High Intensity Facility & SBL
(detectors, beam, infrastr.)
PHYSICS (Short and Long Baselines)
Investigate new programs (mu storage ring, betabeams ?, …)

## Slide 3: Projects presently under consideration
WA104 ICARUS detector overhauling
WA105 construction and test of 2 large prototypes/demonstrators
WA104 NESSiE R&D and test of a new generation of muon spectrometers
Baby MIND : demonstrator and test of a new muon tracking detector (LBNO, ND-HKK?)
LBNF test of a TPC module
ArgonCube : prototypes of a new generation of highly modular TPCs
HKK : R&D and test of detector components (EU)
Construction and test of a new magnetized TPC (future ND ?)
Generic cryogenics support to various detectors (new cryo group at CERN)
Participation in the design and construction of LAR1-ND cryostat and cryo plant

## Slide 4: A few examples !!

## Slide 5: WA104 : ICARUS detector overhauling ICARUS Collaboration with INFN and CERN help
Move the detector from the GS Laboratory to CERN (2014)
Prepare at CERN all the necessary infrastructure (clean rooms, cryogenics, …)
Reshape the detector with new components
Construct a new generation of cryostats
Reshape, maintain and modernize the cryo plant
Reassemble the 2 T300 detectors inside their cryostats
Construct a new outer vessel
Make it ready for shipment to FNAL

## Slide 6: ICARUS Detector at Gran Sasso being dismantled and moved to CERN

## Slide 7: From 19 September

## Slide 8: ICARUS Detector at Gran Sasso being dismantled and moved to CERN

## Slide 9: Ready to start

## Slide 10: ICARUS detector overhauling

## Slide 11
To be constructed : two cold vessels with these dimensions

## Slide 13: SBL at the FNAL ~ 0.8 GeV n Booster Beam
 | LAr | Mass
 | Total | Active
LAr1-ND | 180t | 82t
MicroBooNE | 170t | 89t
T600 | 760t | 476t
ICARUS T600
MicroBooNE
LAr1-ND
NuMi Line

## Slide 14: WA105 : LAGUNA detector Demonstrator LAGUNA Collaboration with CERN help
Prepare at CERN all the necessary infrastructure (clean rooms, cryogenics, …)
Construct a new generation of cryostats based on membrane technology
Provide all the necessary cryogenics
Construct and test 2 prototypes of a 2-phases LAr TPC
  3 x1 x 1 m3
  6 x 6 x 6 m3
Charged beam tests at the SPS with full readout capabilities

## Slide 15
The WA105 - LBNO-Demo Detector
External dimensions: 12.5(w)Å~12.5(l)Å~11.2(h) m

## Slide 16
The WA105 - LBNO-Demo Detector

## Slide 17: First membrane cryostat under construction (ready in spring 2015, 17 m3 LAr)

## Slide 18: The outer structure
Overview
Steel profiles (IPE240)
bolted and welded together
Internal dimensions (now confirmed):
6’812mm x 4’412mm x 4’002mm (L x W x H)
Weight:
12T (confirmed)

## Slide 19: Transportation
Divided in 18 pieces:
  Weight: 1 – 1.5 T each
  Sizes: 4.5m x 2.5m
Standard trucks:
  Probably two
  10T each
  2m height each

## Slide 20: WA104 : Magnetized Muon Spectrometer NESSiE Collaboration with CERN help
Prepare at CERN all the necessary infrastructure (space, logistics)
R&D on a warm air core magnet
R&D on a cold air core magnet
Construct and test prototypes of a possible muon spectrometer
Charged beam tests at the SPS with full readout capabilities

## Slide 21: Air core magnets R&D
Warm
Superconducting

## Slide 22: LBNF : Test of a large TPC module LBNF Collaboration with CERN help
Prepare at CERN all the necessary infrastructure (space, logistics)
Prepare a large cryostat for receiving this detector (new cap)
Bring to CERN components assembled in the UK and USA
Prepare/adapt the necessary cryogenics
Charged beam tests at the SPS with full readout capabilities

## Slide 24: CERN support groups
a detector mechanical engineering team (3 eng. already involved)
a new Lar cryo group : 3 staff engineers + 3 Project associates eng. in rotation. The support of the CERN cryolab infrastructure ( cryo tecs and frames contracts)
a team of technicians
an electrical engineer
a controls group
a (Si)PM characterization lab
a simulation group for beam issues
safety and environment experts
secondary beam experts (from CNGS + new people)
access to many CERN technology groups (EL, power, CV, material, ….)
a new physics team

## Slide 25: EHN1 extension as a new test area

## Slide 26
CENF – Civil Engineering Extension B887
-Prevessin site complex-
-EHN1 Extension Area-
CERN Prototype Meeting – M.Nessi
N.Lopez, M.Manfredi (GS-SE)

## Slide 27: The Experimental Hall North 1 - EHN1

## Slide 28
Extension
Site Installation Area
Tunnel TDC85
Experimental Hall B.887 (EHN1)
Technical Aspect: Location
CENF – Civil Engineering Extension B887
The EHN1 is a large industrial building situated on french territory, in Prévessin. The building has to be extended for the new generation of experiments on the neutrinos.
The Extension will extend northwards from the building for about 70 m in the direction of the beams.
CERN Prototype Meeting – M.Nessi
N.Lopez, M.Manfredi (GS-SE)

## Slide 29
CENF – Civil Engineering Extension B887
Technical Aspect: General info
The Extension's dimensions are 72 m long by 50 m wide and 20 m high.
The extension includes two large pits of 7.35m and 9.0m deep.
The top metallic structure is similar to the existing building, allowing for an easy continuation of the overhead crane and services.
The technical gallery will be prolonged. Swallow service trenches will provide the access from the sidewalls to the pits.
Extension
72.0
50.0
20.0
16.5
19.0
41.0
PIT A:
7.35m deep
PIT B:
9.0m deep
CERN Prototype Meeting – M.Nessi
N.Lopez, M.Manfredi (GS-SE)

## Slide 30
Plan view
Section A-A
Section B-B
A
A
B
B
-Construction sheet piles (or Reduce Cost Alternative Option)
-Construction diaphragm wall and final tie beams
-Construction of reinforced concrete structure (raft foundations, slabs, walls, etc.)
-Demolition of the existing gable retaining wall
Technical Aspect: Civil Engineering main activities (1/2)
CENF – Civil Engineering Extension B887
CERN Prototype Meeting – M.Nessi
N.Lopez, M.Manfredi (GS-SE)

## Slide 31
The works to be carried out will include:
-General worksite installation
-Rerouting and cutting existing underground networks
-Mass and ditch earthworks
-Drawdown of the water table
-Road works, car parks and landscaping.
-Rainwater treatment structures (worksite and definitive)
Notes:
Particular attention should be kept to the extracted cut material within 5.50m of distance from the TDC85
Radiological Protection: People allow to enter the technical gallery or inside the existing building 887 should equipped (passive/operational dosimeter) and accredited by CERN. No special measure need to be planned to work outside
Technical Aspect: Civil Engineering main activities (2/2)
CENF – Civil Engineering Extension B887
CERN Prototype Meeting – M.Nessi
N.Lopez, M.Manfredi (GS-SE)

## Slide 32
-Structural steelwork and associated components (Main and Secondary structures, Internal structures, Travelling crane structures)
-Metalwork: guardrails, stairs, ladders, doors
-Removal of the north gable of the existing building (not before the extension is water-tight and air-tight)
CENF – Civil Engineering Extension B887
Technical Aspect: Structural steel main activities (1/2)
CERN Prototype Meeting – M.Nessi
N.Lopez, M.Manfredi (GS-SE)

## Slide 33
Nord Area EHN1 extension
Ready for beams in 2017

## Slide 34
Anticipated start of the works (if possible) + 18 months
Source : ARCADIS → to be updated after tendering procedures
Schedule

## Slide 35
Civil engineering CERN team
Luigi Scibile (group leader)
Matasha Lopez (project leader)
Martin Manfredi (CE engineer)
new CERN CE engineer to follow the construction on side to be appointed
firm ARCADIS as responsible for design and construction follow up (contract running)
Consortium of firms selected for the construction, Contract still in 2014 after CERN Finance Committee approval

## Slide 38: Neutrino extension

## Slide 39: Neutrino extension
Integration of services and experimental groups steered by one of the support group (leader I. Efthimiopoulos)

## Slide 47
Integration team

## Slide 48: How to get in ?

## Slide 49: MOU frame
https://edms.cern.ch/document/1353815
How to get in?
Present to the CERN SPSC a LOI or an expression of interest
When approved we prepare together an MOU (addendum) which defines all responsibilities and resources needed
Then a CERN experiment is created (WA104, WA105, …), with all priviledges and requirements

## Slide 50: Several MOUs are being prepared for signature

## Slide 51: Summary
CERN is providing the community with a Neutrino Platform to develop detectors, beams and components
A new test area is under preparation
CERN provides the community with technical support, logistics and expertise
Any type of application is welcome
Platform organized via an MOU system