## Slide 1: Far-Forward Detectors in the EIC
EIC CFNS Target Fragmentation Workshop
Sept. 28th - 30th, 2020
Electron Ion Collider
Alex Jentsch (BNL)
Co-Convener for YR FF Subgroup

## Slide 2: Layout of Full IR
~9 m around the IP is reserved for the central detector
But the far forward and far backward detector components are distributed along the beam line within 35 m
FF detectors constrained by machine design.
FF region

## Slide 3: Layout of Far-Forward Region
Roman pots (inside pipe)
Off-Momentum Detectors
B1apf dipole
B0 Silicon Detector
ZDC
B0pf dipole
Hadron beam coming from IP
B0apf dipole
B1pf dipole
Q1apf quadrupole
Q1bpf quadrupole
Q2pf quadrupole
B2pf dipole
Detector | Detector Position (x,z) | Angular Acceptance | Notes
ZDC | (0.96m, 37.5m) | 𝜽 < 5.5 mrad | About 4.0 mrad at ϕ ~ 𝜋
Roman Pots (2 stations) | (0.845m, 26m) & (0.936m, 28m) | 0.0* < 𝜽 < 5.0 mrad | 0.65 < xL < 1.0 10σ cut
Off-Momentum Detectors | (0.8, 22.5m) & (0.85m, 24.5m) | 0.0 < 𝜽 < 5.0 mrad | Roughly 0.4 < xL < 0.6
B0 Sensors (4 layers, evenly spaced) | x = 0.19m, 5.4m < z < 6.4m | 5.5 < 𝜽 < 20.0 mrad | Could change a bit depending on pipe and electron quad.
EicRoot – GEANT4 VMC

## Slide 4: What has been studied so far?
e+p DVCS events with proton tagging.
e+d exclusive J/Psi events with proton or neutron tagging.
e+Au events with neutron tagging to veto breakup and photon acceptance.
Meson structure with neutron tagging (epe’ n X) .
Currently in progress
  e+He3 with spectator proton tagging
  Meson structure with Lambda decays (p and )
  e+He4 coherent He4 tagging.

## Slide 5: Aside: B0 Detector
Roman pots (inside pipe)
Off-Momentum Detectors
B1apf dipole
B0 Silicon Detector
ZDC
B0pf dipole
Hadron beam coming from IP
B0apf dipole
B1pf dipole
Q1apf quadrupole
Q1bpf quadrupole
Q2pf quadrupole
B2pf dipole
B0 detector
Acts as a conventional spectrometer – allowing for tracking of charged particles in a dipole field.
Can also be used for photon detection with pre-shower.
1.2 meters of total available longitudinal space – potential space for both a silicon tracker and EMCAL.
Detects particles that are scattered with high enough angle to leave the beam pipe.
Limitations include beam pipe size and spatial asymmetry.
Borrowed from Holger Witte.

## Slide 6: Aside: Roman Pots
~2m
is the RMS transverse beam size.
  is the Gaussian width of the beam, is the emittance.
General rule of thumb is to keep Roman Pot sensors at ~ distance from beam to limit exposure.
  275 GeV – 1 = 1.79 mm (HA) / 3.58 mm (HD)
  100 GeV – 1 = 2.45 mm (HA) / 5.13mm (HD)
  41 GeV – 1 = 6.14 mm
cut places a limit on low-pT acceptance.

## Slide 7: Aside: Off-Momentum Detectors
Needed for measuring protons from nuclear breakup.
Another set of sensors on the other side can be used to detect negative pions from lambda decay.
Beam Pipe
Roman Pots
Off-Momentum Detectors
p
Nuclear Beam
B0pf magnet
IP
No low-pT cutoff - sensors are outside the beam pipe.
Very off-momentum particles can be lost in the quads.

## Slide 8: Zero-Degree Calorimeter (ZDC)
For detecting neutral forward-going particles (neutrons and photons)
Acceptance limited by bore of magnet where the neutron/photon cone has to exit.
neutron cone

## Slide 9: Geometric Acceptances
Neutrons:
Assume uniform acceptance for 0<θ<4.5 mrad
  Limited by bore of magnet where the neutron cone has to exit.
  Up to 5.5 mrad on one side of the aperture.
Resolutions (ZDC)
  Assume an overall energy resolution of σ_E/E=(50%)/√E ⨁ 5%
  Assume angular resolution of σ_θ=(3 mrad)/√E

## Slide 10: Geometric Acceptances
Neutrons:
Assume uniform acceptance for 0<θ<4.5 mrad
  Limited by bore of magnet where the neutron cone has to exit.
  Up to 5.5 mrad on one side of the aperture.
Resolutions (ZDC)
  Assume an overall energy resolution of σ_E/E=(50%)/√E ⨁ 5%
  Assume angular resolution of σ_θ=(3 mrad)/√E
Protons:
Assume uniform acceptance for 6 < θ <13 mrad (20mrad on the other side) – “B0 spectrometer”

## Slide 11: Geometric Acceptances
Neutrons:
Assume uniform acceptance for 0<θ<4.5 mrad
  Limited by bore of magnet where the neutron cone has to exit.
  Up to 5.5 mrad on one side of the aperture.
Resolutions (ZDC)
  Assume an overall energy resolution of σ_E/E=(50%)/√E ⨁ 5%
  Assume angular resolution of σ_θ=(3 mrad)/√E
Protons:
Assume uniform acceptance for 6 < θ < 13 mrad (20mrad on the other side) – “B0 spectrometer”
For protons with p_z/(beam momentum) > 0.6 – “Roman pots”
  275 GeV: Assume uniform acceptance for 0.5<θ<5.0 mrad
  100 GeV: Assume uniform acceptance for 0.2<θ<5.0 mrad
  41 GeV: Assume uniform acceptance for 1.0<θ<4.5 mrad
For protons with 0.25<p_z/(beam momentum)<0.6 – “Off-momentum Detectors”
Assume uniform acceptance for 0.0<θ<2.0 mrad
for 2.0<θ<5.0 mrad, only accepted for |φ|>1 radian
Resolutions (silicon reconstruction with transfer matrix or conventional tracking).
    pt ~ 3% for pt > 550 MeV/c, p ~ 0.5%

## Slide 12: Resolution: Smearing Contributions
Angular divergence
  Angular “spread” of the beam away from the central trajectory.
  Gives some small initial transverse momentum to the beam particles.
Crab cavity rotation
  Can perform rotations of the beam bunches in 2D.
  Used to account for the luminosity drop due to the crossing angle – allows for head-on collisions to still take place.
Detector Choices
  Pixel size, transfer matrix, etc.
25 mrad
These effects introduce smearing in our momentum reconstruction.

## Slide 13: DVCS Snapshot – 275 GeV
~20 cm
High Divergence
High Divergence
High Acceptance
High Acceptance
High Divergence: smaller at IP, but bigger -> higher lumi., larger beam at RP
High Acceptance: larger at IP, smaller -> lower lumi., smaller beam at RP
275 GeV DVCS Proton Acceptance
Relevant detectors: Roman Pots and B0
10𝜎 cut

## Slide 14: DVCS Snapshot – 275 GeV
Reconstruction includes all smearing effects.
Bin migration present, but the slope can still be accurately extracted.
counts

## Slide 15: e+d -> p + n + j/Psi
Off-momentum detectors
Single B0 plane
Particular process in BeAGLE: incoherent diffractive J/psi production off bounded nucleons.
18x110GeV
Neutron spectator/leading proton case.
t-reconstruction using double-tagging (both proton and neutron). Takes advantage of combined B0 + off-momentum detector coverage.
Good timing is assumed here (i.e. vertex smearing removed). If this contribution was not removed, the slope would be distorted.
arXiv:2005.14706
MC Gen.
OMD
B0

## Slide 16: e+d -> p + n + j/Psi
Off-momentum detectors
Single B0 plane
Proton spectator case.
Some examples of observables (light-cone momentum fraction, 𝛼), and missing-momentum (pm).
arXiv:2005.14706
Particular process in BeAGLE: incoherent diffractive J/psi production off bounded nucleons.
18x110GeV
MC Gen.
OMD
B0

## Slide 17: e+3He spectator proton tagging
Acceptance looks good for double tagging the protons.
More detailed study underway.
  Top row: 10x110GeV/n BeAGLE DIS
  Bottom row: 10x110 GeV/n SRC
All protons
All protons
All protons
All protons
All protons
All protons
Double-tagged proton spectators
Double-tagged proton spectators

## Slide 18: e+Pb Collisions in BeAGLE
Wan Chang

## Slide 19: Lambda Decays
e p -> (K) -> e’ + +
p + (Br~64%)
n+ (Br ~36%)
Detecting Lambda’s decays in the target fragmentation area is very hard, due to very large decay length (meters).
Would require in addition detection of negative charged particles (pi-) at the OFF-mom
Zvtx [m]
Zvtx [m]
Protons
Example (10x100 GeV): ~100% detection for protons from Lambda. Significant loss along the beam line (FFQs) due to low momentum of those pions.
Theta [mrad]
Theta [mrad]
Zvtx [m]
Protons
25mrad crossing angle
25mrad crossing angle
Zvtx [m]
Total momentum [GeV]
Total momentum [GeV]
B0pf
Beam Pipe
Roman Pots
Off-Momentum Detectors
p
Slide credit: Julia Furletova
All plots: accepted particles

## Slide 20: Some comments on the “less far” Forward Region

## Slide 21: Hadron endcap acceptance & the beam pipe
+/- 60 mrad
Material in acceptance, [%]
Max space available for Si tracker, [cm]
+/- 60 mrad
+/- 60 mrad
+/- 60 mrad
Max B*dl for Si tracker, [T*m]
+/- 60 mrad
Plots: 3.5 < h < 4.5; white circle: h = 4.0
What can be the realistic h reach is a good question
Also: do not forget about the fiducial
volume cut and lateral leakage close
to the beam pipe
Slide credit: A. Kiselev

## Slide 22: Azimuthal acceptance asymmetry in the h-endcap
Single axis solenoid:
  Aligned with the incoming electron beam (want to minimize the synchrotron radiation) …
  … therefore 25 mrad field axis slope in the h-endcap …
  … therefore dramatically different bending for f ~ 1800 and f ~ 00 at large h
A two-coil solenoid (with the halves aligned relative to the [eh]-going directions) is presently out of consideration:
  Must be a very challenging design
  Inevitable (and large) energy-dependent vertical excursion of the incoming electron beam
  Certainly not an option for the existing BaBar magnet
remember: h in the h-endcap is counted relative to the hadron beam axis!
Study by Rey Cruz-Torres
Forward silicon tracker momentum resolution study
Assume 5 ITS2-like stations,
3T field and 1m lever arm
Slide credit: A. Kiselev

## Slide 23: Takeaways
Acceptances in the FF region of the EIC IR are well-understood.
  Changes at this point will be minor and mostly to do with the addition of the final vacuum design.
Resolutions for FF detectors look very good.
  Not the limiting factor in performing analysis.
  Several studies done, most comprehensive is on the arXiv:2005.14706.
EIC R&D groups studying detector technologies for the FF region.

## Slide 24: Backup

## Slide 25: How does the crab smearing affect reconstruction of t?
Crab/vertex smearing removed.
Crab/vertex smearing included.
Notes: 1) Above |t|= 0.2, B0 begins to be mainly used. 2) the peak at 0.35 is due to the acceptance gap between the Roman Pots and B0.
MC Only
MC + Reco
MC/Reco
5x100 GeV
0.016 < x < 0.025
HA
RP
Transition region/acceptance gap
B0

## Slide 26: How does the crab smearing affect reconstruction of t?
Crab/vertex smearing removed.
Crab/vertex smearing included.
Note: The first few bins are cutoff, where the ratio is dominated by acceptance.
MC Only
MC + Reco
MC/Reco
18x275 GeV
0.9 < Q2 < 50 GeV2
0.0016 < x < 0.0025
HD (v2) – new parameters from C-AD

## Slide 27: How does the crab smearing affect reconstruction of t?
18x275 GeV
0.9 < Q2 < 50 GeV2
0.0016 < x < 0.0025
HD (v2) – new parameters from C-AD
crossing angle = 50 mrad
Crab/vertex smearing removed.
Crab/vertex smearing included.
MC Only
MC + Reco
MC/Reco
Crab/vertex smearing included.

## Slide 28: Reminder: Timing
RMS hadron bunch length ~10cm*.
Because of the rotation, the Roman Pots see the bunch crossing smeared in x.
Vertex smearing = 12.5mrad (half the crossing angle) * 10cm = 1.25 mm
If the effective vertex smearing was for a 1cm bunch, we would have 0.125mm vertex smearing.
The simulations were done with these two extrema and the results compared.
From these comparisons, reducing the effective vertex smearing to that of the 1cm bunch length reduces the momentum smearing to a negligible amount from this contribution.
This can be achieved with timing of ~ 35ps (1cm/speed of light).
Looking along the beam with no crabbing.
What the RP sees.
~1.25mm
For exclusive reactions measured with the Roman Pots we need good timing to resolve the position of the interaction within the proton bunch. But what should the timing be?
*based on ”ultimate” machine performance.

## Slide 29: Conclusions from Timing
With improved optics, the angular divergence and vertex smearing contributions become comparable.
  Note: we expect improved optics for the Roman Pots for both the HD and HA configurations – we need the resolution to be good for both since the HD configuration helps populate the tails.
A larger crossing angle (up to 50 mrad) is under consideration.
  This would make the vertex smearing the dominant contribution, and it has a clear effect on the t-resolution.
Timing will also be required for background rejection, which is being investigated now.

## Slide 30: Some Comparisons – High Divergence
Moving the sensors ~7.2 mm closer (from 10 to 8) gains about 100 MeV in pt-acceptance.
10
8
Move sensors closer to beam in increments of “1.
1 = 3.58 mm
(for the high divergence optics)

## Slide 31: Reminder: Divergences and Optics Parameters
Two configurations
  High divergence (HD) – beta functions tuned such that small beam at IP (higher luminosity), at the cost of larger beam at Roman Pots (meaning worse low-pt acceptance).
  High acceptance (HA) – Larger beam at IP, lower luminosity, better low-pt acceptance at the Roman Pots.
HD
HA
 | 18x275 GeV |  | 10x100 GeV | 
 | HA | HD | HA | HD
RMS DqH, (urad) | 65 | 133 | 180 | 203
RMS DqV, (urad) | 277 | 251 | 243 | 227
Luminosity 1033 cm-2s-1 | 0.94 | 1.93 | 4.07 | 4.35
Note: there are ongoing discussions with C-AD about different configurations that significantly reduce divergence. One of those test cases was used previously to see what it did to the smearing.

## Slide 32: Reminder: Comparison
Beam angular divergence
  Beam property, can’t correct for it – sets the lower bound of smearing.
  Subject to change (i.e. get better) – beam parameters not yet set in stone
    *using symmetric divergence parameters in x and y at 100urad.
Vertex smearing from crab rotation
  Correctable with good timing (~35ps).
  With timing of ~70ps, effective bunch length is 2cm ->.25mm vertex smearing (~7 MeV/c)
Finite pixel size on sensor
  500um seems like the best compromise between potential cost and smearing
The various contributions add in quadrature (this was checked empirically, measuring each effect independently).
Angular divergence
Primary vertex smearing from crab cavity rotation.
Smearing from finite pixel size.
 | Ang Div. (HD) | Ang Div. (HA) | Vtx Smear | 250um pxl | 500um pxl | 1.3mm pxl
[MeV/c] - 275 GeV | 40 | 28* | 20 | 6 | 11 | 26
[MeV/c] - 100 GeV | 22 | 11 | 9 | 9 | 11 | 16
[MeV/c] - 41 GeV | 14 | - | 10 | 9 | 10 | 12
 | Ang Div. (HD) | Ang Div. (HA) | Vtx Smear | 250um pxl | 500um pxl | 1.3mm pxl
 | 40 | 28* | 20 | 6 | 11 | 26
 | 22 | 11 | 9 | 9 | 11 | 16
 | 14 | - | 10 | 9 | 10 | 12
These studies based on the “ultimate” machine performance with strong hadron cooling.

## Slide 33: Current Parameters in Use
 | 275GeV | 275GeV | 275GeV |  | 100GeV | 100GeV
Configuration | HA | HD | HD v2 |  | HA | HD
RMS DqH, (urad) | 65 | 132 | 119 |  | 180 | 203
RMS DqV, (urad) | 229 | 253 | 119 |  | 243 | 227
Angular Divergence
The above divergences are essentially unchanged compared to what was studied previously.
  ”HD v2” is a new set of parameters we are using to evaluate the effect of symmetric divergences, and smaller divergences.
500um x 500um pixels used for the Roman Pots.
20um x 20um pixels used for the B0 sensors (in backup).
The smaller angular divergence configuration(s) cause the overall smearing contribution from divergences and crab cavity/vertex smearing to be comparable in magnitude.

## Slide 34: 100 GeV DVCS protons
~25 cm
Improves low acceptance.
High Divergence
High Acceptance
High Acceptance
High Divergence
Need both detector systems together here!

## Slide 35: 41 GeV DVCS protons
~25 cm
Only one beam configuration for now.
Acceptance gap still observed.
Lower acceptance at high .
B0 plays largest role at this beam energy.