## Slide 1: BNL’s Science and Technology Contributions to the Short-Baseline Accelerator Neutrino Program
Xin Qian
EDG
~eV Sterile Neutrino?
MicroBooNE
LAr-ND/T600
LBNF
(Anti)-Neutrino-Argon
Cross Section
MH, CPV
Unitarity Test

## Slide 2: Craig Thorn Deputy Project Manager Active Detector Xin Qian Physics, ν-Ar Cross Section Analysis Mary Bishai Physics, Simulation and Analysis Michael Mooney Simulation/Calibration of Space Charge Jyoti Joshi Optimization of Cold Electronics setting Brian Kirby Validation of Neutrino Event Generator Yichen Li Electron & Photon transport Chao Zhang Simulation, LArSoft Susan Duffin Cryostat Manager Bo Yu TPC Design Hucheng Chen Electronics Manager George Mahler Detector Assembly Integration Manager
10.4 m
2.5 m
MicroBooNE @ BNL
BNL has been playing crucial roles to the development of MicroBooNE
One of three initial institutions (BNL + Columbia + Yale)
Major part of design was developed by BNL
Lead contributor to the construction: Cryostat, TPC, Front-end electronics
Tremendous collaboration with university groups
TPC designed at BNL, constructed at Yale and Syracuse
Cold electronics @ BNL, warm electronics @ Columbia
CD4 received recently

## Slide 3
MicroBooNE @ BNL
Susan Duffin: Cryostat Design & Fabrication
Stainless steel vessel
Foam insulation 16’’ thick < 15 W/m2
Foam supports 1 fixed, 1 sliding
Bo Yu: TPC Design
Stainless and FR4 structure
3456 Y collection, 2400 U & V induction wires
Cathode @ 125 kV
500 V/cm drift field for 2.5 m drift
Notes: Evacuable, but we do not plan to do so
Bo did a very careful job to keep the field low

## Slide 4
MicroBooNE @ BNL
Hucheng Chen: Readout electronics Design & Fabrication
BNL low-noise (half) cold CMOS ASIC
Warm intermediate amplifiers with commercial ADCs
Channel
RMS Noise (e-)
Noise is ~550e- with CD = 150pF in LN2 (1us, 14mV/fC)

## Slide 5: Recent BNL-led Achievements
Cryostat
  Vessel and foam supports complete at FNAL
  Endcap welded with TPC & PMTs inside
TPC
  Assembly complete, wire tensioning complete
  TPC is installed in the cryostat
  Field cage voltage divider fixed
Readout Electronics
  All electronics installed on the TPC
  All electronics installed on feedthroughs
  Full chain, through DAQ, verified for all channels
George Mahler
Detector Assembly Integration

## Slide 6: Simulation/Calibration of Space Charge Distortion
Space Charge: excess electric charge (slow-moving ions) distributed in space due to cosmic muons
  Modified E field in TPC, thus track/shower reconstruction
  Challenges for the surface LAr TPC
  Magnitude of distortion scaled with Dimension3 and E-1.7
Space Charge Simulation
Michael Mooney
Xin Qian
Craig Thorn
Bo Yu
cm

## Slide 7: Space Charge Tomography Calibration
Calibration: {x,y,z}reconstructed  {x,y,z}true
Use laser and TPC geometry to obtain points with known pos.
Together with anode (signal) plane and laser crossing points, we have first-order pool of anchor points
With cosmic rays, we enable a new set of anchor points
Iteration process to full-volume calibration
Michael Mooney
Xin Qian
Tomography:
Laser +
Cosmic Muons

## Slide 8: TPC signal response
Improving signal response simulation in LArSoft
The wire signal response is a convolution of
  Field response : simulated by Garfield in 2D
  Electronics response: simulated by SPICE
electrons
U
Y
V
U
V
Y
Yichen Li
Validating and improving existing LArTPC simulation software LArSoft is an important part of our work

## Slide 9
Jyoti Joshi

## Slide 10: Optimization of Cold Electronics Parameters
Metrics considered:
  Peak Signal (saturation)
  Signal to Noise Ratio (deconvolution)
  Positron resolution (timing)
  Two-track separation after deconvolution
Jyoti Joshi, Brian Kirby
Xin Qian

## Slide 11: Preparation for Data
LArSoft successfully installed @ RACF
Validation of
  LAr properties in LArSoft
  TPC response in LArSoft
2D + 3D event display tools constructed to assist further development of automated reconstruction
Chao Zhang
Mary Bishai
Brett Viren
Notes: Talk a little bit about Yale workshop

## Slide 12
SBN Physics Goals and Synergy with LBNF
uBooNE neutrino energy range
MicroBooNE TPC design experience, will play an essential role in the next generation of large LAr TPCs
  BNL’s technical effort extends to the design of LAr-ND
  Technology development and R&D for LBNF
Measure ν-Ar cross section @ LBNF 2nd osc. max.
  Crucial for Mass Hierarchy
  ψ-scaling, Short-Range Correlation, emphasizing the hadron side
Understand the MiniBooNE low energy excess
Notes: Label bottom one MicroBooNE 6e20 POT
Nuclear modeling
The first physics motivation of the SBN program is to search for ~ eV sterile neutrino, which is suggested by the LSND/MiniBooNE anomaly.
In particular, the uBooNE is going to use the unique e/gamma separation of LArTPC to study the MiniBooNE low energy excess.
The second physics motivation is to the neutrino-argon cross section @ 0.8 GeV region. The Phase-II/III will study the anti-neutrino-argon cross section.
The Booster neutrino energy range covers the second oscillation maxima of LBNF. A good understanding of the neutrino-argon cross section and event topology is crucial for the MH determination, and future precision measurement of CP phase.
The third, but in my view the most important motivation of the SBN program is the technology development and R&D for LBNF

## Slide 13: Validation of GENIE with Electron Scattering data
Validation of GENIE neutrino event generator is crucial for cross section extraction
  Garino et al. PRC 45 (1992)
  Importance to understand Quasi-elastic mechanism
  Important to understand the Final State Interaction (subsequent)
Xin Qian
Notes: Pattern recognition, cosmic ray’s challenge

## Slide 14: Synergies with BNL LAr R&D effort
Noble liquid R&D has been the backbone of many successful experiments
On-going BNL LAr R&D includes
  Optimization of photocathodes as a high brightness source of electrons in LAr
  Diffusion of electrons as a function of electric field for both longitudinal and transverse directions
  Attachment cross section (rate constants) of electrons for all impurities
    Early Career Award  toward improving LBNF’s purification system
Noble liquid R&D
1973
1980
2000
BooNE
NA48
2010
R806
D0
1990
ATLAS
HELIOS
LAr-ND
LBNF
Craig Thorn, Xin Qian
Yichen Li, Jyoti Joshi

## Slide 15: Preliminary Results
Measurement of electron transport properties (diffusion, drift velocity and attachment) in LAr are crucial inputs to simulation
Yichen Li
Craig Thorn
Electrons are Thermal
Notes: Need to update a lot of plots … and sentences …

## Slide 16: Stage II&III: LAr-ND + ICARUS-T600
Continuing technology developments towards LBNF
  Next generation cold electronics with ADC & multiplexing in the cold
  Wrapped-Wire TPC design
  Membrane cryostat technology
  Design for ultra purity
Definite answer to the LSND/MiniBooNE anomalies
First Near/Far Setup with LArTPC
  Experiences accumulated and lessons learned from this setup are crucial for LBNF physics analysis
LAr-ND Conceptual Design
Craig Thorn, Bo Yu
Mary Bishai: WG2 beam systematics
Notes: 1 on technolgy (next generation cold electronics, more multiplexing)
Sterile neutrino reach (correlated two detectors)
Near/Far in LArTPC

## Slide 17: LAr-ND (BNL) Design Features
Insulation
450 mm
Insulation
450 mm
Insulation
250 mm
Insulation
450 mm
4,800 mm
1,200 mm
Desired Side Penetration
for LAr pump.
1,000 mm
Upstream View
5,100 mm
Innovative aspects:
  The minimization of the ullage and liquid vapor contact.
  The use of cold feedthroughs.
  The idea of purifying only the boil off GAr from the ullage during operations (not the bulk of the liquid)
  The use of LN2 cooled heat exchange panels inside to control the LAr boil-off
A conceptual design has been developed
Preliminary requirements for the cryostat are established
Beginning to engineer the cryostat and cryogenic systems
Active volume: ~ 50 ton
Craig Thorn, Bo Yu
See more in Hucheng’s talk

## Slide 18: Summary
BNL is a tremendous resource for the community in LAr TPC and cold electronics development
  Major contributor to MicroBooNE and entire Short-Baseline Neutrino Program (SBN)
    Tremendous collaboration with university groups
  LAr R&D is crucial in understanding/simulating LAr detector physics  Great value to SBN and LBNF
SBN is a critically important test bed for LBNF
  Technology development
  Interesting physics reach for ~eV sterile neutrino and neutrino-Argon cross section
  Automated reconstruction and improvements in simulation will be of great value for LBNF
  We are contributing in a big way!