## Slide 1: ENDF/B-VII.1.x Decay Data Sublibrary
A.A. Sonzogni, T.D. Johnson, E.A. McCutchan,
National Nuclear Data Center
Brookhaven National Laboratory
Building 817
Upton, NY 11973-5000
www.nndc.bnl.gov

## Slide 2
Will present work on:
Fixing bugs in ENDF/B-VII.1
New data for ENDF/B-VII.1.1
Related activities we are active on:
Beta-delayed neutron emitters CRP (IAEA).
Decay Heat Consultants meeting (IAEA).
Reactor antineutrinos
ORNL and Jyvaskyla experiments

## Slide 3
ENDF/B-VII.1 decay data sub-library
Errors in ENDF/B-VII.1:
98mY Pn value, should be 0.034 but its is given as 0.00331.
90Kr, 2nd decay should have rfs=1.
Minor bugs in ENDF/B-VII.1:
Nuclides that are known to be 2b- or 2EC, but no half-life is known, much less the beta spectra.
Serious Issue:
ENDF/B-VII.1 is out of synch with ENDF/B fission yields

## Slide 4
What we’ve done since the last release
Improve antineutrino spectra calculations by including Ib from TAGS experiments
and Ib following fit to Tengblad 1990 data
92Rb Use the 2006LH01 gamma normalization
137I Run LOGFT , Added 2 E2 gammas, run BRICC
135sb Run LOGFT , Added 2 E2 gammas, run BRICC
95Sr,140Cs,95Y,143La,145La,141Cs,143Ba,91Rb,93Rb,94Rb,144La use IB TAGS
82Ge Use ENSDF assuming IB(GS)=0
83Ge Use ENSDF assuming IB(GS)=1
90Br,96Rb,98Y,138I,88B,99Y,89br,134sb,95rb,82As Adjust the beta feeding to match Rudstam's data
91Br Use Woehr beta feeding, neutron have to be added

## Slide 5
We have participated in experiments in ORNL and Jyvaskyla that measured new TAGS data for about 30 nuclides, which will be added to the library (IB, EEM, ELP).
The next release may also include antineutrino spectra for some nuclides.
Comparison between different Decay data sub-libraries can be found at www.nndc.bnl.gov/nudat2/ddsl/

## Slide 6
An important drawback of the sub-library is the absence of level information. As a result, it can not be used to obtain coincidences.
If a new XML format is approved, the next major release will include these level data.
Next slides, some applications

## Slide 7
No adjustable parameters
Phys. Rev. C 91, 011301(R) (2015)
For energies > 5 MeV, the electron and antineutrino spectra are mainly due to about 20 nuclides
The decay of these nuclides is of great interest
Recent (n,fission) Beta Spectra Calculations

## Slide 8
The integral of antineutrino multiplicity has a similar behavior as the delayed neutron multiplicity.
Target | Delayed neutron multiplicity/fission
238U | 4.4E-2
235U | 1.59E-2
241Pu | 1.62E-2
239Pu | 6.45E-3
n + p  n + e+ cross section integrated spectra

## Slide 9
235U thermal fission yields
235U thermal Yi/<sI>
Yi=CFYi∫s(e)Ini(e)
<sI>=SYi

## Slide 10
238U fast Yi/<sI>
239Pu thermal Yi/<sI>

## Slide 11
Systematics of <sI> with (3Z-A)
LFF: Light fission fragments ( Z<47)
HFF: Heavy Fission Fragments (Z >= 47)
EE: Even-Z, Even-N
EO: Even-Z, Odd-N
OE: Odd-Z, Even-N
OO: Odd-Z, Odd-N

## Slide 12
Comparison with preliminary RENO data
Excess of antineutrinos

## Slide 13
Next workshop on
Modeling of Antineutrino Flux from Nuclear Reactors
June 2016
Port Jefferson or BNL
Tentatively Tuesday 6/14 – Thursday 6/16, 2016
1st workshop took place at the INT, Seattle, 11/2013
2nd workshop SUBATECH, Nantes, 01/2015

## Slide 14
235U Thermal
Relation to decay heat

## Slide 15
235U Thermal
92Rb, 100Nb, 96Y, 101Nb,102Nb

## Slide 16
IAEA CRP on Beta delayed neutron emitters
nd: Delayed nu-bar, number of neutrons for single fission event. It can be calculated as:
nd =S CFYi Pni , about 0.015/fission for 235U
CFY: cumulative fission yield.
Pn: beta-delayed neutron probability.
Will result in newly evaluated values of Pn and T1/2 for delayed neutron emitters, ex, 88Br. These data will be incorporated in ENSDF as well as the sub-library.

## Slide 17
232Th
238U
235U
241Pu
238Np
233U
239Pu
252Cf
Delayed nu-bars calculated using Pn and CFY

## Slide 18
232Th
238U
As before, but plotting lighter and heavier fission fragments contributions

## Slide 19
Now looking at the contributions of the different fission modes.
Using Katakura’s 5-Gaussian parametrization (IAEA CRP)

## Slide 20
D2, most asymetric fission are the main (90%) contributors to delayed nubars