## Slide 1: ATF Electron Beam and UED plans
Mikhail Fedurin
ATF User meeting
December 7 – 11, 2020

## Slide 2: Outline
ATF main beam parameters
ATF beam diagnostic and manipulation capabilities
FY20 e-beam improvements and plans
Electron beam upgrade perspectives
UED facility improvements
UED plans

## Slide 3: ATF linac main beam parameters
Parameter | Typical value / range | Best value
Energy | 50-65 MeV | 75 MeV
Charge | 0.1 – 2 nC | 2.5 nC
Repetition rate | 1.5 Hz | 3 Hz
Electron spot size on cathode | 2.86 mm | 0.2 – 4 mm
Bunch length | 1-8 ps | 100 fs with compression
Average bunch current | 100 A | 1.2 kA with compression
Emittance | 1 – 3 mm mrad | 0.8 mm mrad @ 0.5 nC

## Slide 4: Facility Overview (Bldg. 820)
CO2 Laser Area
Electron Accelerator Area
Beamline 2:
Experimental station with
plasma cell capillary
Insertion device section
Differential pumping (1 stage)
CO2 & e-beam IP
X-band Deflector cavity (TDC)
Beamline 1:
Experimental stations:
1) Inverse Compton,
2) LWFA with gas jet cell,
3) IGS (big in vacuum space)
Differential pumping (2 stages)
CO2/YAG & e-beam IP

## Slide 5: ATF beam diagnostics
  Beam profile measurements
PMQ triplet assemblies:
G=50 T/m, focal length ~20 cm
G=500 T/m, focal length ~8 cm
Microscope (25-0506 X15 Reflecting Objective NA 0.28, F~13 mm)
Basler Gigabit camera (scA 1400-17gm, F=135 mm).
  Bunch length measurements

## Slide 6: ATF beam manipulation and diagnostics
e-beam mask technique
Images on the screen
after deflector
e-beam spectrometer
Image at mask

## Slide 7: ATF beam manipulation capabilities
  Bunch compression
~1 Tesla magnetic field
50 mm magnetic length
Permanent Magnet Chicane
Electromagnet chicane

## Slide 8: ATF beam manipulation capabilities
  10 um microbunching with CO2 laser
N. Sudar, P. Musumeci, I. Gadjev, et al., PRL 120, 114802 (2018)

## Slide 9: FY20 e-beam improvements and plans
Replacement of ATF old gun klystron in January significantly improved beam stability
X-band klystron refurbish was arranged and may happen after FY21 (>1year repair due to present constraints)
Control system continues upgrade
Bunch compression design for LWFA experiments at beamline #1
ATF received funding from BNL for maintenance work (crane replacement, YAG room air handlers)

## Slide 10: Electron beam bunch compression design
  e-beam compression with permanent magnet chicane (simulations by Yichao Jing)
FWHM bunch length < 20 fs is achievable for higher charge (100 pC in this case) with the combination of the zigzag chicane together with CSR shielding

## Slide 11: Electron beam upgrade perspectives
  Deflector cavity for BL1
TDC BL1
TDC BL2
Beamline #1 design with TDC diagnostics capabilities after completion of laser transport

## Slide 12: Electron beam upgrade perspectives
  Linac energy upgrade
Plan to feed linac acceleration sections with separated klystrons to push maximum operational energy to 110-120 MeV
Gun klystron
Linac
klystron #1
Linac klystron #2

## Slide 13: ATF UED main beam parameters
 | BNL | SLAC | MSU
Beam energy, MeV | 3 | 3.68 | 0.03
N e- per pulse | 1.25 E+6 | 3.8E+5 | 500
Temporal resolution, fs | 180 | 102 | 300
Beam size diameter, mm | 300 (100 best) | 400 (10 best) | 20-40
Max repetition rate | 48 | 120 (180 best) | 1,000
N e- per sec per mm2 | 880 | 360 | 400
Advantage | short bright pulse | short bright pulse | DC (no jitter)

## Slide 14: FY20 UED facility improvements
Repetition rate upgrade from 5Hz to 48Hz obviously speed up user scan rate and decrease systematic drifts influence
Stable performance during last summer
e-beam collimator was replaced with new design

## Slide 15: UED plans: Support Tunable Pump Wavelength
mid-IR pump-probe materials science requires an Optical Parametric Amplifier to access the full range of wavelengths
To reach the needed OPA output energy levels of ~100 mJ at l=10-11 mm, a more energetic pump pulse from a new Ti:sapphire booster amplifier is needed
“Topas HE” OPA from SpectraPhysics installation starts next week

## Slide 16: UED plans: Flexible UED-UEM translation table
Quick change design to switch between UEM and UED baseline drift tube configuration

## Slide 17: UED plans: beam diagnostic beamline extension
Beamline extension for real-time beam diagnostic at the end of beamline will include spectrometer magnet for shot-to-shot energy fluctuations, Faraday cup for charge fluctuations

## Slide 18: Thank you!