## Slide 1: LWIR Laser Plans
Misha Polyanskiy
2020-12-11

## Slide 2: Outline
2021 Upgrades
Timing system upgrade
Vacuum compressor chamber and transport line
  Motivation for vacuum upgrade
  Configuration of the system after upgrade
  Commissioning plan
Ongoing R&D
Towards 25 TW, ≤0.5 ps
  Millijoule solid-state seed
  Post-compression
R&D for long perspective
  Optical pumping

## Slide 3: LWIR Optical Delay Line Overview
Goal: Provide user-friendly CO2 system synchronization with e-beam
Current synchronization of CO2 system involves step-wise, in phase adjustment of a number timing mechanisms:
  Clock/RF signals at 2856, 81.6, 40.8, 10.2 MHz
  Precision triggers at 240 Hz, 1.5 Hz, single-shot at few- to sub-ns resolution
  Optical path internal to CO2 laser via roof reflector/trombone
Complex manual adjustment system requiring laser expertise
Approach: Multiplex critical signals in single long-range optical delay line
Convert various signals from RF/electrical domain to optical
Requires updates to facility timing architecture
  New model of optical clock distribution and synchronization of laser systems
Single software controlled, user-accessible delay for experiments
3

## Slide 4: Why vacuum?
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
Ti:Sapphire amplifier
OPA
Osc
Regenerative CO2 amplifier
Compressor
Stretcher
Final CO2 amplifier
15 μJ 350 fs
10 mJ 70 ps
20 J 70 ps
Ge
Nd:YAG
Coupler
Isolator
Shutter
[2 μJ] [140 ps]
Experimental chamber
Vacuum
Air
NaCl
14 J, 2 ps
5 TW

## Slide 5: Vacuum transport
1.3 J
8.1 J
4.7 J
2.4 J
97.5 mm
≤ 1 J/cm2 (design spec)
5 TW (2 ps): ≤ 0.4 TW/cm2
25 TW (100s fs) ≤ 2.0 TW/cm2
 | Air (12 m) | NaCl (40 mm) | Air + NaCl
n2 | 3.0e-19 cm2/W | 3.0e-16 cm2/W | 
B-integral @ 5 TW | 1.0 | 3.3 | 4.3
B-integral @ 25 TW | 4.9 | 16.4 | 20.3
Standard requirement: B < 1

## Slide 6: Vacuum transport
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~ ~
Compressor
Compressor
NaCl
Vacuum
70 ps
2 ps
≥ 70 ps
≤ 2 ps
Experimental chamber
Vacuum
Air
Experimental chamber
Vacuum
Compressed pulse: B ≈ 0 (vacuum)
NaCl
Stretched pulse: B < 1 (by CPA design)

## Slide 7: LWIR laser infrastructure after upgrade
Seed Laser Table
Final amplifier
Shielding wall
Experimental Hall
CO2 Room
Flexible polarization rotator (FPR)
Compressor
FEL Room
CO2
YAG
7
Plasma shutter
Nonlinear pulse compressor
Test chamber
YAG
CO2
plasma

## Slide 8: Vacuum upgrade: Implementation plan
Now-Summer 2021:Preparations
  Long-lead and other procurements
  Continued evaluation of system components in view of handling higher pulse energy
Summer 2021: Installation
Fall 2021: Commissioning and Return to User Operations
  Initial demonstration of 2TW operation in vacuum
    Basic system optimization at presently available power levels
    Enables interleaved user operations at 2 TW while power upgrade is characterized during machine development time
  Gradual power increase: 2 TW a ~5 TW
    Characterization of component performance at each power level
    Detailed optimization and trouble-shooting
Late 2021: Delivery of higher power user operations

## Slide 9: Compressor gratings
Compressor gratings (4x)
Manufacturer | Richardson Gratings (Newport)
Catalog # | 53028ZD02-970R
Coating material | Au
Substrate | Zerodur
Type | replica
Line density | 100 mm-1
Ruled area | 154 x 206 mm2
Blaze wavelength | 9.0 μm
Shot # | Sample | mV | mJ | ω (µm) | Ф0 (J/cm2) | Damage size (pix) | Damage size (µm) | Damage threshold (J/cm2) | comments
Compressed pulse (~2 ps) @ 9.2 um |  |  |  |  |  |  |  |  | 
1 | Au on Cu replica 100/mm, 9 um Richardson | 63.6 | 3.63 | 140 | 11.79 | 255 | 234 | 2.91 | strong damage
2 |  | 21.2 | 0.82 | 140 | 2.67 | 56 | 51 | 2.49 | some darkening
3 |  | 13.2 | 0.47 | 140 | 1.51 |  |  |  | darkening hardly visible
4 | Au on Zerodur replica 100/mm, 9 um Richardson | 56.2 | 3.03 | 140 | 9.84 | 252 | 231 | 2.51 | 
5 |  | 45.2 | 2.22 | 140 | 7.21 | 204 | 187 | 2.95 | 
6 |  | 12.4 | 0.43 | 140 | 1.41 |  |  |  | no visible damage
7 |  | 33.8 | 1.49 | 140 | 4.85 | 156 | 143 | 2.88 | 
8 | Inprintus test grating (bare Cu, low quality) | 54.0 | 2.86 | 140 | 9.28 | 274 | 252 | 1.85 | 
9 |  | 29.2 | 1.23 | 140 | 4.00 | 203 | 186 | 1.65 | 
10 |  | 6.6 | 0.21 | 140 | 0.70 |  |  |  | no visible damage
11 | Au on SS master 100/mm Bach | 60.0 | 3.33 | 140 | 10.82 | 240 | 220 | 3.14 | 
12 |  | 14.6 | 0.52 | 140 | 1.70 |  |  |  | no visible damage
13 |  | 50.8 | 2.62 | 140 | 8.51 | 184 | 169 | 4.11 | 
14 |  | 42.8 | 2.06 | 140 | 6.69 | 163 | 150 | 3.78 | 
15 |  | 23.4 | 0.93 | 140 | 3.02 |  |  |  | hardly visible darkening
15 |  |  |  |  |  |  |  |  | 
16 | Cu mirror lab grade, new SPAWR | 42.4 | 2.03 | 140 | 6.60 | 160 | 147 | 3.81 | 
17 |  | 51.6 | 2.68 | 140 | 8.70 | 188 | 173 | 4.07 | 
18 |  | 55.8 | 3.00 | 140 | 9.73 | 195 | 179 | 4.30 | 
19 |  | 24.2 | 0.97 | 140 | 3.15 |  |  |  | no visible damage
Damage test protocol 2018-11-28
Mitigation options
Master gratings
Replica, regular replacement
Bigger beam
Au Reflection Absorption
0.8 um 0.987 0.013
9.2 um 0.995 0.005
Calculated using optical constants from: Babar and Weaver. Optical constants of Cu, Ag, and Au revisited, Appl. Opt. 54, 477-481 (2015)

## Slide 10: (10) Millijoule, femtosecond solid state seed
Proposal 308053
800nm 20nm BW 200mJ 200ps
876nm 20nm BW 80mJ 200ps
800nm 20nm BW 80mJ 200ps
9199.6nm 230nm BW
6mJ 200ps
Ge filter
BaGa4S7
CaCO3
Current:
Regen x1012
Final x103
Solid state seed:
Final only x103
2 ps limit for pulse duration is defined by gain narrowing in CO2 amplifiers
Main contributor to gain narrowing is the high-total-gain regenerative amplifier
Gain narrowing in the final amplifier is relatively small
If a 10 mJ sub-picosecond pulse is available from a solid-state laser system, CO2 regen can be eliminated from the amplifier chain
This would allow achieving a sub-picosecond at present energy levels

## Slide 11: Nonlinear pulse compressor
Nonlinear post-compressor
LDRD
n(t) = n0 + n2I(t)
Self-phase modulation
Dispersive compression
Nonlinear properties of LWIR materials
AE-101
Delivery of a proof-of-principle prototype: 2022
Joulemeter
Beam profiler
NaCl
BK7
BK7
BK7
14 m
12.88 mm Dia.
Teflon aperture
[ Imaging lens ]
Sample
85 mJ
150 mJ
300 mJ
500 mJ
Materials with negligible nonlinear absorption
(NaCl, KCl, BaF2[?]..)
Materials with non-negligible nonlinear absorption
(ZnSe, ZnS, Ge, Si…)
NaCl
ZnSe
140 mJ
560 mJ

## Slide 12: Optical pumping (long-long term)
Absorption spectra of a 1 bar CO2 / 9 bar He mix
Population dynamics for a
100 ns, 500 mJ/cm2, 2.8 μm pump
Advantage | Why important
High pressure possible | Smooth gain spectrum
No CO2 dissociation | High rep. rate Compact gas cell Non-equilibrium mixed-isotope CO2
N2-free mixture | Efficient energy extraction in a single pass
High shot-to-shot stability | Real-life applications
[Potentially] high efficiency | 
Direct to upper level
Via a combination vibration
AE-85

## Slide 13: Summary
2021 upgrades
We are aiming at achieving a 5 TW peak power in IP via implementation of a vacuum compressor chamber and a vacuum beam transport
After implementing the upgrades, we will gradually ramp-up power staring at 2 TW where the system is known to perform reliably
The main risk is a long-term degradation of the compressor gratings at increased energy. Mitigation options are available
We will also upgrade the timing system
We keep working on increasing the repetition rate
R&D
An aggressive research program on 10 mJ solid-state seed aimed at 0.5 ps pulse duration via better use of CO2 gain bandwidth
Nonlinear pulse compression will allow 100s of fs long pulse and up to 25 TW peak power. Prototype delivery scheduled in 2 years.
Experimental study of optical pumping is in progress