## Slide 1: 2021 Facility Upgrade Plans
Chris Cullen
December 11, 2020

## Slide 2: Topics
UED
  Ultrafast Electron Microscope (UEM)
  Optical Parametric Amplifier (OPA)
B820 laser rooms
  Pre down configuration
  Present configuration
    Including laser room reconfiguration completed September, 2020
  Scope of NIR upgrades
  Scope of LWIR (CO2) upgrades
  Schedule
  Summary

## Slide 3: Ultrafast Electron Microscope (UEM)
LDRD funded project: Demonstration of feasibility of sub-nm, picosecond electron microscope for the life sciences
  NSLS-II with ATF personnel support
Objective is to obtain tissue sample images with minimal sample degradation due to high speed, short duration pulse
Quick change design to switch between UEM and UED baseline drift tube configuration

## Slide 4: UED Sample Mid-IR Pump Source (OPA)
A DOE early career award (Jing Tao) has provided the opportunity to extend the wavelength range available for pumping UED samples
This will broaden the physical mechanisms that can be studied with the instrument and increase the scientific reach of the facility
A commercial Optical Parametric Amplifier will be installed next week that will provide multi-mJ femtosecond pulses fully tunable from 2-11 microns
Diagnostics, controls, full Integration, and first beam delivery on samples expected in early 2021
ATF previously assembled and demonstrated the Ti:Sapphire booster amplifier required to achieve the higher NIR pulse energies necessary for pumping the OPA itself (below)

## Slide 5: B820 Laser Rooms

## Slide 6: Configuration Prior to Summer, 2020
Shielding wall
Plasma shutter
Final amplifier
Seed Laser Table
CPA
Polarization rotator
Regen
Jib Crane
NIR
LWIR
Experimental Hall

## Slide 7: Present Configuration with Summer 2020 upgrades
Shielding wall
Plasma shutter
Final amplifier
Seed Laser Table
CPA
Polarization rotator
Regen
Jib Crane
NIR
LWIR
Room upgrades:
Vestibule removed
Dividing wall removed
Seed laser table moved
Regen table moved
Experimental Hall

## Slide 8: Present Configuration with Summer 2020 upgrades
Final amplifier
Shielding wall
LWIR path

## Slide 9: Modified Laser Transport Systems – Plan View
Shielding wall
Plasma shutter
Final amplifier
Seed Laser Table
CPA chamber
Polarization rotator
chamber
Regen
NIR
LWIR
NLPC experimental chamber

## Slide 10: Modified Laser Transport Systems – Iso View
Room walls hidden for clarity
Seed Laser Table
Final amplifier
Shielding wall
Experimental Hall
Laser Rooms
NIR Cube with mounting bracket
FPR chamber on steel frame with concrete base

## Slide 11
NIR compressor
Alternate location for NIR compressor
NIR Vacuum Transport Path Diagram - Isometric
NIR vacuum transport runs along the floor in the laser rooms
NIR vacuum transport runs along the ceiling in the ebeam experimental hall
LWIR Components removed for clarity.
Beam enters laser room here
NIR compressor
NIR

## Slide 12: LWIR Vacuum Transport Installation – Plan View
Shielding wall
Plasma shutter
Final amplifier
Seed Laser Table
CPA
chamber
Polarization rotator
chamber
Regen
NLPC chamber
Future NLPC staging area
Collimating mirror
Existing vacuum transport
Circular polarization mirror
LWIR

## Slide 13: LWIR Vacuum Transport Installation – Iso View
Room walls hidden for clarity
Seed Laser Table
Final amplifier
Shielding wall
Experimental Hall
Laser Rooms
CPA
FPR

## Slide 14: CPA Vacuum Chamber
Optics mounted to concrete pedestals for thermal stability and vibration isolation
Vacuum chamber supported by SS legs
Bellows is only mechanical connection
Concrete
Breadboard
Stable frame
Bellows

## Slide 15: CPA Vacuum Chamber Optical Load Path
Concrete base
SS flange connects to concrete base
Structural tube columns
Rigid frame
Breadboards leveled on frame
Bellows connected to flange is the only physical connection between the chamber (and pumps) and the optical mounts

## Slide 16: Flexible Polarization Rotator (FPR)
Concrete base
  Vibration isolation
  Thermal stability
FPR is on hand
Vacuum chamber designed
6” diameter clear aperture

## Slide 17: FPR Motion
Stepper motor drive
Brass worm gear drive
-2° to 92° range of rotation

## Slide 18: NLPC Experimental Chamber
Procurement in process
Intended for NLPC development
Initial vacuum transport does not include optics in this chamber

## Slide 19: Schedule
UEM – March, 2021 installation
OPA – installation planned for next week
Vacuum laser transport
  Proceed with major procurements
    Major procurements are for the CPA, FPR & NIR chambers
  Goal: Delivery of improved NIR and LWIR capabilities to users before the end of calendar 2021!
    Goal: Installation commencing in August 2021
    Major components must be received before installation commences

## Slide 20: Upgrades Summary
UEM will obtain tissue sample images with minimal sample degradation.
UED OPA tunable wave converter will provide a range of wave lengths to study a wider range of physical effects on materials.
NIR vacuum transport & compressor will improve beam stability and optics reliability.
CO2 Vacuum transport will deliver high quality TW beam to experiments for increased particle acceleration.
Polarization rotator will provide infinitely adjustable polarity from horizontal to vertical to simplify viewing plasma waves.
Circular polarization is required for Radiation Pressure ion acceleration and the RUBICON experiment.

## Slide 21: Thank you! Questions? Up next: User Discussion