## Slide 1
Progress on AE85
A Multiatmosphere CO2 Amplifier Optically Pumped by a 4.3 mm Fe:ZnSe Laser
Funded by DOE HEP Accelerator Stewardship Program 2020-2023
SERGEI TOCHITSKY-PI, Dana Tovey, Jeremy Pigeon, Chan Joshi
Department of Electrical Engineering, UCLA
Igor Pogorelsky, Mikhail Polyanskiy
Brookhaven National Laboratory, USA
Sergei Mirov et al
University of Alabama at Birmingham

## Slide 2
Motivation
  Long-wavelength Infrared range is attractive for particle acceleration and radiation generation. At present we experience a Renaissance of mid-IR ultrafast lasers mainly based on OPA and OPCPA in nonlinear crystals pumped at 1-2 mm.
  CO2 laser is efficient and is able to store a great deal of energy within the active medium. The shortest pulse demonstrated so far is ~2 ps and all high-power picosecond systems operate in a single-shot regime limited by electrical discharge stability in a >10 atm molecular gas.
  In AE85 experiment funded by the DoE grant, we study potential of Optically Pumped CO2 laser technology for production of ≤1 ps pulses at a high-repetition rate. A collaborative effort of UCLA/BNL (gas lasers) built around the state-of the art mid-IR solid-state lasers developed at UAB.
ATF User’s 2020

## Slide 3
10.4
10.6
10.8
11
0
0.2
0.4
0.6
0.8
1
Normalized Gain
1atm
10.4
10.6
10.8
11
Wavelength (
m
m)
CO
2
Gain Spectrum
10atm
10.4
10.6
10.8
11
20atm
Recipe for success: High-gain CO2 laser
Population of 001 level Maximized
Population of 100 level Minimized
Optically Pumped CO2 Laser
Normalized Ampl..
Wavelength (mm)
~1.2THz
CO2 Molecule
ATF User’s 2020

## Slide 4
Modeling of Picosecond Pulse Amplification
ATF User’s 2020
4.3 mm
Fe:ZnSe
Laser
10-15 atm
Isotope CO2
Amplifier
10 mm pulses
300-500 fs
10 GW
10 mm
300 fs
OPA
Seed
Feasibility study of a compact GW class CO2 amplifier and gain dynamics.
D. Tovey et al. Appl. Opt., 58, 5756, 2019, J Appl. Phys. 128, 103103, 2020

## Slide 5
Group of Prof. S. Mirov
Tunable 3.9-5 mm Fe:ZnSe source for
Optical Pumping of the CO2 laser
ATF User’s 2020

## Slide 6
Optically Pumped High-pressure CO2 Laser
ATF User’s 2020
High pressure CO2 cell
Dichroic mirror
(T = 99% for 4 μm,
R = 99.5% for 10 μm)
NaCl window
Focusing lens
Dichroic mirror
4.3 μm pump pulse
10 μm cavity
Detector
10 μm filter
2.5 mm
(beam magnified 5x)
12.5 mm
4.3μm Pump Beam
10μm Laser Beam

## Slide 7
With >35 mJ absorbed in the multiatmosphere CO2 cell.
Lasing and Gain Dynamics in OP CO2 cell
ATF User’s 2020

## Slide 8
4.256 mm OPO Source Pumped by Nd:YAG
ATF User’s 2020
CO2 Cell
Amplification
Q-switched
Nd:YAG
OPO
4 μm pulse:
~50-100 mJ, 10 ns
1064 nm
OPO
2128 nm
4.3 mm
Gabriel Mennerat and Philippe Kupecek, OSA TOPS Vol. 19 Advanced Solid State Lasers, 1998

## Slide 9
rear mirror
50% output coupler
2 mm ZGP
2128 nm pump, 10 ns
4256 nm half-harmonic
3 cm cavity
4-mm OPO in ZnGeP2 Modeling
ATF User’s 2020
Dana Tovey, UCLA + Igor & Misha, BNL experimental verification.
2mm ZGP crystal

## Slide 10
Status of the 4-mm OPO
ATF User’s 2020
YAG

## Slide 11: Experimental Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in Laser Rooms) | 1-2 weeks | 2 weeks
Laser(s)* + Electron Beam |  | 
CY2021 Time Request
Capability | Setup Hours | Running Hours
Electron Beam Only |  | 
Laser* Only (in FEL Room) | 2021-2023 5-6 weeks | 5 weeks
Laser(s)* + Electron Beam |  | 
* Laser = Near-IR or LWIR (CO2) Laser
Time Estimate for Remaining Years of Experiment (including CY2021)

## Slide 12
Summary
We have made important and necessary steps in AE85 experiment, a CO2 Laser only, funded by DOE Accelerator Stewardship Program
  Gain dynamics study in optically pumped CO2 active medium pumped by a ~50 mJ Fe:ZnSe laser indicates that a) a short 1-10 cm long cell at >12 atm pressure and b) regenerative amplifier are durable.
  Next step in 2021 will be developing at BNL a 100 mJ, 4.3 um laser system based on NdYAG laser pumped OPO’s. Design and building a 1-10 cm long cell and start with lasing in the >10-12 atm CO2-He medium followed by seeding and amplifying ~0.5 ps pulses using the CPA scheme.
  We request 3-4 weeks in 2021 using front end with the CPA capability and may be the 10 mm CO2 regen.
ATF User’s 2020