## Slide 1: Collinear wakefield accelerator based on corrugated waveguide
drhgfdjhngngfmhgmghmghjmghfmf
PI: A. Zholents, APS/ANL
ATF User meeting, December 9, 2020
Continuing experiment: 306051
Funded by LDRD at ANL
W. Jansma, A. Nassiri, S. Sorsher, K. Suthar, E. Trakhtenberg, G. Waldschmidt, J. Xu (APS/ANL)
S. Doran (HEP/ANL)
S. Siy, N. Behdad (University of Wisconsin)
M. Fedurin, K. Kusche, M. Palmer (ATF/BNL)

## Slide 2: GOAL is to characterize accelerator components
E+
E -
2 mm
Near term plan:
measure both longitudinal and transverse wakefields
measure spectrum of the sub-THz Čerenkov radiation
measure group velocity of the fundamental mode.

## Slide 3: Main results of the first experiment March 9 -13, 2020
Measurements of the wakefield induced by the corrugated waveguides agree with the calculations

## Slide 4: Installation at ATF
ebeam
Paraboloid mirror to collect sub-THz radiation
Tubes and a tube holder mounted on the translation stage

## Slide 5: Calibration of the spectrometer
First image was taken using spectrometer magnet current of 30.4 A
Second image was taken using spectrometer magnet current of 30.1 A
These two plots are used to calibrate screen’s energy resolution and to obtain 0.776 keV/pixel (see below).
Lower field or higher energy is at the left side and higher field and lower energy is at the right side of the screen.
30.4 A
30.1 A
keV/pixel
coeff = (0.7764 ± 0.0005)

## Slide 6: Beam energy spread measurement
FWHM = 4.5 pixels or approximately 4.5*50/sqrt(2)=160 keV (assuming equal betatron and synchrotron sizes and 50 keV/pixel calibration), i.e., sE=68 keV
Wire trace
5 mm/85 pixels
3 mm/52 pixels
Beam size measured with linac running on crest using energy collimator screen
Energy collimator window

## Slide 7: Determine bunch length, Thursday
76 pixels
74 pixels
242 pixels
The window size in energy collimator is 242/75*0.46 = 1.48 mm or 4.95 ps
34 pixels
Window
The microbunch length is 34/75*0.46 = 0.21 mm or 0.7 ps
(Coefficient 0.46 is defined in the next slide)
Beam image taken after energy collimator in second point in a dog-leg with a large dispersion

## Slide 8: Determine bunch length, Thursday
THz
Use interferogram produced by three equally spaced bunches selected by the horizontal mask located in the energy collimator area
Interferogram taken on Thursday: five peaks are expected from a train of three bunches giving five overlapping regions.
Fit with the damped oscillator formula:
Thus, the distance between the centers of the bunches is: 2 * 0.23 mm = 0.46 mm
balometer
Michelson interferometer

## Slide 9: Wakefield
Impact of the wakefield on slice medium energy
Energy histogram
Charge =0.2 nC
A=
= 3.6x1016 V/m/C
FWHM = 1.5 mm (~ 5 ps)
Green’s function, V/m/C
Peak current, (rel. units)
s, m
A Cos(2pf0t)
Loss factor:
f0=180 GHz

## Slide 10: Difference between smooth pipe and Unobstructed path
Note: the beam shifted horizontally between measurements by ~ 31 pixels
Charge=140 pC, bunch length = 5 ps flattop
Data collected on Tuesday 03102020
Use as the reference for Unobstructed path: file name 2020031017061940_Spectr_no_mask_SLIT_IN.asc
Use for the Smooth pipe: file name 2020031017374064_Spectr_no_mask_SLIT_IN_Smooth_Pipe.asc
The difference is shown below: file name Diff 2020031017374064 Smooth minus Unobstructed 17061940.asc
No visible difference between the unobstructed pass and a pass through the smooth pipe is seen after adjustment of horizontal shift caused by the beam drift.
Spectrometer screen

## Slide 11: Use spectrometer measurement in the case of a smooth pipe to define energy distribution in the beam
309 keV=0.776 keV/pixel*399 pixels
Data collected on Tuesday 03102020
Use as the reference for Smooth pipe: file name 2020031017374064_Spectr_no_mask_SLIT_IN_Smooth_Pipe.asc
Lower energy
Higher energy
399 pixels / 309 keV FWHM
Charge=130 pC, bunch length = 5 ps flattop
Gaussian fit
Lower energy
Higher energy
Measured energy spread includes energy chirp

## Slide 12: Measurement of the energy chirp
The best fit is obtained using 3.2 degree of RF phase. Model accounts for 68 keV rms incoherent energy spread.
Measured
Modeled
±3.15sE
Histogram of beam energy distribution

## Slide 13: smooth pipe
Charge=130 pC, bunch length = 5 ps flattop
Data collected on Tuesday 03102020
Use the same reference for Smooth pipe: file name 2020031017374064_Spectr_no_mask_SLIT_IN_Smooth_Pipe.asc
Smooth pipe
Lower energy
Higher energy

## Slide 14: Find Difference between pipe 2 and a smooth pipe (p.2)
Charge=170 pC, bunch length = 5 ps flattop
Data collected on Tuesday 03102020
Use for the Pipe 2: 2020031017510097_Spectr_no_mask_SLIT_IN_Corrug_Pipe_N2.asc
Pipe length = 92.58 mm
Pipe 2 with corrugations

## Slide 15: Find Difference between pipe 2 and a smooth pipe (p.3)
Charge=170 pC, bunch length = 5 ps flattop
Data collected on Tuesday 03102020
The difference between Pipe 2 and Smooth pipe is shown below:
file name Diff 2020031017510097_N2 minus Smooth 2020031017374064.asc
498pixels / 386 keV
Pipe length = 92.58 mm
Note: the beam shifted horizontally by ~ 50 pixels
Error estimate 1.5 pixel/1.0 keV

## Slide 16: Find Difference between pipe 2 and a smooth pipe (p.4)
Charge=170 pC, bunch length = 5 ps flattop
Data collected on Tuesday 03102020
The difference between Pipe 2 and Smooth pipe is shown below:
file name Diff 2020031017510097_N2 minus Smooth 2020031017374064.asc
498pixels / 386 keV
Pipe length = 92.58 mm
Error estimate 1.5 pixel/1.0 keV
rel. units
394 ± 10 keV

## Slide 17: Summary of measurements
Pipe 1
Pipe 2
Pipe 3
= 8.58 keV
D =(theory –measurement)
T-theory; M-measurement
T-M=(357 – 351) keV
T-M=(394 – 386) keV
T-M=(404 – 415) keV
relative error =8.58/394=0.022

## Slide 18
Second ATF experiment using corrugated waveguides
Difficult but doable
December 14 -18, 2020

## Slide 19: The Experiment Goal
1. We will use four corrugated waveguide samples and measure
  the impact of the wakefield using the spectrometer
  THz spectrum using Michelson interferometer
    to find 180 GHz signal
    to determine group velocity of THz signal
2. We will compare four samples with different lengths and determine
a) scaling with the sample length
b) spread in THz frequency measurements

## Slide 20
Experimental setup
Top view
Side view
Unobstructed beam path
Beam target for a transition radiation
TPX window
Horn collecting THz radiation

## Slide 21: ATF experiment setup
e-
1
3
4
5
A conceptual diagram of an experiment at ATF
1) device under the test,
2) horn and waveguides,
3) horizontal slit,
4) spectrometer magnet bending trajectory in horizontal plane,
5) diagnostic screen
6) TPX window
7) Michelson interferometer
8) LiHe cooled bolometer/Gentech bolometer
7
8
6
THz
2
CST MICROWAVE STUDIO®

## Slide 22: 2020 Activities & Impacts Associated with this Experiment
Practically the same talk was given at two different online events:
Invited Talks:
  November 17, 2020, “A compact high repetition rate free-electron laser based on the advanced wakefield accelerator technology”, A. Zholents et al., OSA: High-brightness Sources and Light-driven Interactions Congress. Compact (EUV and X-Ray) Sources.
Contributed talk
  May 11, 2020, “A compact high repetition rate free-electron laser based on the advanced wakefield accelerator technology”, A. Zholents et al., Int. Part. Acc. Conf. 2020.
Continuation of LDRD in ANL was granted in part because of the success of the experiment at ATF.

## Slide 23: COVID-19 Pandemic Impacts
No impact beyond inconvenience

## Slide 24
Electron Beam Requirements

## Slide 25: Special Equipment Requirements and Hazards
Electron Beam
  A special equipment that we expect to need:
    shaped bunch using mask technique (likely),
    bolometer/interferometer setup,
    horizontal translation stage (levered at the beam height)
    the horizontal slit,
    diagnostic screen,
    alignment laser.
Hazards & Special Installation Requirements
  No known hazards