## Slide 1
IR2@EIC Design Status, Luminosity vs CM Energy, Polarization
Vasiliy Morozov
on behalf of 2nd IR Design Team
Workshop Series on the 2nd Interaction Region at the EIC
December 15-16, 2020

## Slide 2: 2nd IR Design Team
Jefferson Lab: V. Burkert, R. Ent, Y. Furletova, R. Gamage, D. Higinbotham, A. Hutton, C. Hyde, F. Lin, T. Michalski, V.S. Morozov, R. Rajput-Ghoshal, A. Seryi, A. Sy, C. Weiss, M. Wiseman, W. Wittmer, Y. Zhang
BNL: E.-C. Aschenauer, A. Kiselev, C. Montag, R. Palmer, B. Parker, V. Ptitsyn, F. Willeke, H. Witte
Stony Brook University: P. Nadel-Turonski

## Slide 3: 2nd IR Considerations
2nd IR of the EIC
  Off project
  Consider alternative design choices
  Capability of having a 2nd IR is one of the EIC design specifications
  Complementary measurements and capabilities to 1st IR
  Interest and support of the nuclear physics community
High-level requirements
  High luminosity at low and medium CM energies of ~60 GeV
  Detector acceptance satisfying physics requirements at low and medium CM energies
  Compatibility with running in parallel with the 1st IR

## Slide 4: 2nd IR Schematic

## Slide 5: Complementarity to 1st IR

## Slide 6
However, crossing angle may cause
- Luminosity loss
Beam dynamics issues
Negative impact on certain aspects of the detector performance
  resolution
  rapidity coverage
Crossing angle allows one to
- avoid parasitic collisions due to short bunch spacing
- place electron and ion machine elements side by side  independent beam energies
- move final focusing quadrupoles close to the IP  high luminosity
separate forward particle form the incoming electron beam and use large apertures in the forward ion quads and  improved forward and far-forward detection
move forward particles away from solenoid axis  improved momentum resolution
- shorten the common section of the detector beam pipe  reduced detector background
eliminated by Crab Crossing:
Crossing Angle
Effective head-on collision restored
Beam dynamic issues resolved

## Slide 7: Acceptance as Function of and
acceptance at
acceptance at
  Requires dispersion
  Secondary focus allows for
  Therefore, one can approach the fundamental limit

## Slide 8
Physics Drivers for Low at Small

## Slide 9: Geometric and Machine Constraints
Consistency with existing infrastructure: experimental hall and tunnel size
Integrate necessary components: spin rotators, crab cavities, ZDC, luminosity monitor, Roman pots, low- tagger, etc.
Geometric and optical match to the rest of the collider rings
All beams transport over full energy range
Magnet aperture-edge fields < 4.6 T
Sufficient DA and momentum acceptance
Total beam-beam < 0.015 (p), 0.1 (e)
Beam aperture (p); H/V (e)
Dispersion and dispersion slope constraints at crab cavities

## Slide 10: 2nd IR Geometry and Optics Matching and Component Integration
Beam crossing direction flipped compared to the 1st IR
Not much flexibility in electron geometry because of electron spin rotator requirements
Electron beam line is a slightly modified baseline design
Enough knobs integrated into the ion beam line design to allow testing of different geometries
Started with 50 mrad crossing angle and plan to optimize it along with other parameters
To ion spin rotator
To ion spin rotator

## Slide 11: Ion 2nd IR Optics from 135 to 275 GeV
Lengths of downstream final focusing quadrupoles optimized to provide 10 mrad polar angle acceptance with aperture-edge fields below 4.6 T
Use constraints on km and km as in the 1st IR
Upstream section is based on the 1st IR
Doublet optics with reversible polarity of the second quad depending on the energy cm (>135 GeV) cm (<135 GeV)
Secondary focus with acceptance
Roman pot
at 2nd focus
IP
Same optics and geometry as in baseline
ions

## Slide 12: 2nd IR Acceptance Simulations Under Way

## Slide 13: Engineering Feasibility
Engineering feasibility of the most challenging magnets
  Largest-aperture forward ion quad
  Forward spectrometer dipole
Parameter | Quadrupole | Dipole
Magnet name | QFFDS02B | BXDS01B
Aperture radius (cm) | 22 | 29
Gradient/Field | 13.92 T/m | 4.59 T
Length (m) | 3.7 | 3

## Slide 14: 2nd IR Design Optimization
Grid search and optimization in the luminosity/ detector acceptance/ beam parameter phase space
Each iteration involves
  Lattice design update
  Luminosity estimate
  Acceptance simulation
Streamline the process as much as possible
IRs optimized individually
2nd IR analysis to be completed
2.3
10.0
9.0
0.4
3.7
4.5

## Slide 15: 2nd IR Configurations for Parameter Scan
 | Configuration # |  |  |  |  |  |  | 
Parameter | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
1. Solenoid shift [m] | 0 | 0.5 | 0 | 0 | 0 | 0 | TBD | TBD
2. Full crossing angle [mrad] | 50 | 50 | 35 | 50 | 50 | 50 |  | 
3. Forward acceptance polar angle [mrad] | 53 | 53 | 37 | 53 | 25 | 53 |  | 
4. Far-forward acceptance polar angle [mrad] | 10 | 10 | 7 | 10 | 10 | 7 |  | 
5. Number of bunches relative to baseline | x2 | x2 | x2 | x1 | x2 | x2 |  | 
Luminosity re-optimization needed? | In progress | No | Yes | Yes | No | Yes |  | 

## Slide 16: Two IR Operation
Possible scenarios
  Only one IR is operated at a time (conceivable if other scenarios not available for some reason or performance is better than in other scenarios)
  One IR operates in its optimum configuration in its optimum energy region while the other IR runs in parasitic mode
  Combined operation of the two IRs is globally optimized
Additional machine components for the 2nd IR
  IR magnets
  Spin rotators
  Crab cavities
Main constraints for simultaneous operation of the two IRs
  Beam-beam tune shift
  Total chromaticity
  Limits such as beam divergences at the IPs

## Slide 17: Comments on Polarization at 2nd IP
The same techniques are used to control the polarization at the 2nd IP as at the 1st one
The same polarization options are available at the 2nd IP as at the first one
The only special case is longitudinal deuteron polarization
  Available at energy points
  The two IPs are separated by 1/6th of the ring. If spin is longitudinal at one IP, it will be longitudinal at the second IP if the spin precession between the two IPs in an integer number of 𝜋 
 |  | Within range? | Longitudinal at both IPs?
6 | 39.3 | Yes | Yes
7 | 45.9 | No | No
8 | 52.5 | No | No
9 | 59.0 | No | Yes
10 | 65.6 | No | No
11 | 72.1 | No | No
12 | 78.7 | No | Yes
13 | 85.3 | No | No
14 | 91.8 | No | No
15 | 98.4 | No | Yes
16 | 104.9 | Yes | No
17 | 111.5 | Yes | No
18 | 118.0 | Yes | Yes
19 | 124.6 | Yes | No
20 | 131.2 | Yes | No
21 | 137.7 | No | Yes
 |  | Within range? | Longitudinal at both IPs?
6 | 39.3 | Yes | Yes
7 | 45.9 | No | No
8 | 52.5 | No | No
9 | 59.0 | No | Yes
10 | 65.6 | No | No
11 | 72.1 | No | No
12 | 78.7 | No | Yes
13 | 85.3 | No | No
14 | 91.8 | No | No
15 | 98.4 | No | Yes
16 | 104.9 | Yes | No
17 | 111.5 | Yes | No
18 | 118.0 | Yes | Yes
19 | 124.6 | Yes | No
20 | 131.2 | Yes | No
21 | 137.7 | No | Yes

## Slide 18: 2nd IR Feasibility Study Plan
Completion of conceptual linear design
  Footprint with optimization knobs developed
  Conceptual linear optics design developed
Proof-of-principle studies of chromatic compensation schemes in the ion collider ring
  Identify and use tracking to evaluate compensation schemes of the chromatic effect of the 2nd IR alone
  Develop and evaluate by tracking a scheme for mutual compensation of the two IRs
Conceptual engineering assessment for critical/challenging components
Beam parameter optimization
  Single-mode operation of the 2nd IR
  Operation in parallel with the 1st IR
Simulation of detector acceptance
Parameter scan
  Identify scan parameters and choose ~3-4 configurations of, e.g., crossing angle, repetition rate, and forward/ far-forward acceptance using nuclear physics input
  Repeat items 4 and 5 for all of the different configurations
Summarize the 2nd IR concepts

## Slide 19: Backup

## Slide 20
Detection Issues with Crossing Angle
Crabbing causes apparent smear of transverse beam size at the IP
Transverse vertex position can be found by
  narrowing down its longitudinal position through precise timing of ~35 ps
  simultaneously measuring particle’s position, angle and energy in the far-forward section
Crossing angle increases the gap in the rapidity coverage in the rear direction
Gap in rapidity coverage:
beam pipe solid angle (~20 mrad) +

## Slide 21: Ion 2nd IR Optics up to 135 GeV
All aperture-edge fields below 4.6 T
cm with on km and km
Roman pot
at 2nd focus
IP

## Slide 22: Electron 2nd IR Optics
Based on 1st IR electron optics design and modified to account for different crossing geometry
The bending angle between the spin rotator solenoids on each side and the IP are constrained by the polarization rotation requirements
Room for optimization in case of a larger than 25 mrad crossing angle due to larger transverse spacing of the electron ion beam, e.g. electron quads moved closer to the IP or aperture of the ion quads increased if beneficial
IP
Same optics and geometry
as in baseline

## Slide 23: Constraints on Two IR Operation
Fundamental dynamical constraint: beam-beam tune shift
An empirical quantity that sets a limit on how much non-linearity originating from the beam-beam interaction can be tolerated by the beam before it loses stability
May result in luminosity sharing
Scaling of luminosity when beam-beam tune shift limited: where is the beam-beam tune shift of the beam-beam limited beam.
When not limited by beam-beam, can potentially have a greater combined luminosity than with a single IR.

## Slide 24: Other Constraints
Somewhat more loosely defined but critical dynamical constraint: natural chromaticity Momentum dependent tune shift that is inversely proportional to No specific limiting value. Usually a few tens to a little over a hundred.
Stronger focusing at the IP may help with beam-beam tune shift but in addition to increasing chromaticity produces a larger beam divergence at the IP leading to further limitations associated with
  Synchrotron radiation pattern
  Beam pipe and magnet apertures
  Limit on the beam size aspect ratio due to beam-beam
  Detector acceptance

## Slide 25: Issues with Doubling of Bunch Numbers
At a fixed luminosity, chromaticities of each IR are doubled
Beam angular divergences are increased by
Larger synchrotron ration cone
More challenging polarimetry due to shorter bunch spacing
Faster kicker for bunch swap in the electron collider ring
Impedance and instabilities need to be re-evaluated due to change of beam spectrum
Background due to events coming from parasitic collisions
Crabbing parameters need re-optimization