## Slide 1: Long Shadow Detector (LSD)
TK Hemmick

## Slide 2: Detector cartoon from Rey Cruz-Torres (LBNL)
Free Real Estate!?
New Challenge:
  10 GeV/c PID in the barrel
New Opportunity:
  All silicon tracker option frees up additional space for PID detectors in the barrel.
What can we imagine in this new space to push PID to higher momentum?

## Slide 3: PID ~ Velocity
p = mgb E = mg velocity(b) measurement yields mass.
Direct measurement:
  Record signal time at multiple locations, calculate v.
  “Fast” detector = low transit time spread (most easily achieved at small transit time)
Velocity-dependent interaction(s) with detector:
  Specific Ionization (aka )
  Cherenkov Radiation:
    qC measured wrt track direction.
    Thus dependent upon deliverables from tracking
  Bremsstrahlung:
  Transition Radiation:
eID mechanisms
Two Presentations:
Pushing the limits of dE/dx (Tom)
Pushing the limits of Cherenkov (Henry)

## Slide 4: dE/dx w/ hybrid detector
Dots = STAR
Boxes = sPHENIX Test Beam
Specific ionization is a function of b.
PID bands vs momentum.
Crossing ~b = 0.7 (TOF can help)
Limitations from Landau tails:
  Primary ionization Statistics = Poisson
  Total ionization = Landau
  Traditional Approach:
    Lots of gas & lots of samples
  Forward thinking approaches:
    Gas choice to minimize Landau
    “Cluster Counting”
Goal: Achieve dE/dx performance with least gas volume

## Slide 5: Scaling Expectations
Scaling to our available length:
Using a 3s reference @ 40 cm gas:
Existing Concept (“Timepix”)
  Avalanche onto Silicon Pixels
  Tiny Pixels (smaller than cluster spacing)
  Sufficient gain for single electron
In principle can work
EXTREMELY expensive for large area.
Can we accomplish with conventional tech?

## Slide 6: What is the meaning of “Long Shadow”?
Camel
Satellite Photo

## Slide 7: Long Shadow Detector -- LSD
Drift leverages huge Lorentz angle as “magnifier”
Clusters spread across space and time.
Higher B = Lower Transverse diffusion
  Example: T2K(130 V/cm) has only
Detect (count) clusters with conventional means.
B-field
track
HV-
New Concept: Like a “Streak Camera”
Sensors
Bad for Tracking
Good for PID
Silicon Tracker
Multiple sections…

## Slide 8: Summary
Long Shadow Detector (LSD) presently just a hallucination.
  Absolutely requires additional space
    All-silicon tracking option?
  Absolutely requires help due to dE/dx band crossings:
    DIRC, TOF, ???
  Likely prefers higher(est) magnetic fields
Garfield Simulations required to optimize sometimes competing constraints:
  Maximal total cluster count.
  Minimal cluster merging.
Readout can take multiple forms:
  Standard charge collection (pads)
  Optical read-out of GEMs:
    e.g. Detecting electroluminescence w/ fast cameras [see f.i. NIMA 886(2018) 24].
    Optical read-out looks the most appropriate for cluster counting (no ion-tail effects).
    Can we replace cameras with SiPM arrays (NOTE: Avalanche supplies a MANY-photon signal lessening radiation damage concerns)
Garfield simulations are ongoing but not yet ready for today…stay tuned
Thank you, Silvia!