## Slide 1: CDR Reference Detector
R. Ent (JLAB)
With input from E.C. Aschenauer (BNL) and T. Ullrich (BNL)
EIC-UG 4th YR Meeting
Electron Ion Collider

## Slide 2: CDR Reference Detector - preamble
From talk of Rolf Ent (and Thomas Ullrich) at 1st YR meeting hosted by Temple University:
It is crucial to complete the Yellow Report January 2021 to stay in phase with the hoped-for EIC early-CD dates.
We are better off completing a Yellow Report and later making a “v2” or revisiting (parts) of the Yellow Report ~1 year later than running late. Do what you can.
My view:
  At CD-1 we need a plausible scenario reference design for any general-purpose* detector.
  At CD-2 we need a reference design for a general-purpose detector with some of the equipment components known in detail.
  At CD-3 we need to have completed >80% of the full engineering & design of at least one general-purpose detector.
This led to the phrase “Reference Detector”. This is the same for the CDR as the YR.

## Slide 3: Reference Detector – technologies
This led to the phrase “Reference Detector”. This is the same for the CDR as the YR
This led to the phrase “Reference Detector”. This is the same for the CDR as the YR, and for the EIC Project!
From the EIC (independent) Design Review this week (a requirement for a large project before a CD-1 review), in the summary slide on the Detector Overview:
Ongoing Yellow Report activity of EICUG to refine EIC detector definition http://www.eicug.org/web/content/yellow-report-initiative
…
We used a reference general-purpose detector optimized for the EIC physics with subdetectors based on the most likely technology, as the final EIC detector(s) will be defined once collaborations are formed.
For purposes of CD-1, this is sufficient. Ultimately, the EIC community will be very influential in determining the trajectory of the EIC detectors.

## Slide 4: CDR section 2 (science) and section 8 (detector) - authors
Walt Akers (JLab), Elke Aschenauer (BNL), Fernando Barbosa (JLab), Andrea Bressan (Trieste), Carlos Munoz Camacho (Orsay), Kai Chen (BNL), Silvia Dalla Torre (Trieste), Latifa Elouadhriri (JLab), Rolf Ent (JLab), Olga Evdokimov (UIC), Yulia Furletova (JLab), Dave Gaskell (JLab), Tanja Horn (CUA), Jin Huang (BNL), Alex Jentsch (BNL), Alexander Kiselev (BNL), Bill Schmidtke (BNL), Ralf Seidl (RIKEN), Thomas Ullrich (BNL)
All members of this assembled editorial board were asked for specific sections that needed updating in the text assembled from existing pre-CDRs, the EIC detector handbook, the ongoing Yellow Report + Other Project Cost activities, etc. – most names were shown at 2nd YR meeting, but we added some as-needed expertise, like for a software section, two electronics engineers, etc.
Many, many thanks to all!!! (and be aware we may need minor changes until December 15)
Now what is in it… (see also “CDR science and experimental equipment” link on http://www.eicug.org/web/content/yellow-report-initiative)

## Slide 5: CDR section 2 (science)
Carlos, Elke, Olga, Ralf, Rolf, Thomas: mainly science context for EIC experimental equipment requirements and ensure consistency with YR

## Slide 6: CDR section 8 (detector)
Alexander, Andrea, Bill, Dave, Elke, Fernando, Jin, Kai, Latifa, Rolf, Tanja, Silvia, Walt, Yulia
Section 8.3-8.7 are essentially copied straight to the YR!
It is the same reference detector!

## Slide 7: Reference Detector – technologies
We used the first column as reference detector but also showed many of the alternate detector technologies as options, as the final call comes from the community detector proposals. The context of this was mentioned in 8.1 “Realization of the Experimental Equipment in the National and International Context”.
Table from CDR, made by
Silvia Dalla Torre and Tanja Horn

## Slide 8: Reference Detector – 2D sketch
electrons
protons/ions

## Slide 9: Reference Detector – Backward/Forward Detectors
far-forward detectors
far-backward detectors

## Slide 10: Reference Detector Location
Hadron Storage Ring
Electron Storage Ring
Electron Injector Synchrotron
Possible on-energy Hadron
injector ring
Hadron injector complex
Two possible locations – IP6 and IP8 – for detectors and Interaction Regions.
Assumption: IP6 is “default” EIC detector location (as IP8 has sPHENIX).
Existing IP6 and IP8 Hall, doors, and situation are different which can lead to complications to use or reuse equipment.
This does not mean IP8 is not considered, just that from project risk view IP6 is the assumption.

## Slide 11: Reference (Central) Detector Maintenance
Scheduled maintenance (months) – detector moved to the assembly hall
  The only option to access the central tracker and the forward / vertex / backward silicon trackers
Short access (hours) - actions without major disassembly
  Electronics trailer
  Hadronic calorimeter frontend electronics
  Cryocan
Longer access (days) – endcaps rolled out in halves
  e/m calorimeter frontend electronics
  B0 magnet detectors (silicon tracker and e/m calorimeter)
  Outer part of the central detector (planar trackers, perhaps the gaseous RICH electronics, perhaps DIRC electronics – if installed)
Alexander Kiselev, Yulia Furletova, Walt Akers

## Slide 12: Reference Detector Integration (some plots beyond CDR)
Note: IP6 has here a larger (3T) new magnet
Note: IP8 we assumed the sPHENIX/BABAR magnet

## Slide 13: CDR Reference Detector Summary
From presentation of Elke Aschenauer and Rolf Ent at quarterly EICUG remote meeting April 2020:
  The call for expression of interest is a crucial step to get guidance on the EIC detector scope.
  The EIC Project needs to assume a scenario at this stage to keep us on track towards a CD-1 review, with manageable risk.
  The presumed 70%-30% split of US and international commitments for the first detector is a starting value as the level of international and non-DOE interest has not yet been fully assessed.
  Ultimately, the EIC community will be very influential in determining the trajectory of both detectors.
CDR Reference Detector = YR Reference Detector = your Reference Detector(s) to fill in for the upcoming Call for Detector Proposals

## Slide 14: CDR Reference Detector Summary
Personal perspective as EIC user:
CY2021 is going to be a defining year for the detector!
Yellow Report ready for inclusion of CD-1 review to support EIC detector.
EIC is (in the eyes of many) a REAL project after CD-1 approval…
… and we can start detector Engineering and Design after CD-1!
We want to have the hand-off from the successful generic EIC-related detector R&D program to a hybrid project/generic detector R&D program.
We want to ensure the EIC is an international project.
We want collaboration(s) to form and transition from a reference detector to the detector(s).
We want a clear path for “the other” IR and detector.