## Slide 1: Accelerator/IR Overview
A. Drees for the EIC team
4th EIC Yellow Report Workshop at LBL
November 20th, 2020

## Slide 2: Outline
Overview EIC complex
  RHIC
  ESR
  HSR
  Key parameters
IR Design Criteria
IR Layout Details
  Forward region
  Rear region
  Matching
  Magnet cryostats
Central Vacuum Chamber
  Synchrotron radiation
Summary

## Slide 3: EIC Collider Concept
Design based on existing RHIC,
RHIC is well maintained, operating at its peak
Hadron storage ring 40-275 GeV (upgraded RHIC)
  many bunches (x10 RHIC)
  bright beam emittance
  need strong cooling or frequent injections
Electron storage ring (2.5–18 GeV (new))
  many bunches,
  large beam current (2.5 A)  10 MW S.R. power
Electron rapid cycling synchrotron (new)
  1-2 Hz
  Spin transparent due to high periodicity
High luminosity interaction region(s) (new)
  L = 1034cm-2s-1
  Superconducting magnets
  25 mrad Crossing angle with crab cavities
  Spin Rotators (longitudinal spin)
  Forward hadron instrumentation
BNL-EIC

## Slide 4
Hadron Storage Ring
Electron Storage Ring
Electron Injector Synchrotron
Possible on-energy Hadron
injector ring
Hadron injector complex
From RHIC to the EIC
EIC
Existing RHIC with
Blue and Yellow ring
Add electron storage ring
Which holds the electrons which collide with hadrons
We add an electron
Injector complex which delivers full energy electrons to the storage ring
The strong hadron cooling facility completes the facility
RCS
HSR
ESR

## Slide 5: EIC CDR Parameters for Ecm and Luminosity

## Slide 6: Interaction Region Design criteria
The Interaction Region with the colliding beam and surrounding detector is the most complex and most constrained section of a collider.
Inside the IR section we need to combine
  strong focusing,
  complex superconducting magnets with novel but-prototyped magnet technology
  Collisions with a crossing angle,
  large aperture for good acceptance of forward physics,
  tolerable chromatic aberrations,
  manageable synchrotron radiation,
  manageable impedance of the vacuum systems,
  feasible warm-cold transitions around super conducting magnets
Matching of the IR layout with the lattice of the ring
  Requires more dedicated and one-of-a-kind magnets
mask and collimation systems
provide favorable condition for luminosity measurements and auxiliary detectors

## Slide 7: EIC IR: Overview
Forward
Rear
RHIC yellow ring: EIC hadron ring (HSR)
Add electron storage ring in existing tunnel (ESR)
Detector centered in center of IP
-Possible location: IP6

## Slide 8: EIC IR
Fits into RHIC tunnel and experimental hall
RHIC sec5
Forward
RHIC sec6
Rear
Hadrons
Electrons

## Slide 9: EIC Collisions with a Crossing Angle
However, crossing angle causes
- Low luminosity
- Beam dynamics issues
As a consequence:
Effective head-on collision restored
beam dynamic issues resolved
Modest crossing angle of 25 mrad
- avoid parasitic collisions due to short bunch spacing,
- for machine elements, to improve detection
- reduce detector background,
avoided by Crab Crossing
Several transverse RF resonator (crab-cavity) prototypes built
- tested with proton beam in the CERN-SPS

## Slide 10: EIC IR: Forward Direction (RHIC sec5)
Requirements for hadron beam direction
  B0pF: Forward Spectrometer (6 - 20 mrad)
  Neutron Detector (+/-4 mrad)
  Roman pots (sensitive 1 to 5 mrad)
Mostly interleaved magnets
  Exception: B0 and Q1BpF/Q1eF
Large apertures of proton forward magnets
Name | R1 | length | B | grad | B pole
 | [m] | [m] | [T] | [T/m] | [T]
B0ApF | 0.043 | 0.6 | -3.3 | 0 | -3.3
Q1ApF | 0.056 | 1.46 | 0 | -72.608 | -4.066
Q1BpF | 0.078 | 1.61 | 0 | -66.18 | -5.162
Q2pF | 0.131 | 3.8 | 0 | 40.737 | 5.357
B1pF | 0.135 | 3 | -3.4 | 0 | -3.4
IP
Hadrons
Electrons

## Slide 11: Hadron Forward - Apertures
275 GeV
41 GeV
100 GeV
Magnet aperture optimization:
Magnets tilted and displaced
Magnets split in two (e.g. Q1A and Q1B)

## Slide 12: Forward Side, Two Cryostat Layout
Highlights:
Final assembly will be done inside the RHIC tunnel.
Gaps between all magnets – space for coil leads (some nested in end plates), inner helium vessel welding.
Bellows between all cold masses, at outer yoke/shells – no positional shifting due to welding.
Near IP End
Outgoing Hadron Beam
Incoming Electron Beam
Q0EF
Q1EF
B0PF
B0APF
Q1APF
Q1BPF
Q2PF
B1PF
B1APF

## Slide 13: EIC IR: Rear Direction (RHIC sec6)
B2eR: separate photons from beam, separate low Q2 electrons from beam
2-in-1 magnets
  Lepton magnet aperture defined by SynRad fan
  Hadron magnets: 10s beam size aperture
Name | R1 | R2 | length | grad | B pole
 | [mm] | [mm] | [m] | [T/m] | [T]
Q1ApR | 20 | 26 | 1.8 | 78.4 | 2.0
Q1BpR | 28 | 28 | 1.4 | 78.4 | 2.2
Q2pR | 54 | 54 | 4.5 | 33.8 | 1.8
Name | R1 | R2 | length | B | grad | B pole
 | [mm] | [mm] | [m] | [T] | [T/m] | [T]
Q1eR | 66 | 79 | 1.8 | 0 | 14 | -1.1
Q2eR | 83 | 94 | 1.4 | 0 | 14.1 | 1.3
B2eR | 97 | 139 | 5.5 | 0.2 | 0 | -0.2
Bethe Heitler
Hadrons
Electrons

## Slide 14: Rear Side Magnets, Cryostat Layout
Found that the space between rear elements is adequate.
Magnets in three separate helium vessels supported inside a common cryostat.
Helium Vessel Detail
Hadron Beam
Electron Beam with Synrad
Hadron Beam
Electron Beam with Synrad
Rear Cryostat Inside Tunnel
Near IP End

## Slide 15: Match to Hadron Ring
Forward and rear hadron lattice matched into RHIC/HSR
  Snake at correct angle
  95 mrad IP to rotator
  1300m at crab cavities
    Hor. phase advance 90º
Repurpose RHIC magnets
  Few additional magnets required
    Need to re-cryostat existing magnets
  New: 2 warm quads (5T/m)
b function
Dispersion
Crab cavities
Rotators
Forward
Rear
Red: dipoles
Blue: Quads
275 GeV, β∗x = 80 cm, and β∗y=7.2 cm

## Slide 16: Match to Electron Lattice
Forward
Rear
Matched into electron lattice
  150m β at crab cavities
IP
Last dipole: 80mT
IP

## Slide 17: Central Vacuum Chamber
Loss factor kloss = 2.2mV/pC
Bunch length σs = 12mm
Total power loss = 262W
Iavg = 2.48A, N = 660, To = 12.79µs
Loss factor kloss = 0.2mV/pC
Bunch length σs = 24mm
Total power loss = 30W
Iavg = 2.48A, N = 660, To = 12.79µs
Real part of long. Impedance
Small diameter, thin walled Be in center region.
Smooth tapers and transitions to limit energy deposited by beam in trapped modes (wakes).
Considering HOM absorbers
Hadrons

## Slide 18: Synchrotron Radiation
Generated by quads and bending magnet upstream
Tails: can produce hard radiation
  Non-Gaussian
  Conventional collimators in the ESR
Aggressive collimation to a few sigma: extremely poor lifetime
Most radiation has to be passed through detector, absorbed far downstream to minimize backscatter
Photon absorber at -3.5 m from the IP (21/32 mm (h,v))
Preliminary studies of beam tails: 1-2h beam lifetime
  Detector backgrounds look acceptable
Synrad studies: using SYNC_BKG and Synrad3D
  Very good agreement

## Slide 19: Summary
IR developed in collaboration with physics community
  Meets requirements of ‘white paper’
Lattices are stable
  Match into RHIC: recycle existing magnets
Synrad studies: masking scheme
  Reduces rear magnet apertures
IR Magnets
  Magnet and cryostat design mature

## Slide 20
Thank you for your attention

## Slide 21: Back-up Slides

## Slide 22: Synrad3D Studies
FPA allows to reduce
Electron rear magnet apertures (18-20mm radially)
Cooling scheme
Q1BpR/Q2eR
Non-tapered
FPA

## Slide 23
DVCS with proton tagging:
e+d exclusive J/Psi with proton/neutron tagging:
Both Roman Pots and B0-Det. needed to cover the full acceptance for forward protons from DVCS!
IR Simulations with GEANT4 for Various Physics Channels
Three of the four subsystems needed to cover the full acceptance range for e+d!
Generated
Roman Pots
B0 Det.
Detector | Angular Accep. [mrad] | Pt coverage
ZDC @ ~30m | 𝜽 < 5.5 (𝜂 > 6) | pT<1.3 GeV
Roman Pots | 0.0* < 𝜽 < 5.0 (𝜂 > 6) | Low pT (t) (*cutoff driven by beam optics)
Off-Momentum Detectors | 0.0 < 𝜽 < 5.0 (𝜂 > 6) | Low-rigidity particles from nuclear breakup
B0-Forward spectrometer | 5.5 < 𝜽 < 20.0 (4.6 < 𝜂 < 5.9) | High pT (t)

## Slide 24: EIC Detector Infrastructure