## Slide 1: PID in the Yellow Report Status and Beyond
TK Hemmick P Rossi

## Slide 2: Outline
Two basic sections:
  Technologies Summary
  Match of technology to needs.
Information Gleaned from two basic sources:
  PID Presentations: https://indico.bnl.gov/category/277/
  PID Wiki Page(s): https://wiki.bnl.gov/eicug/index.php/Yellow_Report_Detector_PID
Tech
Match

## Slide 3: Status of the PID Section
Draft is ~Complete.
  Some typos are known and will be addressed when unfrozen.
  Some places where the clarity of text should be improved.
  Improve referencing to physics section to minimize duplication.
  Stylistic uniformity pass required.
  Figure captions need to be more elaborated
  Assumptions/details column required in performance summary tables.
  References need throughout.
DRAFT

## Slide 4: Reference Detector and Beyond
Much discussion yesterday:
Solid case for:
  Detailed simulation to learn “Full Limits”
  Future R&D:
    Continued improvements of existing tech.
    Development of new concepts
What Co-Convenors Hear
PID
PID

## Slide 5: Reference Detector PID
PID often requires a multi-detector approach in each aperture.
  Many technologies have a “band” sensitivity:
    dE/dx band crossings greatly assisted by TOF.
    hID Cherenkov is complete only above Kaon threshold (K-proton separation)
Rolf’s Presentation Yesterday
b ~ 0.7

## Slide 6: Forward Direction
Cherenkov is only route to PID at extreme momentum.
Layered indices to combat high threshold in low index material.
Dual-RICH internally does two ranges.
LAPPD is present best TOF (OK in end caps, B-field trouble in barrel).
LAPPD - TOF
Current World’s Best Timing

## Slide 7
Hadron End: Dual RICH
Cherenkov radiator
○ Refractive Index
n = 1.02 (aerogel) 1.0008 (C2F6)
○ Length of the radiator
L = 4 cm (aerogel) , 160 cm (C2F6)
Mirrors
Photon Detector
3 mm pixel size; 200-500 nm MAPMT
Particle Generation
Originate from the vertex
Exquisite detail in simulation.
AI-based optimization.
Uses constant external angular resolution assumption.
Similar external constraint assumed as deduced for separate gas & aerogel RICHes
Tracking maybe tolerates ~2X sim (0.5 – 1.0 mrad)
NOTE: PMTs to the side makes optical aberration (“Emission”) dominant

## Slide 8: Backward Direction
mRICH viable in Forward and Backward.
Aerogel radiator “medium” momentum.
dRICH great performance, but space-challenged.

## Slide 9
Electron Arm: Modular RICH
Cherenkov radiator
(Aerogel) refractive index, n = 1.03
Length of the radiator, L = 3cm
lens with focal length, 𝑓= 6”
Photon Detector
3 mm pixel size
NOTE: Similar performance to aerogel in dRICH
Hadron ID requirements relaxed…aerogel only
Additionally require eID ~ 4GeV/c
Modular RICH focused by Fresnel Lens
  Sharp image improves resolution.
  Transmission of lens combats dispersion
Provides TOF with suitable readout device (LAPPD)
Intrinsic TOF

## Slide 10: eID by Transition Radiation (TRD)
“Threshold detector” (TR X-rays produced or not)
Pmin ~ 1 GeV (rejection ~constant at higher momentum)
1: Make TR photons:
Index, n, change
X-ray regime
Film, foam, fleece
2: Layered to get more photons
3: ID TR photons by energy/pos
4: Reject Pions
Balance between X0 and rejection

## Slide 11: Barrel
Least high momentum requirement.
Most strict space requirement.
All things weighed, the barrel is a real challenge to eID and PID.

## Slide 12
Leading Barrel PID Technology: DIRC
12
:
Generic reference design: 1m barrel radius, 16 sectors
176 bars: synthetic fused silica,17mm (T) ´ 32mm (W) ´ 4200mm (L)
Photo sensors: MCP-PMTs -3x3mm2 pixels
DIRC in sPHENIX
hpDIRC ala eRD14
At normal incidence, Cerenkov light is internally reflected for
Cerenkov angle preserved if bars meticulously flat with 90 degree corners.
Spectacularly compact PID device with photon detection at end.

## Slide 13: hpDIRC Performance Simulations
Original BaBar DIRC was effectively “proximity focused”
hpDIRC section creates focused ring improving resolution.
Excellent match to EIC needs.
Strict requirements on “correlated terms”, (e.g. angular resolution of tracking)
Works with either standard tracking solution.

## Slide 14: Speculative Cluster Counting Concept
Scaling to our available length:
Using a 3s reference @ 40 cm gas:
Existing Concept (“Timepix”)
  Avalanche onto Silicon Pixels
  Tiny Pixels (smaller than cluster spacing)
  Sufficient gain for single electron
In principle can work
Expensive for large area.
Can we accomplish with conventional tech?

## Slide 15: Long Shadow Detector -- LSD
Drift leverages huge Lorentz angle as “magnifier”
Clusters spread across space and time.
Higher B = Lower Transverse diffusion
  Example: T2K(130 V/cm) has only
Detect (count) clusters with conventional means.
B-field
track
HV-
New Concept: Like a “Streak Camera”
Sensors
Bad for Tracking
Good for PID
Silicon Tracker
Multiple sections…
Early Conceptual Stage: LSD merely a hallucination?

## Slide 16: Photon Detection Technologies
Photon Detection Technology critical for many PID devices.
  Cherenkov detection requires single photon-electron!
    High gain.
    Can tolerate/compensate moderate gain loss
    Little room for Efficiency Loss
  Many Technologies are B-field sensitive!
Can SiPM be operated longterm in a RICH?
  Radiation damage prevention/mitigation (dark current makes HITS, not a simple pedestal shift)
New gas-tolerant B-tolerate photocathodes

## Slide 17: Summary and Outlook
Draft of PID Yellow Report PID section is basically complete.
Contains the “usual” hit-list of needs to advance from draft to final.
Reference detector design well addressed by existing known technologies.
A few notes of tension between physics and reference design:
  eID in barrel
  PID reach in barrel.
Future work should address “global” PID within reference detector.
  Need to understand the exact limits and smooth roll-off.
Future work should include R&D to develop/extend known technologies.
Future work should investigate speculative options (only some of which shown here)