## Slide 1: Discussion on YR Content: Magnetic Field Strength, Magnet Bore
R. Rajput-Ghoshal (JLAB)
E.C. Aschenauer (BNL)
R. Ent (JLAB)
EIC-UG 4th YR Meeting
Electron Ion Collider

## Slide 2: Detector Solenoid Magnetic Field Requirements
ERD-18 Discs (1.5T)
ERD-18 Discs (3T)
Leading order 1/B dependence clearly can be seen (regardless of pixel size  3 T field clearly helps!

## Slide 3: Detector Solenoid Magnetic Field Requirements
Even with TPC hybrid baseline, 3T field and ITS3 10x10 pixel size do not always make what we would like to have (at forward pseudo-rapidity)… but 1.5 T for sure can’t reach it.
Studies by Hakan Wennlof et al.

## Slide 4: Detector Solenoid Magnetic Field Musings
The main advantage of accessibility of low central solenoid fields (down to ~0.5 T) is towards the low-PT acceptance of charged-particle tracks.
A central field of 0.5 T roughly equates to a detection capability of charged particles down to transverse momenta of below ~0.1 GeV/c.
  For example relevant for mapping the decay products of heavy-flavor mesons.
The main advantage of a 3 T versus a 1.5 T central solenoid field is for the momentum resolution of charged particles as function of pseudo-rapidity.
Doubling the magnetic field can lead to a reduction of the momentum resolution by a factor of ~2 from a leading order 1/B dependence.
This is relevant in the central region, but even more so in the forward pseudo-rapidity regions, h > 2, where the momentum resolutions rapidly worsen.
  For example, for h ~ 3, a momentum resolution of ~2-3% is achievable for pions with momenta up to about 30 GeV/c with a 3 T central field, and only double that resolution for a 1.5 T central field.
aka YR Content

## Slide 5: Detector Solenoid Bore and Barrel Detector Space Needs
Function | Minimum [cm] | Maximum [cm] | Minimum [cm] | Maximum [cm]
Tracking (includes 5 cm support) | All-Si |  | Si + TPC | 
 | 65 |  | 85 | 
Hadron particle identification | RICH |  | DIRC | 
 | 50 |  | 10 | 
EM Calorimetry | 30 | 50 | High-Resolution to achieve P < 2 GeV | 
 |  |  | 50 | 
PID & EMCal support structure | 10 | 15 | 10 | 15
Total | 145 | 165 | 155 | 160
Tracking all-Si maybe down to 50-60 cm, Si + TPC = 80 cm
Tracking support structure 5 cm
Hadron particle identification DIRC only needs 10 cm, RICH 50 cm but better for uniformity
EM Calorimetry 50 cm for high-resolution, 30 cm for less-resolution (or costly)
PID & EMCal support structure 10-15 cm likely enough
Conclusion: to fit all detectors in the existing magnet with bore 2.8 meter will be a tour de force and it is possible some functionality has to give. For a new magnet, a bore of 3.2 meter is a safer option. Only in one of these four cases, we needed 5 cm more.

## Slide 6: Detector solenoid - Coil length and Cryostat length
Component | Axial length (cm)
Coil end support | 2
Gap for Helium | 2
Inner Helium vessel end | 1
MLI | 1.5
Thermal shield end | 1
MLI | 2
Vacuum vessel end | 2.5
}
12 cm
Need +/- 12 cm outside coil length for cryostat length
Illustration for:
3 m magnet bore
3 m coil length
 4.2 m outside diameter (+1.2), and 3.24 m (+0.24) cryostat length

## Slide 7: Detector Solenoid Bore and Coil Length Musings
Reference detector: barrel region is “defined” as between pseudo-rapidity of -1 and 1.  This means that for a certain bore x, the coil space can be ~1.2*x.
A new detector solenoid with a bore of 3.2 meter seems a safe assumption
  sufficient flexibility for detector choices to satisfy EIC science requirements of good tracking and particle identification, and hermetic electromagnetic calorimetry.
  assumes any hadronic calorimetry will be located outside the magnet coil.
  gives a cryostat length of 3.84 meter, and a coil length of 3.6 meter, folding in the 12 cm additional need each side of the magnet coil. These numbers can be a little loose, and as required a coil length of 3.8 meter would not be a major issue.
The coil/cryostat length is a delicate balance:
  The cryostat length defines the separation between the central barrel region and the forward and/or backward end cap regions.
  Space in the barrel region for detector is much more limited than in forward and backward regions, which poses limits on reaching the EIC detector requirements.
  The edge of the cryostat is likely one of the regions where detector infrastructure (support, cabling, etc.) will reside, and detectors such as a Ring-Imaging Cherenkov will “flare out”, or tradeoffs between hermeticity of an electromagnetic calorimeter and a DIRC will occur.

## Slide 8: Detector Solenoid Bore and Coil Length
This leads us to the following magnet requirements:
Magnet field up to 3 T, should be able to operate down to 0.5 T.
Magnet field minimum >2.5 T (a guess, this should come from the YR effort)*
Magnet bore 3.2 meter
Cryostat length 3.84 meter (can be loosened slightly)
Cryostat outer diameter 4.4 meter
Cryostat outer diameter (max) 4.8 meter (+1 m of HCal leaves 0.467 m to door height)
* somewhere this question likely needs to be quantitatively answered, what is the science loss for up to 3T versus up to 2.5 T versus up to ? T

## Slide 9: Summary of some of the main requirements of the EIC detector Solenoid Magnet
Note: this is a subset of a larger list of magnet specifications, which Renuka Rajput-Ghoshal compiled to pass on to Lionel Quettier et al from CEA, Saclay.
CEA, Saclay confirmed interest and availability to do engineering and design for the SC solenoid magnet, both for the new solenoid (up to CD-2 at least), and to provide expertise for evaluation of the ex-BABAR/sPHENIX magnet. THANKS!